## Slide 1: CSCI 466: Networks
FTP, Peer 2 Peer Networks (P2P), Content Distribution Networks (CDN)
Reese Pearsall
Fall 2024
https://www.cs.montana.edu/pearsall/classes/fall2024/466/main.html
*All images are stolen from the internet

## Slide 2
Announcements
Wireshark Lab 1 due tonight at 11:59 PM
Everyone needs to submit something to D2L, even if you work with partners
i hope you have a good weekend

## Slide 3
FTP
File Transfer Protocol (FTP)- protocol used for transferring files from server to client
FTP
client
FTP
server
TCP control connection,
server port 21
TCP data connection,
server port 20
FTP communicates over two connections
  Port 21 for control information
  Port 20 for data
Differences from HTTP
  Control communication “out-of-band”
  Server maintains per client state: authentication, current directory
FTP procedure:
  FTP client contacts FTP server at port 21, using TCP
  Client authorized over control connection
  Client browses remote directory, sends commands over control connection
  When server receives file transfer command, server opens 2nd TCP data connection (for file) to client
  After transferring one file, server closes data connection
Why use a separate control connection?

## Slide 4
WinSCP

## Slide 5
P2P Networks
No always-on server
Arbitrary end systems directly communicate
Peers are intermittently connected and change IP addresses
Client-Server Architecture
Time to distribute a file of size F to N clients
Time to distribute a file of size F to N clients

## Slide 6
P2P Networks
Client-Server Architecture
Existing clients have to share resources with new users
New peers are both a client and a server. There will not be a negative impact on current peers
P2P architectures are self-scaling
New peers bring increasing capacity!

## Slide 7
P2P Networks
Client server distribution time grows with the number of clients
P2P distribution time approaches 1 hour as number of clients grows

## Slide 8
Service for sharing files over the internet in a decentralized fashion
(BitTorrent, uTorrent, qBittorrent are all popular torrent clients)
P2P file distribution: BitTorrent

## Slide 9
User 1

## Slide 10
User 1
A Tracker is made, typically located at the person who created the torrent
Tracker
Chunk1: 10.1.2.3
Chunk2: 10.1.2.3
Chunk3: 10.1.2.3
Chunk4: 10.1.2.3
…
ChunkN: 10.1.2.3
10.1.2.3

## Slide 11
User 1
A Tracker is made, typically located at the person who created the torrent
Tracker
Chunk1: 10.1.2.3
Chunk2: 10.1.2.3
Chunk3: 10.1.2.3
Chunk4: 10.1.2.3
…
ChunkN: 10.1.2.3
10.1.2.3
User 2
10.1.2.4
User 2 wants the file, so they download a TorrentFile which allows them to contact the Tracker and join the P2P

## Slide 12
User 1
A Tracker is made, typically located at the person who created the torrent
Tracker
Chunk1: 10.1.2.3
Chunk2: 10.1.2.4
Chunk3: 10.1.2.4
Chunk4: 10.1.2.3
…
ChunkN: 10.1.2.3
10.1.2.3
User 2
10.1.2.4

## Slide 13
User 1
A Tracker is made, typically located at the person who created the torrent
Tracker
Chunk1: 10.1.2.3
Chunk2: 10.1.2.4
Chunk3: 10.1.2.4
Chunk4: 10.1.2.3
…
ChunkN: 10.1.2.3
10.1.2.3
User 2
10.1.2.4
User 3
10.1.2.5

## Slide 14
User 1
A Tracker is made, typically located at the person who created the torrent
Tracker
Chunk1: 10.1.2.5
Chunk2: 10.1.2.4
Chunk3: 10.1.2.4
Chunk4: 10.1.2.3
…
ChunkN: 10.1.2.3
10.1.2.3
User 2
10.1.2.4
User 3
10.1.2.5
User 3
10.1.2.6

## Slide 15
User 1
A Tracker is made, typically located at the person who created the torrent
Tracker
Chunk1: 10.1.2.5
Chunk2: 10.1.2.4
Chunk3: 10.1.2.4
Chunk4: 10.1.2.3
…
ChunkN: 10.1.2.3
10.1.2.3
User 2
10.1.2.4
User 3
10.1.2.5
User 3
10.1.2.6
As more users join the network, it grows the capability of the networks and chunks are more scattered

## Slide 16
P2P file distribution: BitTorrent
tracker: tracks peers
participating in torrent
Alice arrives …
… obtains list
of peers from tracker
… and begins exchanging
file chunks with peers in torrent
torrent: group of peers exchanging chunks of a file
Files are divided into chunks
Peers in torrent send/receive file chunks

## Slide 17
P2P file distribution: BitTorrent
tracker: tracks peers
participating in torrent
Alice arrives …
… obtains list
of peers from tracker
… and begins exchanging
file chunks with peers in torrent
torrent: group of peers exchanging chunks of a file
Files are divided into chunks
Peers in torrent send/receive file chunks
peer joining torrent:
  has no chunks, but will accumulate them over time from other peers
  registers with tracker to get list of peers, connects to subset of peers (“neighbors”)

## Slide 18
P2P file distribution: BitTorrent
tracker: tracks peers
participating in torrent
Alice arrives …
… obtains list
of peers from tracker
… and begins exchanging
file chunks with peers in torrent
torrent: group of peers exchanging chunks of a file
Files are divided into chunks
Peers in torrent send/receive file chunks
while downloading, peer uploads chunks to other peers
peer may change peers with whom it exchanges chunks
churn: peers may come and go
once peer has entire file, it may (selfishly) leave or (altruistically) remain in torrent

## Slide 19
P2P file distribution: BitTorrent
Collaborative download

## Slide 20
P2P file distribution: BitTorrent
Collaborative download
Which chunks to download?
Rarest first
Try to equalize the number of copies of each chunk in the system

## Slide 21
P2P file distribution: BitTorrent
Collaborative download
From which peers to download?
Allow download to N peers with highest upload rates
Allows peers with similar upload rates to find each other

## Slide 22
P2P file distribution: BitTorrent
requesting chunks:
at any given time, different peers have different subsets of file chunks
periodically, Alice asks each peer for list of chunks that they have
Alice requests missing chunks from peers, rarest first

## Slide 23
P2P file distribution: BitTorrent
sending chunks: tit-for-tat
Alice sends chunks to those four peers currently sending her chunks at highest rate
  other peers are choked by Alice (do not receive chunks from her)
  re-evaluate top 4 every10 secs
every 30 secs: randomly select another peer, starts sending chunks
  “optimistically unchoke” this peer
  newly chosen peer may join top 4
higher upload rate: find better trading partners, get file faster !
BitTorrent is referred to as an unstructured P2P
Security Concerns?
IP Address
Malware

## Slide 24
CDNs
  Netflix, YouTube: 37%, 16% of downstream residential ISP traffic
  ~1B YouTube users, ~75M Netflix users
challenge: scale - how to reach ~1B users?
  single mega-video server won’t work (why?)
challenge: heterogeneity
  different users have different capabilities (e.g., wired versus mobile; bandwidth rich versus bandwidth poor)
solution: distributed, application-level infrastructure
video traffic: major consumer of Internet bandwidth

## Slide 25
CDNs
Conditional GET
  Cache: specify date of cached copy in HTTP request If-modified-since: <date>
  Server: response contains no object if cached copy is up-to-date: HTTP/1.0 304 Not Modified
Client
Server
GET index.htm
OK
GET
Cache
Caching
  Save previously delivered data
  Subsequent requests served from cache on the browser, or in the access network
Applications
  Reduce response time for client request
  Reduce ISP traffic costs
Content distribution networks
  Distributed caches
  Web objects addressed to CDN server
  CDN server fetches from content provider on first access

## Slide 26
CDNs
Challenge:
  How to stream content to millions of users?
Option 1:
  Single mega-datacenter
  Pros: Simple
  Cons:
    Single point of failure
    Point of network congestion
    Long path to distant clients
    Multiple copies of video sent over outgoing link

## Slide 27
CDNs
Option 2:
  Store/serve multiple copies of videos at multiple geographically distributed sites
Origin server
LDNS
34 DNS lookups
204 HTTP requests
520 KB of data downloaded
56% of domains resolve to a CDN
A content delivery network (CDN) refers to a geographically distributed group of cache servers which work together to provide fast delivery of Internet content.
(not a web host)

## Slide 28
CDNs
https://cdn.discordapp.com/attachments/1017630358621143110/1017849417216294972/unknown.png

## Slide 29
CDNs
Challenge: how does CDN DNS select “good” CDN node to stream to client
  Pick CDN node geographically closest to client’s local DNS
  Pick CDN node with shortest delay (or min # hops) to client (CDN nodes periodically ping access ISPs, reporting results to CDN DNS)
?
?
?
?

## Slide 30
CDNs
In HTTP steaming, video is stored at an HTTP server and retrieved with a GET request
Frames are sent to a client buffered and played back after a certain threshold
All clients receiving the same encoding of the video despite widely different bandwidth

## Slide 31
CDNs
In HTTP steaming, video is stored at an HTTP server and retrieved with a GET request
Frames are sent to a client buffered and played back after a certain threshold
All clients receiving the same encoding of the video despite widely different bandwidth
Dynamic Adaptive Streaming over HTTP (DASH)- video is encoded into several different versions
Different encoding rate, different quality, etc
Clients dynamically request chunks of video segments every few seconds via GET requests
Is the current bandwidth good?  Retrieve good quality
Is the current bandwidth bad?  Retrieve ok quality

## Slide 32
CDNs
When streaming, you are consistently issuing GET requests

## Slide 33
CDNs
Studio maser versions are uploaded to a private Amazon cloud

## Slide 34
CDNs
Studio maser versions are uploaded to a private Amazon cloud
Videos are processed into many different formats, allowing for DASH

## Slide 35
CDNs
Studio maser versions are uploaded to a private Amazon cloud
Videos are processed into many different formats, allowing for DASH
Versions are uploaded to Netflix’s CDNs