## Slide 1: CSCI 466: Networks
Pipelining
Reese Pearsall
Fall 2024
https://www.cs.montana.edu/pearsall/classes/fall2024/466/main.html
*All images are stolen from the internet

## Slide 2
Announcements
PA 2 Posted. Due Sunday, October 13th

## Slide 3
Application Layer
Presentation Layer
Session Layer
Transport Layer
Network Layer
Data Link Layer
Physical Layer
OSI Model
Messages from Network Applications
Application Layer
Physical Layer
Bits being transmitted over some medium
*In the textbook, they condense it to a 5-layer model, but 7 layers is what is most used
*
*

## Slide 4
So far, our reliable data transfer protocols have been stop-and-wait

## Slide 5
So far, our reliable data transfer protocols have been stop-and-wait
Waiting to receive an ACK is inefficient
We spend a lot of time waiting

## Slide 6
Pipelining: sender allows multiple, “in-flight”, yet-to-be acknowledged packets

## Slide 7
Pipelining: sender allows multiple, “in-flight”, yet-to-be acknowledged packets
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
1
2
3
4
5
6
7
8
Consequences:
Need to use a wider range of sequence numbers

## Slide 8
Pipelining: sender allows multiple, “in-flight”, yet-to-be acknowledged packets
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
1
2
3
4
5
6
7
8
Consequences:
Need to use a wider range of sequence numbers
Sender and receiver may need to buffer more than one packet

## Slide 9: Go-Back-N: sender
sender: “window” of up to N, consecutive transmitted but unACKed pkts
  k-bit seq # in pkt header
cumulative ACK: ACK(n): ACKs all packets up to, including seq # n
  on receiving ACK(n): move window forward to begin at n+1
timer for oldest in-flight packet
timeout(n): retransmit packet n and all higher seq # packets in window

## Slide 10: Go-Back-N: sender
sender: “window” of up to N, consecutive transmitted but unACKed pkts
  k-bit seq # in pkt header
cumulative ACK: ACK(n): ACKs all packets up to, including seq # n
  on receiving ACK(n): move window forward to begin at n+1
timer for oldest in-flight packet
timeout(n): retransmit packet n and all higher seq # packets in window
(Why not have an infinite window size?)

## Slide 11: Go-Back-N: receiver
ACK-only: always send ACK for correctly-received packet so far, with highest in-order seq #
  may generate duplicate ACKs
  need only remember rcv_base
on receipt of out-of-order packet:
  can discard (don’t buffer) or buffer: an implementation decision
  re-ACK pkt with highest in-order seq #
rcv_base
received and ACKed
Out-of-order: received but not ACKed
Not received
Receiver view of sequence number space:
…
…

## Slide 12
send pkt0
send pkt1
send pkt2
send pkt3
(wait)
sender
receiver
receive pkt0, send ack0
receive pkt1, send ack1
receive pkt3, discard,
(re)send ack1
send pkt2
send pkt3
send pkt4
send pkt5
X
loss
pkt 2 timeout
receive pkt4, discard,
(re)send ack1
receive pkt5, discard,
(re)send ack1
rcv pkt2, deliver, send ack2
rcv pkt3, deliver, send ack3
rcv pkt4, deliver, send ack4
rcv pkt5, deliver, send ack5
ignore duplicate ACK
sender window (N=4)
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
rcv ack0, send pkt4
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
rcv ack1, send pkt5

## Slide 13
https://www2.tkn.tu-berlin.de/teaching/rn/animations/gbn_sr/

## Slide 14: Selective repeat: the approach
pipelining: multiple packets in flight
receiver individually ACKs all correctly received packets
  buffers packets, as needed, for in-order delivery to upper layer
sender:
  maintains (conceptually) a timer for each unACKed pkt
    timeout: retransmits single unACKed packet associated with timeout
  maintains (conceptually) “window” over N consecutive seq #s
    limits pipelined, “in flight” packets to be within this window

## Slide 15
https://www2.tkn.tu-berlin.de/teaching/rn/animations/gbn_sr/

## Slide 16: Selective repeat: sender and receiver
data from above:
if next available seq # in window, send packet
timeout(n):
resend packet n, restart timer
ACK(n) in [sendbase,sendbase+N-1]:
mark packet n as received
if n smallest unACKed packet, advance window base to next unACKed seq #
sender
packet n in [rcvbase, rcvbase+N-1]
send ACK(n)
out-of-order: buffer
in-order: deliver (also deliver buffered, in-order packets), advance window to next not-yet-received packet
packet n in [rcvbase-N,rcvbase-1]
ACK(n)
otherwise:
ignore
receiver

## Slide 17: Selective Repeat in action
send pkt0
send pkt1
send pkt2
send pkt3
(wait)
sender
receiver
send pkt2
(but not 3,4,5)
X
loss
pkt 2 timeout
sender window (N=4)
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
rcv ack0, send pkt4
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
rcv ack1, send pkt5
receive pkt0, send ack0
receive pkt1, send ack1
receive pkt3, buffer,
send ack3
record ack3 arrived
receive pkt4, buffer,
send ack4
receive pkt5, buffer,
send ack5
rcv pkt2; deliver pkt2,
pkt3, pkt4, pkt5; send ack2
Q: what happens when ack2 arrives?

## Slide 18: Selective repeat: a dilemma!
0 1 2 3 0 1 2
0 1 2 3 0 1 2
0 1 2 3 0 1 2
pkt0
pkt1
pkt2
0 1 2 3 0 1 2
pkt0
timeout
retransmit pkt0
0 1 2 3 0 1 2
0 1 2 3 0 1 2
0 1 2 3 0 1 2
X
X
X
will accept packet
with seq number 0
(b) oops!
receiver window
(after receipt)
sender window
(after receipt)
0 1 2 3 0 1 2
0 1 2 3 0 1 2
0 1 2 3 0 1 2
pkt0
pkt1
pkt2
0 1 2 3 0 1 2
pkt0
0 1 2 3 0 1 2
0 1 2 3 0 1 2
0 1 2 3 0 1 2
X
will accept packet
with seq number 0
0 1 2 3 0 1 2
pkt3
(a) no problem
example:
seq #s: 0, 1, 2, 3 (base 4 counting)
window size=3

## Slide 19: Selective repeat: a dilemma!
Q: what relationship is needed between sequence # size and window size to avoid problem in scenario (b)?
0 1 2 3 0 1 2
0 1 2 3 0 1 2
0 1 2 3 0 1 2
pkt0
pkt1
pkt2
0 1 2 3 0 1 2
pkt0
timeout
retransmit pkt0
0 1 2 3 0 1 2
0 1 2 3 0 1 2
0 1 2 3 0 1 2
X
X
X
will accept packet
with seq number 0
receiver window
(after receipt)
sender window
(after receipt)
0 1 2 3 0 1 2
0 1 2 3 0 1 2
0 1 2 3 0 1 2
pkt0
pkt1
pkt2
0 1 2 3 0 1 2
pkt0
0 1 2 3 0 1 2
0 1 2 3 0 1 2
0 1 2 3 0 1 2
X
will accept packet
with seq number 0
0 1 2 3 0 1 2
pkt3
(a) no problem
example:
seq #s: 0, 1, 2, 3 (base 4 counting)
window size=3
receiver can’t see sender side
receiver behavior identical in both cases!
something’s (very) wrong!

## Slide 20
Checksum- Used to detect bit errors in transmitted packets
RDT Principles
Transport Layer

## Slide 21
Checksum- Used to detect bit errors in transmitted packets
Timer- Used to timeout/retransmit a packet, possibly because the packet (or its ACK) was lost within a channel
RDT Principles
Transport Layer

## Slide 22
Checksum- Used to detect bit errors in transmitted packets
Timer- Used to timeout/retransmit a packet, possibly because the packet (or its ACK) was lost within a channel
Sequence Number- Used for sequential numbering of packets of data flowing form sender to receiver. Gaps in sequence number of packets allow the receiver to detect a lost or duplicate packet
RDT Principles
Transport Layer

## Slide 23
Checksum- Used to detect bit errors in transmitted packets
Timer- Used to timeout/retransmit a packet, possibly because the packet (or its ACK) was lost within a channel
Sequence Number- Used for sequential numbering of packets of data flowing form sender to receiver. Gaps in sequence number of packets allow the receiver to detect a lost or duplicate packet
Acknowledgement- Used by the receiver to tell the sender that a packet or set of packets has been received correctly. ACKs will typically carry the sequence # of the packet being acknowledged
RDT Principles
Transport Layer

## Slide 24
Checksum- Used to detect bit errors in transmitted packets
Timer- Used to timeout/retransmit a packet, possibly because the packet (or its ACK) was lost within a channel
Sequence Number- Used for sequential numbering of packets of data flowing form sender to receiver. Gaps in sequence number of packets allow the receiver to detect a lost or duplicate packet
Acknowledgement- Used by the receiver to tell the sender that a packet or set of packets has been received correctly. ACKs will typically carry the sequence # of the packet being acknowledged
Negative Acknowledgement- Used by the receiver to tell the sender that a packet has not been received correctly. Negative acknowledgements will typically carry the sequence number of the packet that was not received correctly
RDT Principles
Transport Layer

## Slide 25
Checksum- Used to detect bit errors in transmitted packets
Timer- Used to timeout/retransmit a packet, possibly because the packet (or its ACK) was lost within a channel
Sequence Number- Used for sequential numbering of packets of data flowing form sender to receiver. Gaps in sequence number of packets allow the receiver to detect a lost or duplicate packet
Acknowledgement- Used by the receiver to tell the sender that a packet or set of packets has been received correctly. ACKs will typically carry the sequence # of the packet being acknowledged
Negative Acknowledgement- Used by the receiver to tell the sender that a packet has not been received correctly. Negative acknowledgements will typically carry the sequence number of the packet that was not received correctly
Window, pipelining- The sender may be restricted to sending only packets with sequence numbers that fall within a given range. By allowing multiple packets to be transmitted but not yet acknowledged, sender utilization can be increased over a stop-and-wait mode of operation
RDT Principles
Transport Layer