## Slide 1: CSCI 466: Networks Network Layer – Routing (Control Plane)
Reese Pearsall Fall 2022
https://www.cs.montana.edu/pearsall/classes/fall2022/466/main.html
1
*All images are stolen from the internet

## Slide 2: Announcements
NO CLASS on Monday (10/24)
Email/DM me if you need to chat or have questions
HW2 Released. Due one week from today (10/28)
PA2 due tonight* at 11:59 PM
 You can submit it any time this weekend without a late pass and you won’t lose points 

## Slide 3
Forwarding refers to moving packets from a router’s input to appropriate router output, and is implemented in the data plane.
Routing refers to determining the route taken by packets from source to destination, and is implemented in the control plane.
Ideally, this output links are the most optimal path to get to the destination
What is the best way to get from u to z?

## Slide 4: Generalized Forwarding and Software Defines Network (SDN)
Control Plane and Data Plane need to work together in order to create efficient routing tables

## Slide 5: Network as a Graph
An example network with 6 hosts/routers
A graph G consists of N nodes
N = { u v x w y z }
A node could be a host, a router, or a smaller network!
A graph consists of edges E
E1
(u,v) = 2
E2
(u,w) = 5
E6
(x,y) = 1
In most cases, edges will also have a cost
What do the costs represent??

## Slide 6: Network as a Graph
An example network with 6 hosts/routers
A graph G consists of N nodes
N = { u v x w y z }
A node could be a host, a router, or a smaller network!
A graph consists of edges E
E1
(u,v) = 2
E2
(u,w) = 5
E6
(x,y) = 1
In most cases, edges will also have a cost
What do the costs represent?? Physical distance, time needed, bandwidth, delay

## Slide 7: Network as a Graph
The cost from A to B is the sum of the edge weights of the path taken
C(u,z) = 1 + 1 + 2 = 4
C(u,z) = 2 + 3 + 5 = 10
If a packet needs to go from U to Z, we want it to take the most optimal path!
Routing algorithm: algorithm that finds the least cost path
Do you know any?
👀

## Slide 8: Link-state Algorithm (Dijkstra’s algorithm)
Dijkstra’s algorithm is a shortest path algorithm that is guaranteed to find a solution
step | N’ | D(v), p(v) | D(w), p(w) | D(x), p(x) | D(y), p(y) | D(z), p(z)
0 | u | 2, u | 5, u | 1, u | N/A | N/A
1 |  |  |  |  |  | 
2 |  |  |  |  |  | 
3 |  |  |  |  |  | 
4 |  |  |  |  |  | 
5 |  |  |  |  |  | 
Goal: Find shortest path from u to z
N’ is our current optimal path. We must start at u obviously

## Slide 9: Link-state Algorithm (Dijkstra’s algorithm)
Dijkstra’s algorithm is a shortest path algorithm that is guaranteed to find a solution
step | N’ | D(v), p(v) | D(w), p(w) | D(x), p(x) | D(y), p(y) | D(z), p(z)
0 | u | 2, u | 5, u | 1, u | N/A | N/A
1 |  |  |  |  |  | 
2 |  |  |  |  |  | 
3 |  |  |  |  |  | 
4 |  |  |  |  |  | 
5 |  |  |  |  |  | 
Goal: Find shortest path from u to z
N’ is our current optimal path. We must start at u obviously

## Slide 10: Link-state Algorithm (Dijkstra’s algorithm)
Dijkstra’s algorithm is a shortest path algorithm that is guaranteed to find a solution
step | N’ | D(v), p(v) | D(w), p(w) | D(x), p(x) | D(y), p(y) | D(z), p(z)
0 | u | 2, u | 5, u | 1, u | N/A | N/A
1 |  |  |  |  |  | 
2 |  |  |  |  |  | 
3 |  |  |  |  |  | 
4 |  |  |  |  |  | 
5 |  |  |  |  |  | 
Goal: Find shortest path from u to z
The path with the least cost is to X, so x will get added onto our path!

## Slide 11: Link-state Algorithm (Dijkstra’s algorithm)
Dijkstra’s algorithm is a shortest path algorithm that is guaranteed to find a solution
step | N’ | D(v), p(v) | D(w), p(w) | D(x), p(x) | D(y), p(y) | D(z), p(z)
0 | u | 2, u | 5, u | 1, u | N/A | N/A
1 | ux |  |  |  |  | 
2 |  |  |  |  |  | 
3 |  |  |  |  |  | 
4 |  |  |  |  |  | 
5 |  |  |  |  |  | 
Goal: Find shortest path from u to z

## Slide 12: Link-state Algorithm (Dijkstra’s algorithm)
Dijkstra’s algorithm is a shortest path algorithm that is guaranteed to find a solution
step | N’ | D(v), p(v) | D(w), p(w) | D(x), p(x) | D(y), p(y) | D(z), p(z)
0 | u | 2, u | 5, u | 1, u | N/A | N/A
1 | ux | 2, u | 4, x |  | 2, x | N/A
2 |  |  |  |  |  | 
3 |  |  |  |  |  | 
4 |  |  |  |  |  | 
5 |  |  |  |  |  | 
Goal: Find shortest path from u to z
The shortest path from u to v is still the same
The shortest path from u to w is now 4 (travel through x) instead of taking the 4 cost path

## Slide 13: Link-state Algorithm (Dijkstra’s algorithm)
Dijkstra’s algorithm is a shortest path algorithm that is guaranteed to find a solution
step | N’ | D(v), p(v) | D(w), p(w) | D(x), p(x) | D(y), p(y) | D(z), p(z)
0 | u | 2, u | 5, u | 1, u | N/A | N/A
1 | ux | 2, u | 4, x |  | 2, x | N/A
2 | uxy | 2, u | 3, y |  |  | 4,y
3 |  |  |  |  |  | 
4 |  |  |  |  |  | 
5 |  |  |  |  |  | 
Goal: Find shortest path from u to z
Now that y is on our path, we can now reach z!
We also have a more optimal path to W now
Path(u,z) = uxyz
Cost = 1 +1 + 2 = 4

## Slide 14: Link-state Algorithm (Dijkstra’s algorithm)
Dijkstra’s algorithm is a shortest path algorithm that is guaranteed to find a solution
step | N’ | D(v), p(v) | D(w), p(w) | D(x), p(x) | D(y), p(y) | D(z), p(z)
0 | u | 2, u | 5, u | 1, u | N/A | N/A
1 | ux | 2, u | 4, x |  | 2, x | N/A
2 | uxy | 2, u | 3, y |  |  | 4,y
3 | uxyv |  | 3,y |  |  | 4,y
4 |  |  |  |  |  | 
5 |  |  |  |  |  | 
NEW Goal: Find shortest path from u to any node

## Slide 15: Link-state Algorithm (Dijkstra’s algorithm)
Dijkstra’s algorithm is a shortest path algorithm that is guaranteed to find a solution
step | N’ | D(v), p(v) | D(w), p(w) | D(x), p(x) | D(y), p(y) | D(z), p(z)
0 | u | 2, u | 5, u | 1, u | N/A | N/A
1 | ux | 2, u | 4, x |  | 2, x | N/A
2 | uxy | 2, u | 3, y |  |  | 4,y
3 | uxyv |  | 3,y |  |  | 4,y
4 | uxyvw |  |  |  |  | 4,y
5 | uxyvwz |  |  |  |  | 
NEW Goal: Find shortest path from u to any node

## Slide 16: Link-state Algorithm (Dijkstra’s algorithm)
Routing table for node u
We will then run the same algorithm on each node to create its forwarding table!
LS complexity = O(N^2)
Issues? Concerns?

## Slide 17: Link-state Algorithm (Dijkstra’s algorithm)
LS is a centralized routing algorithm, which means it has global knowledge about all the edge of the network!
?
?
?
?
?
?
?
However, it is very likely we will not know information about the network beforehand!
Additionally, path costs can frequently change based on network congestion

## Slide 18: Distance Vector Algorithm
Dx(y) = estimate of least cost from x to y
  x maintains distance vector Dx = [Dx(y): y є N ]
node x:
  knows cost to each neighbor v: c(x,v)
  maintains its neighbors’ distance vectors. For each neighbor v, x maintains Dv = [Dv(y): y є N ]
DV is not a centralized algorithm, which means that it does not require global knowledge about network edge costs
key idea:
from time-to-time, each node sends its own distance vector estimate to neighbors
when x receives new DV estimate from neighbor, it updates its own DV using B-F equation:
Dx(y) ← minv{c(x,v) + Dv(y)} for each node y ∊ N

## Slide 19: Distance vector algorithm
iterative, asynchronous: each local iteration caused by:
local link cost change
DV update message from neighbor
distributed:
each node notifies neighbors only when its DV changes
  neighbors then notify their neighbors if necessary
wait for (change in local link cost or msg from neighbor)
recompute estimates
if DV to any dest has changed, notify neighbors
each node:

## Slide 20: Comparison of LS and DV algorithms
message complexity
LS: with n nodes, E links, O(nE) msgs sent
DV: exchange between neighbors only
  convergence time varies
speed of convergence
LS: O(n2) algorithm requires O(nE) msgs
  may have oscillations
DV: convergence time varies
  may be routing loops
  count-to-infinity problem
robustness: what happens if router malfunctions?
LS:
  node can advertise incorrect link cost
  each node computes only its own table
DV:
  DV node can advertise incorrect path cost
  each node’s table used by others
    error propagate thru network

## Slide 21
Intra-AS Routing: OSPF
An autonomous system is a group of routers that are under the same administrative control
AS 1
AS 2
AS 3

## Slide 22
Intra-AS Routing: OSPF
An autonomous system is a group of routers that are under the same administrative control
AS 1
OSPF is a link-state protocol that uses flooding of link-state information and Dijkstra’s least-cost algorithm
Open Shortest Path First

## Slide 23
Intra-AS Routing: OSPF
An autonomous system is a group of routers that are under the same administrative control
AS 1
OSPF is a link-state protocol that uses flooding of link-state information and Dijkstra’s least-cost algorithm
Open Shortest Path First
1. Each router constructors a topological map of the AS

## Slide 24
Intra-AS Routing: OSPF
An autonomous system is a group of routers that are under the same administrative control
AS 1
OSPF is a link-state protocol that uses flooding of link-state information and Dijkstra’s least-cost algorithm
Open Shortest Path First
1. Each router constructors a topological map of the AS
2. Run Dijikstra’s to determine shortest path to each subnet
(Edge costs will be set by a network administrator)
(could set all edges to be a cost of 1)

## Slide 25
Intra-AS Routing: OSPF
An autonomous system is a group of routers that are under the same administrative control
AS 1
OSPF is a link-state protocol that uses flooding of link-state information and Dijkstra’s least-cost algorithm
Open Shortest Path First
1. Each router constructors a topological map of the AS
2. Run Dijikstra’s to determine shortest path to each subnet
(Edge costs will be set by a network administrator)
(could set all edges to be a cost of 1)
3. Fill in routing table
A | 1
B | 2
C | 3
… | …

## Slide 26
Routing Among the ISPs: BGP
Inter-AS routing protocol involves coordination amongst multiple AS’s, a common protocol needs to be used
AS 1
Border Gateway Protocol (BGP) is used for exchanging routing information between AS

## Slide 27
Routing Among the ISPs: BGP
Inter-AS routing protocol involves coordination amongst multiple AS’s, a common protocol needs to be used
AS 1
Border Gateway Protocol (BGP) is used for exchanging routing information between AS
BGP allows a router to tell other AS’s that it exists and needs to be connected

## Slide 28
Routing Among the ISPs: BGP
Inter-AS routing protocol involves coordination amongst multiple AS’s, a common protocol needs to be used
AS 1
Border Gateway Protocol (BGP) is used for exchanging routing information between AS
BGP allows a router to tell other AS’s that it exists and needs to be connected
AS2
AS3
AS4
AS5
AS6
AS6
AS consists of gateway routers and internal routers

## Slide 29
Routing Among the ISPs: BGP
Inter-AS routing protocol involves coordination amongst multiple AS’s, a common protocol needs to be used
AS 1
Border Gateway Protocol (BGP) is used for exchanging routing information between AS
BGP allows a router to tell other AS’s that it exists and needs to be connected
AS2
AS3
AS4
AS5
AS6
AS6
AS consists of gateway routers and internal routers

## Slide 30
Routing Among the ISPs: BGP
Inter-AS routing protocol involves coordination amongst multiple AS’s, a common protocol needs to be used
AS 1
AS2
AS3
AS4
AS5
AS6
AS6
AS consists of gateway routers and internal routers
“I am AS1 AND I EXIST!”

## Slide 31
Routing Among the ISPs: BGP
Inter-AS routing protocol involves coordination amongst multiple AS’s, a common protocol needs to be used
AS 1
AS2
AS3
AS4
AS5
AS6
AS6
AS consists of gateway routers and internal routers
“I am AS1 AND I EXIST!”
“A1 EXISTS AND FOUND THROUGH AS2”

## Slide 32
Announcements
HW2 due tonight
PA3 due Monday November 14th

## Slide 33
Routing Among the ISPs: BGP
BGP is the routing protocol used for routing amongst different ISPs + AS
Two important functions
Obtain prefix reachability information from neighboring ASs
 Determine the “best” routes to the prefixes
eBGP connectivity
iBGP connectivity
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS 2
AS 3
AS 1
1c
∂
gateway routers run both eBGP and iBGP protools

## Slide 34
Routing Among the ISPs: BGP
BGP is the routing protocol used for routing amongst different ISPs + AS
Two important functions
Obtain prefix reachability information from neighboring ASs
 Determine the “best” routes to the prefixes
eBGP connectivity
iBGP connectivity
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS 2
AS 3
AS 1
1c
gateway routers run both eBGP and iBGP protools
X
Prefix X connect
3a  2c “Hey I have X”
2a  1c “Hey AS 3 has X and I have AS3”
External BGP (eBGP)
Internal BGP (iBGP)
2c  2b
2c  2d
2c  2a

## Slide 35: BGP basics
when AS3 gateway router 3a advertises path AS3,X to AS2 gateway router 2c:
  AS3 promises to AS2 it will forward datagrams towards X
BGP session: two BGP routers (“peers”) exchange BGP messages over semi-permanent TCP connection:
  advertising paths to different destination network prefixes (BGP is a “path vector” protocol)
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS 2
AS 3
AS 1
X
BGP advertisement:
AS3, X

## Slide 36: BGP basics
Advertisements with BGP also include “BGP attributes”
Prefix (ip address or subnet) + attributes = “route”
Two important attributes:
  AS-PATH: list of ASes through which prefix advertisement has passed
  NEXT-HOP: indicates specific internal-AS router to next-hop AS

## Slide 37
2d learns (via iBGP) it can route to X via 2a or 2c
hot potato routing: choose local gateway that has least intra-domain cost (e.g., 2d chooses 2a, even though more AS hops to X): don’t worry about inter-domain cost!
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS2
AS3
AS1
X
AS3,X
AS1,AS3,X
OSPF link weights
201
152
112
263
5-37
Network Layer: Control Plane
Hot Potato Routing

## Slide 38
ICMP (Internet Control Message Protocol)
used by hosts & routers to communicate network-level information
  error reporting: unreachable host, network, port, protocol
  echo request/reply (used by ping)
network-layer “above” IP:
  ICMP msgs carried in IP datagrams
ICMP message: type, code plus first 8 bytes of IP datagram causing error
Type Code description
0 0 echo reply (ping)
3 0 dest. network unreachable
3 1 dest host unreachable
3 2 dest protocol unreachable
3 3 dest port unreachable
3 6 dest network unknown
3 7 dest host unknown
4 0 source quench (congestion
control - not used)
8 0 echo request (ping)
9 0 route advertisement
10 0 router discovery
11 0 TTL expired
12 0 bad IP header

## Slide 39
approaches to network control plane
  - per-router control (traditional)
  - logically centralized control (software defined networking)
traditional routing algorithms
  - routing: link state, distance vectors
  - implementation in Internet: OSPF, BGP
Internet Control Message Protocol
Control Plane Wrap up
Routing
Algorithm
data
plane
control
plane
Next:
Link Layer
Security
Random Topics in session, presentation, and physical layers