## Slide 1: CSCI 466: Networks
Reliable Data Transfer (RDT)
Reese Pearsall
Fall 2023
https://www.cs.montana.edu/pearsall/classes/fall2023/466/main.html
*All images are stolen from the internet

## Slide 2
Announcements
PA1 Due tonight
Quiz 3 on Friday
DNS
SMTP
DTP
P2P
Transport Layer Intro
Reliable Data Transfer

## Slide 3
Announcements
PA1 Due tonight
Quiz 3 on Friday
DNS
SMTP
DTP
P2P
Transport Layer Intro
Reliable Data Transfer

## Slide 4
Application Layer
Presentation Layer
Session Layer
Transport Layer
Network Layer
Data Link Layer
Physical Layer
OSI Model
Messages from Network Applications
Application Layer
Physical Layer
Bits being transmitted over some medium
*In the textbook, they condense it to a 5-layer model, but 7 layers is what is most used
*
*

## Slide 5
Transport Layer
Multiplexing is the process of gathering chunks from sockets, encapsulating chunks with header information, and passing the segment into the network layer
Socket
data
data
data
data
data
data
header
header
header
Segment
Demultiplexing is the receiving segments from the transport layer and delivering the segment to the correct socket.

## Slide 6
Transport Layer
Service | TCP/UDP Port Number
HTTP | 80
DNS | 53
HTTPS | 443
FTP | 20 & 21
SMTP | 25
POP3 | 110
SSH | 22
Runescape | 43594, 43595

## Slide 7
Transport Layer
Source Port #
Dest. Port #
Length
Checksum
Data
16 bits
16 bits
Transport Layer provides a checksum that is used to determine whether bits within a segment have been altered
(HTTP Request, DNS, FTP, etc)

## Slide 8
Transport Layer
Reliable Data Transfer
Application
Transport
Network
Characteristics of unreliable channel will determine complexity of reliable data transfer protocol (rdt)
What are some ways in which the network channel can be unreliable?
Things to consider:
Corruption
Loss of packets
Duplicate delivery

## Slide 9
Transport Layer
Reliable Data Transfer

## Slide 10
Transport Layer
Reliable Data Transfer
Bruce Lee FSM
Wait for ball
in_court(ball) == True
send_it(ball)
Event causing state transition
Actions taken on state transition

## Slide 11
Transport Layer
Reliable Data Transfer 1.0
RDT 1.0
Assumptions:
Unidirectional long data flows
Perfectly reliable channel
No bit errors
No packet loss
No packet reordering

## Slide 12
Transport Layer
Reliable Data Transfer 1.0
RDT 1.0
Assumptions:
Unidirectional long data flows
Perfectly reliable channel
No bit errors
No packet loss
No packet reordering

## Slide 13
Transport Layer
Reliable Data Transfer 1.0
RDT 1.0
Assumptions:
Unidirectional long data flows
Perfectly reliable channel
No bit errors
No packet loss
No packet reordering
Sender
Wait for call from above

## Slide 14
Transport Layer
Reliable Data Transfer 1.0
RDT 1.0
Assumptions:
Unidirectional long data flows
Perfectly reliable channel
No bit errors
No packet loss
No packet reordering
rdt_send(data)
Sender
Wait for call from above

## Slide 15
Transport Layer
Reliable Data Transfer 1.0
RDT 1.0
Assumptions:
Unidirectional long data flows
Perfectly reliable channel
No bit errors
No packet loss
No packet reordering
packet = make_pkt(data)
udt_send(packet)
rdt_send(data)
Sender
Wait for call from above

## Slide 16
Transport Layer
Reliable Data Transfer 1.0
RDT 1.0
Assumptions:
Unidirectional long data flows
Perfectly reliable channel
No bit errors
No packet loss
No packet reordering
packet = make_pkt(data)
udt_send(packet)
rdt_send(data)
Sender
Wait for call from above
Receiver
Wait for call from Network

## Slide 17
Transport Layer
Reliable Data Transfer 1.0
RDT 1.0
Assumptions:
Unidirectional long data flows
Perfectly reliable channel
No bit errors
No packet loss
No packet reordering
packet = make_pkt(data)
udt_send(packet)
rdt_send(data)
Sender
Wait for call from above
Receiver
Wait for call from Network
rdt_rcv(data)

## Slide 18
Transport Layer
Reliable Data Transfer 1.0
RDT 1.0
Assumptions:
Unidirectional long data flows
Perfectly reliable channel
No bit errors
No packet loss
No packet reordering
packet = make_pkt(data)
udt_send(packet)
rdt_send(data)
Sender
Wait for call from above
Receiver
Wait for call from Network
rdt_rcv(data)
data = extract(packet)
deliver_data(data)

## Slide 19
Transport Layer
Reliable Data Transfer 2.0
RDT 2.0
Potential for bit errors
How can we detect errors?
Reliable Channel
Unreliable Channel
Reliable Channel
1110
0010
???

## Slide 20
Transport Layer
Reliable Data Transfer 2.0
RDT 2.0
Potential for bit errors
How can we detect errors?
-Checksum
Reliable Channel
Unreliable Channel
Reliable Channel
1110
0010
???

## Slide 21
Transport Layer
Reliable Data Transfer 2.0
RDT 2.0
Potential for bit errors
How can we detect errors?
-Checksum
What is a good way to handle and prevent errors?
Reliable Channel
Unreliable Channel
Reliable Channel
1110
0010
???

## Slide 22
Transport Layer
Reliable Data Transfer 2.0
RDT 2.0
Potential for bit errors
How can we detect errors?
-Checksum
What is a good way to handle and prevent errors?
- Acknowledged packet, Ask for retransmit if needed
Reliable Channel
Unreliable Channel
Reliable Channel
1110
0010
???

## Slide 23
Transport Layer
Reliable Data Transfer 2.0
RDT 2.0
Potential for bit errors
How can we detect errors?
-Checksum
What is a good way to handle and prevent errors?
- Acknowledged packet, Ask for retransmit if needed
Sender
Wait for call from appl
sndpkt = make_pkt(data, checksum)
udt_send(sndpkt)
rdt_send(data)
Stop-and-wait: sender sends one packet, then waits for receiver response

## Slide 24
Transport Layer
Reliable Data Transfer 2.0
RDT 2.0
Potential for bit errors
How can we detect errors?
-Checksum
What is a good way to handle and prevent errors?
- Acknowledged packet, Ask for retransmit if needed
Sender
Wait for call from appl
sndpkt = make_pkt(data, checksum)
udt_send(sndpkt)
rdt_send(data)
Wait for ACK or NAK
Stop-and-wait: sender sends one packet, then waits for receiver response

## Slide 25
Transport Layer
Reliable Data Transfer 2.0
Sender
Wait for call from appl
sndpkt = make_pkt(data, checksum)
udt_send(sndpkt)
rdt_send(data)
Wait for ACK or NAK
Receiver

## Slide 26
Transport Layer
Reliable Data Transfer 2.0
Sender
Wait for call from appl
sndpkt = make_pkt(data, checksum)
udt_send(sndpkt)
rdt_send(data)
Wait for ACK or NAK
Receiver
Wait for call from below

## Slide 27
Transport Layer
Reliable Data Transfer 2.0
Sender
Wait for call from appl
sndpkt = make_pkt(data, checksum)
udt_send(sndpkt)
rdt_send(data)
Wait for ACK or NAK
Receiver
Wait for call from below
udt_send(NAK)
rdt_rcv(rcvpkt) && corrupt(rcvpkt)

## Slide 28
Transport Layer
Reliable Data Transfer 2.0
Sender
Wait for call from appl
sndpkt = make_pkt(data, checksum)
udt_send(sndpkt)
rdt_send(data)
Wait for ACK or NAK
Receiver
Wait for call from below
udt_send(NAK)
rdt_rcv(rcvpkt) && corrupt(rcvpkt)
rdt_rcv(rcvpkt) && !corrupt(rcvpkt)
data = extract(packet)
deliver_data(data)
udt_send(ACK)

## Slide 29
Transport Layer
Reliable Data Transfer 2.0
Sender
Wait for call from appl
sndpkt = make_pkt(data, checksum)
udt_send(sndpkt)
rdt_send(data)
Wait for ACK or NAK
Receiver
Wait for call from below
udt_send(NAK)
rdt_rcv(rcvpkt) && corrupt(rcvpkt)
rdt_rcv(rcvpkt) && !corrupt(rcvpkt)
data = extract(packet)
deliver_data(data)
udt_send(ACK)

## Slide 30
Transport Layer
Reliable Data Transfer 2.0
Sender
Wait for call from appl
sndpkt = make_pkt(data, checksum)
udt_send(sndpkt)
rdt_send(data)
Wait for ACK or NAK
Receiver
Wait for call from below
udt_send(NAK)
rdt_rcv(rcvpkt) && corrupt(rcvpkt)
rdt_rcv(rcvpkt) && !corrupt(rcvpkt)
data = extract(packet)
deliver_data(data)
udt_send(ACK)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
isNAK(rcvpkt)

## Slide 31
Transport Layer
Reliable Data Transfer 2.0
Sender
Wait for call from appl
sndpkt = make_pkt(data, checksum)
udt_send(sndpkt)
rdt_send(data)
Wait for ACK or NAK
Receiver
Wait for call from below
udt_send(NAK)
rdt_rcv(rcvpkt) && corrupt(rcvpkt)
rdt_rcv(rcvpkt) && !corrupt(rcvpkt)
data = extract(packet)
deliver_data(data)
udt_send(ACK)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
isNAK(rcvpkt)
rdt_rcv(rcvpkt) && isACK(rcvpkt)
Λ
Λ = do no action, follow arrow to next state

## Slide 32
Transport Layer
Reliable Data Transfer 2.0
Sender
Wait for call from appl
sndpkt = make_pkt(data, checksum)
udt_send(sndpkt)
rdt_send(data)
Wait for ACK or NAK
Receiver
Wait for call from below
udt_send(NAK)
rdt_rcv(rcvpkt) && corrupt(rcvpkt)
rdt_rcv(rcvpkt) && !corrupt(rcvpkt)
data = extract(packet)
deliver_data(data)
udt_send(ACK)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
isNAK(rcvpkt)
rdt_rcv(rcvpkt) && isACK(rcvpkt)
Λ
Λ = do no action, follow arrow to next state
What happens if ACK/NAK Corrupted?
Duplicate delivery, or no retransmission
Solution?
Retransmit if CORRUPT packet received
How to deal we duplicate Packets?
 ???

## Slide 33
Transport Layer
Reliable Data Transfer 2.0
Sender
Wait for call from appl
sndpkt = make_pkt(data, checksum)
udt_send(sndpkt)
rdt_send(data)
Wait for ACK or NAK
Receiver
Wait for call from below
udt_send(NAK)
rdt_rcv(rcvpkt) && corrupt(rcvpkt)
rdt_rcv(rcvpkt) && !corrupt(rcvpkt)
data = extract(packet)
deliver_data(data)
udt_send(ACK)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
isNAK(rcvpkt)
rdt_rcv(rcvpkt) && isACK(rcvpkt)
Λ
Λ = do no action, follow arrow to next state
What happens if ACK/NAK Corrupted?
Duplicate delivery, or no retransmission
Solution?
Retransmit if CORRUPT packet received
How to deal we duplicate Packets?
 Sequence Numbers

## Slide 34
Transport Layer
Reliable Data Transfer 2.1
Sender
Potential for bit errors and garbled ACKs
Wait for call 0 from above
(We only need to use 0 or 1 for the sequence number)

## Slide 35
Transport Layer
Reliable Data Transfer 2.1
Sender
Potential for bit errors and garbled ACKs
Wait for call 0 from above
(We only need to use 0 or 1 for the sequence number)
Wait for ACK or NAK 0
rdt_send(data)
sndpkt = make_pkt(0, data, checksum)
udt_send(sndpkt)

## Slide 36
Transport Layer
Reliable Data Transfer 2.1
Sender
Potential for bit errors and garbled ACKs
Wait for call 0 from above
(We only need to use 0 or 1 for the sequence number)
Wait for ACK or NAK 0
rdt_send(data)
sndpkt = make_pkt(0, data, checksum)
udt_send(sndpkt)
rdt_rcv(rcvpacket) &&
( corrupt(rcvpkt) || isNAK(rcvpkt)
udt_send(sndpkt)

## Slide 37
Transport Layer
Reliable Data Transfer 2.1
Sender
Potential for bit errors and garbled ACKs
Wait for call 0 from above
(We only need to use 0 or 1 for the sequence number)
Wait for ACK or NAK 0
rdt_send(data)
sndpkt = make_pkt(0, data, checksum)
udt_send(sndpkt)
rdt_rcv(rcvpacket) &&
( corrupt(rcvpkt) || isNAK(rcvpkt)
udt_send(sndpkt)
Wait for call 1 from above
rdt_rcv(rcvpacket) &&
notcorrupt(rcvpkt) &&
isAck(rcvpkt)
Λ

## Slide 38
Transport Layer
Reliable Data Transfer 2.1
Sender
Potential for bit errors and garbled ACKs
Wait for call 0 from above
(We only need to use 0 or 1 for the sequence number)
Wait for ACK or NAK 0
rdt_send(data)
sndpkt = make_pkt(0, data, checksum)
udt_send(sndpkt)
rdt_rcv(rcvpacket) &&
( corrupt(rcvpkt) || isNAK(rcvpkt)
udt_send(sndpkt)
Wait for call 1 from above
Wait for ACK or NAK 1
rdt_rcv(rcvpacket) &&
notcorrupt(rcvpkt) &&
isAck(rcvpkt)
Λ
rdt_send(data)
sndpkt = make_pkt(1, data, checksum)
udt_send(sndpkt)

## Slide 39
Transport Layer
Sender
Wait for call 0 from above
Wait for ACK or NAK 0
rdt_send(data)
sndpkt = make_pkt(0, data, checksum)
udt_send(sndpkt)
rdt_rcv(rcvpacket) &&
( corrupt(rcvpkt) || isNAK(rcvpkt)
udt_send(sndpkt)
Wait for call 1 from above
Wait for ACK or NAK 1
rdt_rcv(rcvpacket) &&
notcorrupt(rcvpkt) &&
isAck(rcvpkt)
Λ
rdt_send(data)
sndpkt = make_pkt(1, data, checksum)
udt_send(sndpkt)
rdt_rcv(rcvpacket) &&
( corrupt(rcvpkt) || isNAK(rcvpkt)
udt_send(sndpkt)

## Slide 40
Transport Layer
Sender
Wait for call 0 from above
Wait for ACK or NAK 0
rdt_send(data)
sndpkt = make_pkt(0, data, checksum)
udt_send(sndpkt)
rdt_rcv(rcvpacket) &&
( corrupt(rcvpkt) || isNAK(rcvpkt)
udt_send(sndpkt)
Wait for call 1 from above
Wait for ACK or NAK 1
rdt_rcv(rcvpacket) &&
notcorrupt(rcvpkt) &&
isAck(rcvpkt)
Λ
rdt_send(data)
sndpkt = make_pkt(1, data, checksum)
udt_send(sndpkt)
rdt_rcv(rcvpacket) &&
( corrupt(rcvpkt) || isNAK(rcvpkt)
udt_send(sndpkt)
rdt_rcv(rcvpacket) &&
notcorrupt(rcvpkt) &&
isAck(rcvpkt)
Λ

## Slide 41
Transport Layer
Reliable Data Transfer 2.1
RDT 2.1
Potential for bit errors and garbled ACKs
Stop-and-wait: sender sends one packet, then waits for receiver response
(We only need 0 or 1 for the sequence #)

## Slide 42
Transport Layer
Reliable Data Transfer 2.1
Receiver

## Slide 43
Transport Layer
Reliable Data Transfer 2.1
Receiver

## Slide 44
Transport Layer
Reliable Data Transfer 2.1
Receiver

## Slide 45
Transport Layer
Reliable Data Transfer 2.1
Receiver

## Slide 46
Transport Layer
Reliable Data Transfer 2.1
Receiver

## Slide 47
Transport Layer
Reliable Data Transfer 2.2
Sender
Instead of NAKs, we provide the sequence number of the packet for our ACK (ACK1, ACK0)
Duplicate ACK at sender results in same action as NAK: retransmit current pkt

## Slide 48
Transport Layer
Reliable Data Transfer 2.2
Receiver

## Slide 49
Transport Layer
A quick meatball break…

## Slide 50
Transport Layer
Reliable Data Transfer 3.0
Potential for:
bit errors
garbled ACKs
Lost/dropped packets
We will still need checksums, Seq #’s, ACKS, but we need more
What if an ACK gets dropped? Sender is stuck waiting forever

## Slide 51
Transport Layer
Reliable Data Transfer 3.0
Potential for:
bit errors
garbled ACKs
Lost/dropped packets
We will still need checksums, Seq #’s, ACKS, but we need more
What if an ACK gets dropped? Sender is stuck waiting forever
Solution?

## Slide 52
Transport Layer
Reliable Data Transfer 3.0
Potential for:
bit errors
garbled ACKs
Lost/dropped packets
We will still need checksums, Seq #’s, ACKS, but we need more
What if an ACK gets dropped? Sender is stuck waiting forever
A timer
Retransmit if ACK received in X amount of time
What if the ACK is just taking a really long time to arrive?

## Slide 53
Transport Layer
Reliable Data Transfer 3.0
Potential for:
bit errors
garbled ACKs
Lost/dropped packets
We will still need checksums, Seq #’s, ACKS, but we need more
What if an ACK gets dropped? Sender is stuck waiting forever
A timer
Retransmit if ACK received in X amount of time
What if the ACK is just taking a really long time to arrive? This will be duplicate data, but we have a Seq # to handle that

## Slide 54
Transport Layer
Reliable Data Transfer 3.0
(Packets can get dropped or lost)
Sender

## Slide 55
Transport Layer
Reliable Data Transfer 3.0
(Packets can get dropped or lost)
Sender

## Slide 56
Transport Layer
Reliable Data Transfer 3.0
(Packets can get dropped or lost)
Sender

## Slide 57
Transport Layer
Reliable Data Transfer 3.0
(Packets can get dropped or lost)
Sender

## Slide 58
Transport Layer
Reliable Data Transfer 3.0
(Packets can get dropped or lost)
Sender

## Slide 59
Transport Layer
Reliable Data Transfer 3.0
(Packets can get dropped or lost)
Sender

## Slide 60
Transport Layer
Reliable Data Transfer 3.0
(Packets can get dropped or lost)
Sender
Receiver will be same as 2.2

## Slide 61
Transport Layer
Reliable Data Transfer 3.0
(Packets can get dropped or lost)
Sender
If we are waiting to send packet, but we receive a packet for some reason, this packet must be a duplicate packet, so do nothing

## Slide 62
Transport Layer
Reliable Data Transfer 3.0
(Packets can get dropped or lost)

## Slide 63
Transport Layer
Reliable Data Transfer 3.0
(Packets can get dropped or lost)

## Slide 64
Transport Layer
Reliable Data Transfer 3.0
(Packets can get dropped or lost)

## Slide 65
Transport Layer
Reliable Data Transfer 3.0
(Packets can get dropped or lost)