## Slide 1: CSCI 466: Networks Network Layer – Data Plane
Reese Pearsall Fall 2023
https://www.cs.montana.edu/pearsall/classes/fall2023/466/main.html
1
*All images are stolen from the internet

## Slide 2: Announcements
Wireshark Lab 2 due on Friday
Quiz 4 also on Friday
“Who is congesting the network???”
UDP:
meme made by reese

## Slide 3: Application Layer
Presentation Layer
Session Layer
Transport Layer
Network Layer
Data Link Layer
Messages from Network Applications
Application Layer
Physical Layer
Physical Layer
*In the textbook, they condense it to a 5-layer model,
but 7 layers is what is most used
Bits being transmitted over a medium
*
*

## Slide 4: Application Layer
Presentation Layer
Session Layer
Transport Layer
Network Layer
Data Link Layer
Messages from Network Applications
Application Layer
Physical Layer
Bits being transmitted over a medium
*
*
Physical Layer
*In the textbook, they condense it to a 5-layer model,
but 7 layers is what is most used

## Slide 5: Application Layer
Transport Layer
Message
Transport Layer Header
“Segment”
Application Layer Protocol (ex. HTPP)
Transport Layer Protocol
(ex. TCP)
Our packet of information so far…

## Slide 6: Application Layer
Transport Layer
Message
Transport Layer Header
“Segment”
Application Layer Protocol (ex. DNS)
Transport Layer Protocol
(ex. UDP)
Our packet of information so far…

## Slide 7
Application Layer
Transport Layer
???
Network Layer
We’ve only looked at protocols that are running on some host

## Slide 8: We will now shift our focus towards routers, or packet switches
In the network layer, we finally get to leave the host and adventure into the network

## Slide 9
Routers do not have functionality for application & transport layer protocols
TCP
TCP

## Slide 10: We will now shift our focus towards routers, or packet switches
Routing: determine route taken by packets from source to destination

## Slide 11
We will now shift our focus towards routers, or packet switches
Routing: determine route taken by packets from source to destination
There is likely very many paths from one host to another! Which is the most efficient path?

## Slide 12: We will now shift our focus towards routers, or packet switches
Forwarding: move packets from router’s input to appropriate router output
?
?
?
Which path should be taken?

## Slide 13
Individual routing algorithm components in each and every router interact in the control plane
Routing
Algorithm
data
plane
control
plane
1
2
0111
values in arriving
packet header
3

## Slide 14
Individual routing algorithm components in each and every router interact in the control plane
Routing
Algorithm
data
plane
control
plane
1
2
0111
values in arriving
packet header
3

## Slide 15: Software-Defined Networking (SDN) control plane
Remote controller computes, installs forwarding tables in routers
data
plane
control
plane
Remote Controller
CA
CA
CA
CA
CA
1
2
0111
3
values in arriving
packet header

## Slide 16: Network Layer
Responsible for the delivery of data through a network
Routing
Forwarding
forwarding
routing

## Slide 17: Network Layer
No guarantees on:
  successful datagram delivery to destination
  timing or order of delivery
  bandwidth available to end-end flow
Internet “best effort” service model

## Slide 18: Router Architecture Overview
Destination-based forwarding
  Forwarding decisions are based on the destination of the packet
Generalized forwarding
  Forwarding decisions based on any set of header field values

## Slide 19: Router Architecture Overview
Bit-level reception (physical layer)
Link Layer Protocol
Lookup, forwarding, queueing
Bits received
…
…
Such as over the wire or through the air
Next layer of OSI
model
Ex. Ethernet
Evaluate header field values, lookup output port using forwarding table in memory
Queueing will occur if datagrams arrive faster
than forwarding rate into the switching fabric
“Switching Fabric”
INPUT PORT

## Slide 20: Router Architecture Overview
Storing, ready for send off
Link Layer Protocol
Send bits
“Switching Fabric”
…
…
To destination
OUTPUT PORT

## Slide 21: Forwarding Techniques
Lookup, forwarding, queueing
…
…
Address range | Interface (output link)
128.11.52.0 – 128.11.52.255 | 1
153.90.2.0 – 153.90.2.255 | 2
153.90.2.87 – 153.90.2.89 | 3
Routing Table
Connection-less
does not require startup,
Has no idea where the final destination is
This routing table could get very big…
IP addresses need 32/64 bits of memory each

## Slide 22: Forwarding Techniques
Lookup, forwarding, queueing
…
…
Address range | Interface (output link)
128.11.52.0 – 128.11.52.255 | 1
153.90.2.0 – 153.90.2.255 | 2
153.90.2.87 – 153.90.2.89 | 3
Routing Table
Connection-less
does not require startup,
Has no idea where the final destination is
Ranges of IP Addresses
Prefix of IP addresses

## Slide 23: Forwarding Techniques
Lookup, forwarding, queueing
…
…
Address range | Interface (output link)
11001000 00010111 00010*** ********* | 1
11001000 00010111 00011000 ********* | 2
11001000 00010111 00011*** ******** | 3
otherwise | 4
Longest prefix matching
when looking for forwarding table entry for given destination address, use longest address prefix that matches destination address
examples:
DA: 11001000 00010111 000
11000 10101010
DA: 11001000 00010111 000
10110 10100001
which interface? which interface?

## Slide 24: Forwarding Techniques
Lookup, forwarding, queueing
…
…
Address range | Interface (output link)
11001000 00010111 00010*** ********* | 1
11001000 00010111 00011000 ********* | 2
11001000 00010111 00011*** ******** | 3
otherwise | 4
Longest prefix matching
when looking for forwarding table entry for given destination address, use longest address prefix that matches destination address
examples:
DA: 11001000 00010111 000
11000 10101010
DA: 11001000 00010111 000
10110 10100001
which interface? which interface?

## Slide 25: Forwarding Techniques
Lookup, forwarding, queueing
…
…
Address range | Interface (output link)
11001000 00010111 00010*** ********* | 1
11001000 00010111 00011000 ********* | 2
11001000 00010111 00011*** ******** | 3
otherwise | 4
Longest prefix matching
when looking for forwarding table entry for given destination address, use longest address prefix that matches destination address
examples:
DA: 11001000 00010111 000
11000 10101010
DA: 11001000 00010111 000
10110 10100001
which interface? which interface?

## Slide 26: Forwarding Techniques
Lookup, forwarding, queueing
…
…
Address range | Interface (output link)
11001000 00010111 00010*** ********* | 1
11001000 00010111 00011000 ********* | 2
11001000 00010111 00011*** ******** | 3
otherwise | 4
Longest prefix matching
when looking for forwarding table entry for given destination address, use longest address prefix that matches destination address
examples:
DA: 11001000 00010111 000
11000 10101010
DA: 11001000 00010111 000
10110 10100001
which interface? which interface?

## Slide 27: Forwarding Techniques
Lookup, forwarding, queueing
…
…
Address range | Interface (output link)
11001000 00010111 00010*** ********* | 1
11001000 00010111 00011000 ********* | 2
11001000 00010111 00011*** ******** | 3
otherwise | 4
Longest prefix matching
when looking for forwarding table entry for given destination address, use longest address prefix that matches destination address
These lookups need to happen in nanoseconds for our network to function
Ternary content addressable memories (TCAMs) are used in modern routers to do LPM
Cisco routers can carry millions of TCAM entries in their routers

## Slide 28: Fabric Switch and Switching
Switching fabric: Mechanism that forwards data from an input port to output port
Switching via memory:
Handled by a CPU (routing processor) Cannot forward data in parallel

## Slide 29: Fabric Switch and Switching
Switching fabric: Mechanism that forwards data from an input port to output port
Switching via memory:
Handled by a CPU (routing processor) Cannot forward data in parallel
Switching via bus:
Datagrams are prepended with a header
A “bus” transports input port datagrams to output ports
“keep going around the roundabout until you find your port”

## Slide 30: Fabric Switch and Switching
Switching fabric: Mechanism that forwards data from an input port to output port
Switching via memory:
Handled by a CPU (routing processor) Cannot forward data in parallel
Switching via bus:
Datagrams are prepended with a header
A “bus” transports input port datagrams to output ports
Switching via network:
A network of buses
“keep going around the roundabout until you find your port”
One shared bus, but can only fit one datagram

## Slide 31: Input Queueing
fabric slower than input ports combined  queueing may occur at input queues
Input ports
Input ports
Output ports
Output ports
Head-of-the-Line (HOL) blocking: queued datagram at front of queue prevents others in queue from moving forward

## Slide 32: Output Queueing
Storing, ready
for send off
Link Layer Protocol
Send bits
OUTPUT PORT
Input
port
Input port
Input port
Input
port
Switching Fabric
Incoming packets will have to wait for buffer space to become available
Possible solutions:
Remove a packet
  Tail drop: drop arriving packet
  Priority: drop/remove on a priority basis
  Random: drop/remove randomly

## Slide 33: Packet Scheduling
Scheduling is used to determine the next packet to send on the link
FIFO (first in first out): Send in order of arrival to queue

## Slide 34: Packet Scheduling
Scheduling is used to determine the next packet to send on the link
Priority: packets are classified into priority classes. High priority = sent over link first

## Slide 35: Packet Scheduling
Scheduling is used to determine the next packet to send on the link
Round robin weighted fair queueing: packets are classified into priority classes. Each class gets to send one packet during a “cycle”
Packet from the priority group gets sent
Packet from the middle class gets sent Packet from the plebian class gets sent