## Slide 1: CSCI 466: Networks IP Addresses, IP Protocol, Subnets
Reese Pearsall Fall 2023
https://www.cs.montana.edu/pearsall/classes/fall2023/466/main.html
1
*All images are stolen from the internet

## Slide 2: Announcements
PA2 Due date pushed to this Friday (10/20)
Friday will be a work day for PA2 (no lecture)

## Slide 3: Application Layer
Presentation Layer
Session Layer
Transport Layer
Network Layer
Data Link Layer
Messages from Network Applications
Application Layer
Physical Layer
Physical Layer
*In the textbook, they condense it to a 5-layer model,
but 7 layers is what is most used
Bits being transmitted over a medium
*
*

## Slide 4: Application Layer
Presentation Layer
Session Layer
Transport Layer
Network Layer
Data Link Layer
Messages from Network Applications
Application Layer
Physical Layer
Bits being transmitted over a medium
*
*
Physical Layer
*In the textbook, they condense it to a 5-layer model,
but 7 layers is what is most used

## Slide 5: Application Layer
Transport Layer
Message
Transport Layer Header
“Segment”
Application Layer Protocol (ex. HTPP)
Transport Layer Protocol
(ex. TCP)
Our packet of information so far…

## Slide 6: Application Layer
Transport Layer
Message
Transport Layer Header
“Segment”
Application Layer Protocol (ex. DNS)
Transport Layer Protocol
(ex. UDP)
Our packet of information so far…

## Slide 7
Routers do not have functionality for application & transport layer protocols

## Slide 8
We will now shift our focus towards routers, or packet switches
Routing: determine route taken by packets from source to destination
There is likely very many paths from one host to another! Which is the most efficient path?

## Slide 9: We will now shift our focus towards routers, or packet switches
Forwarding: move packets from router’s input to appropriate router output
?
?
?
Which path should be taken?

## Slide 10: Network Layer
Responsible for the delivery of data through a network
Routing
Forwarding

## Slide 11: Forwarding Techniques
Lookup, forwarding, queueing
…
…
Address range | Interface (output link)
11001000 00010111 00010*** ********* | 1
11001000 00010111 00011000 ********* | 2
11001000 00010111 00011*** ******** | 3
otherwise | 4
Longest prefix matching
when looking for forwarding table entry for given destination address, use longest address prefix that matches destination address
examples:
DA: 11001000 00010111 000
11000 10101010
DA: 11001000 00010111 000
10110 10100001
which interface? which interface?

## Slide 12: IP addressing, IPv4, and IPv6
https://www.rfc-editor.org/rfc/rfc791

## Slide 13: IPv4: 32-bit addresses (decimal)
Packets traversing through the network layer are referred to as a datagram. Each packet gets an IPv4/IPv6 header
Message
Transport
Layer Header
IP Header
Transport Layer Header
Message
IPv4 Header
192.149.252.76
IPv6: 128-bit addresses (hexademical)
3ffe:1900:fe21:4545::
Why do we need IPv6?

## Slide 14: Packets traversing through the network layer are referred to as a datagram. Each packet gets an IPv4/IPv6 header
Message
Transport
Layer Header
IP Header
Transport Layer Header
Message
IPv4 Header
TCP header = 20 bytes IP header = 20 bytes

## Slide 15
IP Address: Globally unique* 32 bit (4 byte) dotted decimal number assigned to interfaces on hosts and routers
193.32.216.9

## Slide 16: IP Address: Globally unique* 32 bit (4 byte) dotted decimal number assigned to interfaces on hosts and routers
193.32.216.9
1 bytes
1 bytes 1 bytes
1 bytes
(1 byte = 8 bits)
128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
1 | 1 | 0 | 0 | 0 | 0 | 0 | 1
128 + 64 + 1 = 193
193 = 11000001 in binary

## Slide 17
IP Address: Globally unique* 32 bit (4 byte) dotted decimal number assigned to interfaces on hosts and routers
193.32.216.9
=
11000001 00100000 11011000 00001001
(1 byte = 8 bits)
How many addresses are possible with a 32 bit number? ~4 billion possible IPv4 addresses

## Slide 18: 223.1.2.1
223.1.1.4
223.1.2.9
223.1.3.27
223.1.2.2
223.1.1.2
223.1.1.1
Subnet is a logical subdivision of an IP network
223.1.1.3
223.1.3.2
223.1.3.1

## Slide 19: 223.1.2.1
223.1.1.4
223.1.1.3
223.1.3.2
223.1.3.1
223.1.2.9
223.1.3.27
223.1.2.2
223.1.1.2
223.1.1.1
Subnet is a logical subdivision of an IP network In this network, we have 3 subnets

## Slide 20
223.1.1.4
223.1.2.9
223.1.3.27
223.1.2.1
223.1.2.2
223.1.3.1
223.1.3.2
223.1.1.3
223.1.1.2
223.1.1.1
IP addresses on the same subnet share a common prefix
38
Hosts on the same subnet can reach each other without going through a router
Subnet is a logical subdivision of an IP network In this network, we have 3 subnets
Computers usually have 1
interface. Routers have many
Devices usually have a private IP address, and a public IP address

## Slide 21
223.1.1.253
223.1.1.2
223.1.1.1
…
It is very common to have a range of IP addresses assigned to you (random assignment would be chaos)
Subnet mask
223.1.1.0/24
The leftmost 24 bits represent the prefix of the subnet
11111111 11111111 11111111 XXXXXXXX = 255.255.255.0
223.1.1.67
223.2.1.67
223.2.1.255
193.32.216.9
11000001 00100000 11011000 00001001
Host bits
Network bits

## Slide 22: Computers usually have 1 interface. Routers have many
223.1.1.0/24 223.1.2.0/24
223.1.3.0/24
Subnet is a logical subdivision of an IP network In this network, we have 3 subnets

## Slide 23: 6 subnets
1. 223.1.1.0/24
2. 223.1.7.0/24
3. 223.1.3.0/24
4. 223.1.8.0/24
5. 223.1.2.0/24
6. 223.1.9.0/23

## Slide 24: 223.1.1.0/24
Managing and Assigning Subnets
The subnet
contains the following addresses
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.1.5
…
223.1.1.252
223.1.1.253
223.1.1.254
How many addresses does a /24 subnet provide?
0 and 255 are reserved for special services (?)

## Slide 25: 223.1.1.0/24
Managing and Assigning Subnets
The subnet
contains the following addresses
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.1.5
…
223.1.1.252
223.1.1.253
223.1.1.254
How many addresses does a /24 subnet provide?
2^8 – 2 = 253
Class C network
0 and 255 are reserved for special services (?)

## Slide 26: Managing and Assigning Subnets
Subnet Type | Slash | Subnet Mask | Available Addresses
Class A | /8 | 255.0.0.0 | 2^24 – 2 = 16777216
Class B | /16 | 255.255.0.0 | 2^16 – 2 = 65,634
Class C | /24 | 255.255.255.0 | 2^8 – 2 = 254
Issues with this type of assignment?

## Slide 27: Managing and Assigning Subnets
Subnet Type | Slash | Subnet Mask | Available Addresses
Class A | /8 | 255.0.0.0 | 2^24 – 2 = 16777216
Class B | /16 | 255.255.0.0 | 2^16 – 2 = 65,634
Class C | /24 | 255.255.255.0 | 2^8 – 2 = 254
If I have 2000 devices, I will either need 8 class C subnets or 1 class B
subnet (but waste 63,000ish IP addresses)
We need a better way to subnet!

## Slide 28: Managing and Assigning Subnets
Our only available subnet masks have been:
255.255.255.0 | 11111111 11111111 11111111 00000000
255.255.0.0 | 11111111 11111111 00000000 00000000
255.0.0.0 | 11111111 00000000 00000000 00000000
CIDR introduces a more flexible way for subnetting We can any number of bits for our mask
Host bits!
200.23.16.0/20 = 11001000.00010111.00010000.00000000
Mask = 11111111.11111111.11110000.00000000
/24
/16
/8

## Slide 29: ISPs can now group and advertise organizations by IP blocks
We once again have another hierarchy 

## Slide 30
ISP’s block | 200.23.16.0/20 | 11001000 00010111 00010000 00000000
Organization 0 | 200.23.16.0/23 | 11001000 00010111 00010000 00000000
Organization 1 | 200.23.18.0/23 | 11001000 00010111 00010010 00000000
Organization 2 | 200.23.20.0/23 | 11001000 00010111 00010100 00000000
… |  | 
Organization 7 | 200.23.30.0.23 | 11001000 00010111 00011110 00000000
One possible way an ISP could organize IP blocks

## Slide 31: Devices on the same subnet communicate with each other by broadcasting a special message
223.1.3.27
223.1.1.2
223.1.1.3
223.1.3.2
223.1.3.1
223.1.1.1
This special message is when the source IP address of some packet is 255.255.255.255
223.1.1.4

## Slide 32: Devices on the same subnet communicate with each other by broadcasting a special message
223.1.1.4
223.1.3.27
223.1.1.2
223.1.1.1
This special message is when the source IP address of some packet is 255.255.255.255
255.255.255.255
(This request can sometimes be echoed to
neighboring subnets)
223.1.1.3
223.1.3.2
223.1.3.1

## Slide 33: How do IPs get obtained/assigned?
The Internet Corporation for Assigned Names and Numbers (ICANN) is responsible for managing and allocating IP address space for ISPs and organizations
(they also manage the DNS root servers!)
When an organization gets a range of IP addresses to use, how to we give assign them to devices?
Do we do it manually?
we could….

## Slide 34: DHCP
Dynamic Host Configuration Protocol (DHCP) is a plug-and-play, client-server protocol that allows a host to obtain an IP address automatically
When a host is automatically assigned an IP address, it might keep that one forever, or the IP addresses can be temporary
(more common)

## Slide 35: This process is similar to a TCP handshake!
Broadcast gets sent to all devices on the subnet!!
But devices that are not the dhcp server will ignore it

## Slide 36
This process is similar to a TCP handshake!

## Slide 37
This process is similar to a TCP handshake!

## Slide 38
IP/DHCP in Wireshark