## Slide 1: CSCI 466: Networks Link Layer: Addressing, LANs, ARP
Reese Pearsall Fall 2023
https://www.cs.montana.edu/pearsall/classes/fall2023/466/main.html
1
*All images are stolen from the internet

## Slide 2: Announcements
Next week’s quiz will be on Wednesday
No class Friday (Veterans Day)
PA2 Grades

## Slide 3: Multiple Access Links
Shared medium = possibility for receivers to get two frame at the same time, AKA a collision
Frame X
Frame y
Frames get tangled together, and neither frame can be read clearly by receiver

## Slide 4: Multiple Access Links
Shared medium = possibility for receivers to get two frame at the same time, AKA a collision
Frame X
Frame y
Frames get tangled together, and neither frame can be read clearly by receiver
In English, we have some rules to prevent collisions from happening
In the link layer, we will discuss 3 multiple access protocols:
Channel Partitioning, Random Access, and Taking Turns

## Slide 5: Random Access
Collisions will occur, but we will try to recover from them
Slotted ALOHA: Divide up time into discrete L/R “slots”
L = size of frame
R = Bandwidth
L/R = Time needed to transmit one frame
L/R
2 L/R
3 L/R
…
If collisions occur, the colliding nodes will flip a coin to see who should retransmit
Collision
Empty
Collision
Waiting a random delay
Waiting a random delay
Success
Empty
Collision
Success
Success

## Slide 6: “Taking turns” MAC protocols
polling:
centralized controller “invites” other nodes to transmit in turn
typically used with “dumb” devices
concerns:
  polling overhead
  latency
  single point of failure (master)
Bluetooth uses polling
centralized controller
client devices
poll
data
data

## Slide 7: Taking Turns
Token Passing
Nodes are connected in a circular manner, and pass a special frame (token) between each other
Can only transmit messages if you have the token

## Slide 8: LAN
Local Area Network (LAN)- A collection of devices in one physical location, typically that share a centralized internet connection
Router
Switch
(Within a LAN, we could have several Subnets)

## Slide 9: MAC addresses
32-bit IP address:
  network-layer address for interface
  used for layer 3 (network layer) forwarding
  e.g.: 128.119.40.136
MAC (or LAN or physical or Ethernet) address:
  function: used “locally” to get frame from one interface to another physically-connected interface (same subnet, in IP-addressing sense)
  48-bit MAC address (for most LANs) burned in NIC ROM, also sometimes software settable
hexadecimal (base 16) notation
(each “numeral” represents 4 bits)
  e.g.: 1A-2F-BB-76-09-AD

## Slide 10
Why do we need MAC addresses?
We need a way to physically identify a device on a network
IP addresses change frequently, but a MAC address will always be the same
An IP address is used to locate a device, a MAC address is used to identify a device
IP Address = Street Address, MAC Address = Name of person living in House
We need both an IP address and a MAC address to transmit a message

## Slide 11
192.168.0.4
01-08-4C-42-1B-52
192.168.0.2
00-04-5A-63-A1-66
192.168.0.3
02-06-1B-45-A2-12
192.168.0.1
04-06-2C-58-C5-78

## Slide 12
192.168.0.4
01-08-4C-42-1B-52
192.168.0.2
00-04-5A-63-A1-66
192.168.0.3
02-06-1B-45-A2-12
192.168.0.1
04-06-2C-58-C5-78
DST IP: 192.168.0.3

## Slide 13
192.168.0.4
01-08-4C-42-1B-52
192.168.0.2
00-04-5A-63-A1-66
192.168.0.3
02-06-1B-45-A2-12
192.168.0.1
04-06-2C-58-C5-78
DST IP: 192.168.0.3
A
B
C
We need Computer B’s MAC address!

## Slide 14: ARP
Protocol for mapping IP Addresses to MAC addresses
Used only for hosts and router interfaces on the same subnet
If the entry does not exist in the table, construct and send an ARP packet
First the machine checks its ARP table
Broadcasts the ARP packet to all interfaces on the LAN (255.255.255.255)
These tables are self-updated, and do not require manual entry*

## Slide 15: ARP
A wants to send datagram to B
  B’s MAC address not in A’s ARP table.
A broadcasts ARP query packet, containing B's IP address
  destination MAC address = FF-FF-FF-FF-FF-FF
  all nodes on LAN receive ARP query
B receives ARP packet, replies to A with its (B's) MAC address
  frame sent to A’s MAC address (unicast)
A caches (saves) IP-to-MAC address pair in its ARP table until information becomes old (times out)
  soft state: information that times out (goes away) unless refreshed
ARP is “plug-and-play”:
  nodes create their ARP tables without intervention from net administrator

## Slide 16
192.168.0.4
01-08-4C-42-1B-52
192.168.0.2
00-04-5A-63-A1-66
192.168.0.3
02-06-1B-45-A2-12
192.168.0.1
04-06-2C-58-C5-78
DST IP: 192.168.0.3
A
B
C
Computer A see’s that this IP is in its “group”, so it knows that Computer B must be in the same subnet!

## Slide 17
192.168.0.4
01-08-4C-42-1B-52
192.168.0.2
00-04-5A-63-A1-66
192.168.0.3
02-06-1B-45-A2-12
192.168.0.1
04-06-2C-58-C5-78
DST IP: 192.168.0.3
A
B
C
Broadcast an ARP request to the subnet, and hope that we get a response back

## Slide 18
192.168.0.4
01-08-4C-42-1B-52
192.168.0.2
00-04-5A-63-A1-66
192.168.0.3
02-06-1B-45-A2-12
192.168.0.1
04-06-2C-58-C5-78
DST IP: 192.168.0.3
A
B
C
Broadcast an ARP request to the subnet, and hope that we get a response back
Who is 192.168.0.3?
I need your MAC Address

## Slide 19
192.168.0.4
01-08-4C-42-1B-52
192.168.0.2
00-04-5A-63-A1-66
192.168.0.3
02-06-1B-45-A2-12
192.168.0.1
04-06-2C-58-C5-78
DST IP: 192.168.0.3
A
B
C
Broadcast an ARP request to the subnet, and hope that we get a response back
Who is 192.168.0.3?
I need your MAC Address
!!!
My MAC Address is:
02-06-1B-45-A2-12

## Slide 20
192.168.0.4
01-08-4C-42-1B-52
192.168.0.2
00-04-5A-63-A1-66
192.168.0.3
02-06-1B-45-A2-12
192.168.0.1
04-06-2C-58-C5-78
DST IP: 192.168.0.3
DST MAC: 02-06-1B-45-A2-12
A
B
C
Broadcast an ARP request to the subnet, and hope that we get a response back
!!!
My MAC Address is:
02-06-1B-45-A2-12

## Slide 21
192.168.0.2
00-04-5A-63-A1-66
192.168.0.1
04-06-2C-58-C5-78
DST IP: 12.56.78.34
A
G
34.11.16.58
23.44.76.81
12.56.78.34
Google.com
Home LAN

## Slide 22
192.168.0.2
00-04-5A-63-A1-66
192.168.0.1
04-06-2C-58-C5-78
DST IP: 12.56.78.34
A
G
34.11.16.58
23.44.76.81
12.56.78.34
Google.com
Home LAN
This IP address is not in its “group”, so it forwards it to the default gateway
(In most cases, we will need to issue an ARP request to get the MAC address of the default gateway)

## Slide 23
192.168.0.2
00-04-5A-63-A1-66
192.168.0.1
04-06-2C-58-C5-78
DST IP: 12.56.78.34
A
G
34.11.16.58
23.44.76.81
12.56.78.34
Google.com
Home LAN
The gateway router will look at the IP address of the packet, and determine the best route to get to google.com (network layer)

## Slide 24
192.168.0.2
00-04-5A-63-A1-66
192.168.0.1
04-06-2C-58-C5-78
DST IP: 12.56.78.34
A
G
34.11.16.58
23.44.76.81
12.56.78.34
Google.com
Home LAN
It now needs to forward the packet to 34.11.16.58, but it does not know its MAC address

## Slide 25
192.168.0.2
00-04-5A-63-A1-66
192.168.0.1
04-06-2C-58-C5-78
DST IP: 12.56.78.34
A
G
34.11.16.58
23.44.76.81
12.56.78.34
Google.com
Home LAN
It now needs to forward the packet to 34.11.16.58, but it does not know its MAC address
Issue another ARP request!
Who is 34.11.16.58?
I need your MAC Address

## Slide 26
192.168.0.2
00-04-5A-63-A1-66
192.168.0.1
04-06-2C-58-C5-78
DST IP: 12.56.78.34
A
G
34.11.16.58
23.44.76.81
12.56.78.34
Google.com
Home LAN
It now needs to forward the packet to 34.11.16.58, but it does not know its MAC address
Issue another ARP request!
Who is 34.11.16.58?
I need your MAC Address
My MAC address is:
05-52-3F-10-C5-57
05-52-3F-10-C5-57

## Slide 27
192.168.0.2
00-04-5A-63-A1-66
192.168.0.1
04-06-2C-58-C5-78
DST IP: 12.56.78.34
A
G
34.11.16.58
23.44.76.81
12.56.78.34
Google.com
Home LAN
The next destination is 23.44.76.81, but we need its MAC address!
05-52-3F-10-C5-57

## Slide 28
192.168.0.2
00-04-5A-63-A1-66
192.168.0.1
04-06-2C-58-C5-78
DST IP: 12.56.78.34
A
G
34.11.16.58
23.44.76.81
12.56.78.34
Google.com
Home LAN
The next destination is 23.44.76.81, but we need its MAC address!
Do another ARP!
05-52-3F-10-C5-57
My MAC address is:
09-12-0D-25-D8-74
(Remember that ARP gets broadcasted to all direct neighbors)

## Slide 29
192.168.0.2
00-04-5A-63-A1-66
192.168.0.1
04-06-2C-58-C5-78
DST IP: 12.56.78.34
A
G
34.11.16.58
23.44.76.81
12.56.78.34
Google.com
Home LAN
05-52-3F-10-C5-57
09-12-0D-25-D8-74

## Slide 30
192.168.0.2
00-04-5A-63-A1-66
192.168.0.1
04-06-2C-58-C5-78
DST IP: 12.56.78.34
A
G
34.11.16.58
23.44.76.81
12.56.78.34
Google.com
Home LAN
05-52-3F-10-C5-57
09-12-0D-25-D8-74
My MAC address is:
01-33-2F-84-B8-55
Who is 12.56.78.34?
I need your MAC Address
We need to issue one final ARP request, and get the MAC address of our final destination

## Slide 31
192.168.0.2
00-04-5A-63-A1-66
192.168.0.1
04-06-2C-58-C5-78
DST IP: 12.56.78.34
A
G
34.11.16.58
23.44.76.81
12.56.78.34
Google.com
Home LAN
05-52-3F-10-C5-57
09-12-0D-25-D8-74
We need to issue one final ARP request, and get the MAC address of our final destination
01-33-2F-84-B8-55

## Slide 33
Finding your MAC Address
Ipconfig/all

## Slide 34: Ethernet
“dominant” wired LAN technology:
single chip, multiple speeds (e.g., Broadcom BCM5761)
first widely used LAN technology
simpler, cheap
kept up with speed race: 10 Mbps – 10 Gbps
Metcalfe’s Ethernet sketch

## Slide 35: Ethernet
switch
bus: coaxial cable
star
Link Layer and LANs
Ethernet Topology
(outdated)

## Slide 36
Ethernet frame structure
sending adapter encapsulates IP datagram (or other network layer protocol packet) in Ethernet frame
preamble:
7 bytes with pattern 10101010 followed by one byte with pattern 10101011
used to synchronize receiver, sender clock rates
dest.
address
source
address
data (payload)
CRC
preamble
type

## Slide 37: Ethernet frame structure (more)
addresses: 6 byte source, destination MAC addresses
  if adapter receives frame with matching destination address, or with broadcast address (e.g. ARP packet), it passes data in frame to network layer protocol
  otherwise, adapter discards frame
type: indicates higher layer protocol (mostly IP but others possible, e.g., Novell IPX, AppleTalk)
CRC: cyclic redundancy check at receiver
  error detected: frame is dropped
dest.
address
source
address
data (payload)
CRC
preamble
type

## Slide 38
Ethernet switch
Switches will store and forward ethernet frames
Hosts have dedicated, direct connection to switch
Ethernet protocol used on each incoming link, but no collisions between links
Switching: A-A’ and B-B’ can transmit simultaneously, without collisions
Transparent: Hosts are not aware
they are connected to a switch
Plug and play; self-learning
A
A’
B
B’
C
C’
1
2
3
4
5
6
= ethernet cable

## Slide 39
Switches vs. routers
both are store-and-forward:
routers: network-layer devices (examine network-layer headers)
switches: link-layer devices (examine link-layer headers)
both have forwarding tables:
routers: compute tables using routing algorithms, IP addresses
switches: learn forwarding table using flooding, learning, MAC addresses
application
transport
network
link
physical
network
link
physical
link
physical
switch
datagram
application
transport
network
link
physical
frame
frame
frame
datagram

## Slide 40
https://www.youtube.com/watch?v=1z0ULvg_pW8