## Slide 1: CSCI 466: Networks
Network Performance
Reese Pearsall
Fall 2024
https://www.cs.montana.edu/pearsall/classes/fall2024/466/main.html

## Slide 2
Data Forwarding
Packet Switching
Uses store-and-forward transmission
Time to transmit L bits over a link with transmission rate of R:
L / R

## Slide 3
Data Forwarding
Packet Switching
Uses store-and-forward transmission
Time to transmit L bits over a link with transmission rate of R:
L / R
We have many forms of delay though…

## Slide 4
Network Delay
Processing delay- time required to examine the packet’s header and determine where to direct the packet
Queueing Delay- Time the packet sits in the queue
Transmission delay- Amount of time required to push all the packet’s bits into the link
Propagation Delay- time needed to propagate to destination
(dependent on the medium)
Nodal Delay = Processing delay + Queueing delay + Transmission delay + Propagation delay

## Slide 5
Network Delay
Processing delay- time required to examine the packet’s header and determine where to direct the packet
Queueing Delay- Time the packet sits in the queue
Transmission delay- Amount of time required to push all the packet’s bits into the link
Propagation Delay- time needed to propagate to destination
(dependent on the medium)
Nodal Delay = Processing delay + Queueing delay + Transmission delay + Propagation delay
https://www2.tkn.tu-berlin.de/teaching/rn/animations/propagation/

## Slide 6
Network Delay
Transmission delay- Amount of time required to push all the packet’s bits into the link
Transmission Delay = L / R
L = length of packet (bits) R = transmission rate of link

## Slide 7
Network Delay
Propagation = d / s
d = distance between host and router s = propagation speed of medium
Propagation Delay- time needed to propagate to destination
(dependent on the medium)

## Slide 8
Network Delay Example Problem
Link 1
Link 2
Transmission Rate: 1000 Mbps
Link Length: 3 Km
Transmission Rate: 100 Mbps
Link Length: 1 Km
Length of Packet = 12000 bits. Propagation Speed of links = 3 * 10^8 m/s
Transmission Delay = L / R
Propogation Delay = d / s
What is the transmission delay of link 1?

## Slide 9
Network Delay Example Problem
Link 1
Link 2
Transmission Rate: 1000 Mbps
Link Length: 3 Km
Transmission Rate: 100 Mbps
Link Length: 1 Km
Length of Packet = 12000 bits. Propagation Speed of links = 3 * 10^8 m/s
Transmission Delay = L / R
Propogation Delay = d / s
What is the transmission delay of link 1?
Dtransmission = L / R

## Slide 10
Network Delay Example Problem
Link 1
Link 2
Transmission Rate: 1000 Mbps
Link Length: 3 Km
Transmission Rate: 100 Mbps
Link Length: 1 Km
Length of Packet = 12000 bits. Propagation Speed of links = 3 * 10^8 m/s
Transmission Delay = L / R
Propogation Delay = d / s
What is the transmission delay of link 1?
Dtransmission = L / R
Dtransmission = 12000 / (1000 * 100000)
Must convert Mbps to bps!

## Slide 11
Network Delay Example Problem
Link 1
Link 2
Transmission Rate: 1000 Mbps
Link Length: 3 Km
Transmission Rate: 100 Mbps
Link Length: 1 Km
Length of Packet = 12000 bits. Propagation Speed of links = 3 * 10^8 m/s
Transmission Delay = L / R
Propogation Delay = d / s
What is the transmission delay of link 1?
Dtransmission = L / R
Dtransmission = 12000 / (1000 * 1000000)
Dtransmission = 12000 / 1000000000

## Slide 12
Network Delay Example Problem
Link 1
Link 2
Transmission Rate: 1000 Mbps
Link Length: 3 Km
Transmission Rate: 100 Mbps
Link Length: 1 Km
Length of Packet = 12000 bits. Propagation Speed of links = 3 * 10^8 m/s
Transmission Delay = L / R
Propogation Delay = d / s
What is the transmission delay of link 1?
Dtransmission = L / R
Dtransmission = 12000 / (1000 * 1000000)
Dtransmission = 12000 / 1000000000
Dtransmission = 0.000012 seconds

## Slide 13
Network Delay Example Problem
Link 1
Link 2
Transmission Rate: 1000 Mbps
Link Length: 3 Km
Transmission Rate: 100 Mbps
Link Length: 1 Km
Length of Packet = 12000 bits. Propagation Speed of links = 3 * 10^8 m/s
Transmission Delay = L / R
Propogation Delay = d / s
What is the transmission delay of link 1?
Dtransmission = L / R
Dtransmission = 12000 / (1000 * 1000000)
Dtransmission = 12000 / 1000000000
Dtransmission = 0.000012 seconds
What is the Propagation delay of link 1?

## Slide 14
Network Delay Example Problem
Link 1
Link 2
Transmission Rate: 1000 Mbps
Link Length: 3 Km
Transmission Rate: 100 Mbps
Link Length: 1 Km
Length of Packet = 12000 bits. Propagation Speed of links = 3 * 10^8 m/s
Transmission Delay = L / R
Propogation Delay = d / s
What is the transmission delay of link 1?
Dtransmission = L / R
Dtransmission = 12000 / (1000 * 1000000)
Dtransmission = 12000 / 1000000000
Dtransmission = 0.000012 seconds
What is the Propagation delay of link 1?
Dpropagation = d / s

## Slide 15
Network Delay Example Problem
Link 1
Link 2
Transmission Rate: 1000 Mbps
Link Length: 3 Km
Transmission Rate: 100 Mbps
Link Length: 1 Km
Length of Packet = 12000 bits. Propagation Speed of links = 3 * 10^8 m/s
Transmission Delay = L / R
Propogation Delay = d / s
What is the transmission delay of link 1?
Dtransmission = L / R
Dtransmission = 12000 / (1000 * 1000000)
Dtransmission = 12000 / 1000000000
Dtransmission = 0.000012 seconds
What is the Propagation delay of link 1?
Dpropagation = d / s
Dpropagation = (3 * 1000) / 3 * 10^8
Must convert Km to m!

## Slide 16
Network Delay Example Problem
Link 1
Link 2
Transmission Rate: 1000 Mbps
Link Length: 3 Km
Transmission Rate: 100 Mbps
Link Length: 1 Km
Length of Packet = 12000 bits. Propagation Speed of links = 3 * 10^8 m/s
Transmission Delay = L / R
Propogation Delay = d / s
What is the transmission delay of link 1?
Dtransmission = L / R
Dtransmission = 12000 / (1000 * 1000000)
Dtransmission = 12000 / 1000000000
Dtransmission = 0.000012 seconds
What is the Propagation delay of link 1?
Dpropagation = d / s
Dpropagation = (3 * 1000) / 3 * 10^8
Dpropagation = (3000) / 3 * 10^8

## Slide 17
Network Delay Example Problem
Link 1
Link 2
Transmission Rate: 1000 Mbps
Link Length: 3 Km
Transmission Rate: 100 Mbps
Link Length: 1 Km
Length of Packet = 12000 bits. Propagation Speed of links = 3 * 10^8 m/s
Transmission Delay = L / R
Propogation Delay = d / s
What is the transmission delay of link 1?
Dtransmission = L / R
Dtransmission = 12000 / (1000 * 1000000)
Dtransmission = 12000 / 1000000000
Dtransmission = 0.000012 seconds
What is the Propagation delay of link 1?
Dpropagation = d / s
Dpropagation = (3 * 1000) / 3 * 10^8
Dpropagation = (3000) / 3 * 10^8
Dpropagation = 0.00001

## Slide 18
Network Delay
Processing delay- time required to examine the packet’s header and determine where to direct the packet
Queueing Delay- Time the packet sits in the queue
Transmission delay- Amount of time required to push all the packet’s bits into the link
Propagation Delay- time needed to propagate to destination
(dependent on the medium)
In an uncongested network with N links between source and destination
End-to-end Delay= N(Processing delay + Transmission delay + Propagation delay)

## Slide 19
Queueing Delay
Packets arrive to the queue at a rate of a (packets/sec)
L bits per packet
Bits are pushed out on the communication link at a rate of R (bits/sec)

## Slide 20
Queueing Delay
Packets arrive to the queue at a rate of a (packets/sec)
L bits per packet
Bits are pushed out on the communication link at a rate of R (bits/sec)
Ratio of average bits that arrive at queue to how quick we can process one bit

## Slide 21
Queueing Delay
Packets arrive to the queue at a rate of a (packets/sec)
L bits per packet
Bits are pushed out on the communication link at a rate of R (bits/sec)
Ratio of average bits that arrive at queue to how quick we can process one bit
If traffic intensity > 1 ?

## Slide 22
Queueing Delay
Packets arrive to the queue at a rate of a (packets/sec)
L bits per packet
Bits are pushed out on the communication link at a rate of R (bits/sec)
Ratio of average bits that arrive at queue to how quick we can process one bit
If traffic intensity > 1 ?
Bits arrive to the queue faster than we can process them
Bad!

## Slide 23
Queueing Delay
Packets arrive to the queue at a rate of a (packets/sec)
L bits per packet
Bits are pushed out on the communication link at a rate of R (bits/sec)
Ratio of average bits that arrive at queue to how quick we can process one bit
If traffic intensity <= 1 ?
We can process bits faster than they arrive
Good!

## Slide 24
Packet Loss
Queues have finite space.
If a router has no place to store the packet, the packet will be dropped or lost
The number of lost packets will increase as traffic intensity increases
In addition to delay, the probability of packet loss is helpful to calculate

## Slide 25
Packet Loss
Queues have finite space.
If a router has no place to store the packet, the packet will be dropped or lost
The number of lost packets will increase as traffic intensity increases
In addition to delay, the probability of packet loss is helpful to calculate
Ping Test
ping –n 10 8.8.8.8
ping –n 5 131.255.7.26

## Slide 26
Throughput
Throughput is the amount of data transferred from one place to another within a given time period

## Slide 27
Throughput
Throughput is the amount of data transferred from one place to another within a given time period

## Slide 28: Throughput
Throughput is the amount of data transferred from one place to another within a given time period
Instantaneous throughput is the
throughput for a given point in time

## Slide 29: Throughput
Throughput is the amount of data transferred from one place to another within a given time period
Instantaneous throughput is the
throughput for a given point in time
The instantaneous throughput at 7:00 PM is roughly 6.5 Mbps

## Slide 30: Throughput
Throughput is the amount of data transferred from one place to another within a given time period
Instantaneous throughput is the
throughput for a given point in time
The instantaneous throughput at 7:00 PM is roughly 6.5 Mbps
In general, if F bits takes T seconds to transfer from one endpoint to another, the average throughput is:
𝐹
𝑇

## Slide 31: Throughput
Rs = transmission rate for server to router
Rc = transmission rate for client to router
Throughput for server to client?

## Slide 32: Throughput
Rs > Rc
Rs = transmission rate for server to router
Rc = transmission rate for client to router
Throughput for server to client?
Rs
Rc

## Slide 33: Throughput
Rs > Rc
Rs = transmission rate for server to router
Rc = transmission rate for client to router
Throughput for server to client?
Rs
Rc
Point in network where flow of data is impaired or stopped
Bottleneck

## Slide 34: Throughput
Rs = transmission rate for server to router
Rc = transmission rate for client to router
Throughput for server to client?
Rs > Rc
Rs
Rc
Point in network where flow of data is impaired or stopped
Bottleneck
Buildup

## Slide 35: Throughput
Rs = transmission rate for server to router
Rc = transmission rate for client to router
Rs > Rc
Rs
Rc
Point in network where flow of data is impaired or stopped
Bottleneck
Buildup
Throughput for server to client?
Dependent on the bottleneck link!

## Slide 36: Throughput
Rs = transmission rate for server to router
Rc = transmission rate for client to router
Rs > Rc
Rs
Rc
Point in network where flow of data is impaired or stopped
Bottleneck
Buildup
Throughput for server to client?
Dependent on the bottleneck link!
𝐹
min{Rs, Rc}

## Slide 37: Throughput
Rs = transmission rate for server to router
Rc = transmission rate for client to router
Time needed to transfer file?
Rc
Rs = 2 Mbps
= 1 Mbps
F = 32,000,000 bits

## Slide 38: Throughput
Rs = transmission rate for server to router
Rc = transmission rate for client to router
Time needed to transfer file?
Rc
Rs = 2 Mbps
= 1 Mbps
F = 32,000,000 bits = 32 Mb

## Slide 39: Throughput
Rs = transmission rate for server to router
Time needed to transfer file?
Rc
Rs = 2 Mbps
= 1 Mbps
F = 32,000,000 bits = 32 Mb
32 seconds
Dependent on the bottleneck
Rc = transmission rate for client to router

## Slide 40: Throughput

## Slide 41: Throughput
2
2
2
10
Link is shared across 10 servers
So each link supports 0.5 Mbps
1
1
1

## Slide 42: Throughput
2
2
2
10
Link is shared across 10 servers
So each link supports 0.5 Mbps
1
1
1
Sometimes, the bottleneck won’t be the link with the slowest transmission rate