## Slide 1: CSCI 466: Networks Network Layer – Routing (Control Plane)
Reese Pearsall Fall 2024
https://www.cs.montana.edu/pearsall/classes/fall2024/466/main.html
1
*All images are stolen from the internet

## Slide 2: Announcements
PA2 due on Sunday at 11:59 PM
Make sure everything is inside of a /PA2 folder in your repo
Everyone needs to submit video demo link to D2L
No class on Friday
Workday for PA2 (I’ll be in my office still if you need help)
ACM is hosting a guest speaker tonight at 5PM in Barnard Hall 347
Speaker has experience working at HP, Microsoft, Amazon
Great opportunity to learn about industry, careers, etc

## Slide 3
https://www.bozemandailychronicle.com/news/montana_state_university/exponent/kind-of-scary-montana-state-officials-confirm-learning-platform-tracks-student-locations/article_740f212e-859d-11ef-a536-771135b8a5d8.html

## Slide 4
Forwarding refers to moving packets from a router’s input to appropriate router output, and is implemented in the data plane.
Routing refers to determining the route taken by packets from source to destination, and is implemented in the control plane.
Ideally, this output links are the most optimal path to get to the destination
What is the best way to get from u to z?
Routing Metrics:
Shortest Path
Highest Throughput Path
Minimum Number of Hops
Lowest Congested Path

## Slide 5
Routing tables are filled via routing algorithms
There are two types of routing algorithms

## Slide 6
Routing tables are filled via routing algorithms
There are two types of routing algorithms
Centralized/Global- we know the edge costs of the network
Link State algorithms
(Dijkstra’s Algorithm)
We can compute the shortest path from one node, to all other nodes in polynomial time.
Once we know the shortest path from A to B, we can update routing tables to reflect that shortest path

## Slide 7: Shortest Path
0
1
2
3
4
5
6
7
0.35
0.35
0.37
0.1
0.28
0.22
0.38
0.26
0.39
0.29
0.34
0.52
0.93
0.58
0.4
7

## Slide 8: Shortest Path
0
1
2
3
4
5
6
7
0.35
0.35
0.37
0.1
0.28
0.22
0.38
0.26
0.39
0.29
0.34
0.52
0.93
0.58
0.4
8

## Slide 9: Shortest Path
0
1
2
3
4
5
6
7
0.35
0.35
0.37
0.1
0.28
0.22
0.38
0.26
0.39
0.29
0.34
0.52
0.93
0.58
0.4
What is the shortest path between vertex 0 and vertex 6?
Path with the smallest sum of edge weights.
9

## Slide 10: Shortest Path
0
1
2
3
4
5
6
7
0.35
0.35
0.37
0.1
0.28
0.22
0.38
0.26
0.39
0.29
0.34
0.52
0.93
0.58
0.4
We are going to find the shortest path between vertex 0 and every other vertex, flooding out from 0.
10

## Slide 11: Shortest Path
0
1
2
3
4
5
6
7
0.35
0.35
0.37
0.1
0.28
0.22
0.38
0.26
0.39
0.29
0.34
0.52
0.93
0.58
0.4
Distance from 0
0 | ?
1 | ?
2 | ?
3 | ?
4 | ?
5 | ?
6 | ?
7 | ?
11

## Slide 12: Shortest Path
0
1
2
3
4
5
6
7
0.35
0.35
0.37
0.1
0.28
0.22
0.38
0.26
0.39
0.29
0.34
0.52
0.93
0.58
0.4
Distance from 0
How can we keep track of routes?
0 | 0
1 | ∞
2 | ∞
3 | ∞
4 | ∞
5 | ∞
6 | ∞
7 | ∞
12

## Slide 13: Shortest Path
0
1
2
3
4
5
6
7
0.35
0.35
0.37
0.1
0.28
0.22
0.38
0.26
0.39
0.29
0.34
0.52
0.93
0.58
0.4
Distance from 0
0 | -
1 | 
2 | 
3 | 
4 | 
5 | 
6 | 
7 | 
Previous vertex
How can we keep track of routes?
0 | 0
1 | ∞
2 | ∞
3 | ∞
4 | ∞
5 | ∞
6 | ∞
7 | ∞
13

## Slide 14: Shortest Path
0
1
2
3
4
5
6
7
0.35
0.35
0.37
0.1
0.28
0.22
0.38
0.26
0.39
0.29
0.34
0.52
0.93
0.58
0.4
Distance from 0
0 | -
1 | 
2 | 0
3 | 7
4 | 
5 | 
6 | 3
7 | 2
Previous vertex
How can we keep track of routes?
0 | 0
1 | ∞
2 | 0.26
3 | 0.99
4 | ∞
5 | ∞
6 | 1.51
7 | 0.60
14

## Slide 15: Shortest Path
0
1
2
3
4
5
6
7
0.35
0.35
0.37
0.1
0.28
0.22
0.38
0.26
0.39
0.29
0.34
0.52
0.93
0.58
0.4
Distance from 0
0 | -
1 | 
2 | 0
3 | 7
4 | 
5 | 
6 | 3
7 | 2
Previous vertex
If this is the shortest path from 0 to 6, what can we say about the shortest path from 0 to 3?
0 | 0
1 | ∞
2 | ∞
3 | ∞
4 | ∞
5 | ∞
6 | ∞
7 | ∞
15

## Slide 16: Shortest Path
0
1
2
3
4
5
6
7
0.35
0.35
0.37
0.1
0.28
0.22
0.38
0.26
0.39
0.29
0.34
0.52
0.93
0.58
0.4
Distance from 0
0 | -
1 | 
2 | 
3 | 
4 | 
5 | 
6 | 
7 | 
Previous vertex
0 | 0
1 | ∞
2 | ∞
3 | ∞
4 | ∞
5 | ∞
6 | ∞
7 | ∞
What can we reach from connected vertices and at what distance (from 0)?
Priority queue
16
vertex (distance)

## Slide 17: Shortest Path
0
1
2
3
4
5
6
7
0.35
0.35
0.37
0.1
0.28
0.22
0.38
0.26
0.39
0.29
0.34
0.52
0.93
0.58
0.4
Distance from 0
0 | -
1 | 
2 | 
3 | 
4 | 
5 | 
6 | 
7 | 
Previous vertex
0 | 0
1 | ∞
2 | ∞
3 | ∞
4 | ∞
5 | ∞
6 | ∞
7 | ∞
What can we reach from connected vertices and at what distance (from 0)?
Priority queue
2 (0.26)
4 (0.38)
17
vertex (distance)

## Slide 18: Shortest Path
0
1
2
3
4
5
6
7
0.35
0.35
0.37
0.1
0.28
0.22
0.38
0.26
0.39
0.29
0.34
0.52
0.93
0.58
0.4
Distance from 0
0 | -
1 | 
2 | 0
3 | 
4 | 0
5 | 
6 | 
7 | 
Previous vertex
0 | 0
1 | ∞
2 | ∞
3 | ∞
4 | ∞
5 | ∞
6 | ∞
7 | ∞
What can we reach from connected vertices and at what distance (from 0)?
Priority queue
2 (0.26)
4 (0.38)
18
vertex (distance)

## Slide 19: Shortest Path
0
1
2
3
4
5
6
7
0.35
0.35
0.37
0.1
0.28
0.22
0.38
0.26
0.39
0.29
0.34
0.52
0.93
0.58
0.4
Distance from 0
0 | -
1 | 
2 | 0
3 | 
4 | 0
5 | 
6 | 
7 | 
Previous vertex
0 | 0
1 | ∞
2 | 0.26
3 | ∞
4 | 0.38
5 | ∞
6 | ∞
7 | ∞
What can we reach from connected vertices and at what distance (from 0)?
Priority queue
2 (0.26)
4 (0.38)
19
vertex (distance)

## Slide 20: Shortest Path
0
1
2
3
4
5
6
7
0.35
0.35
0.37
0.1
0.28
0.22
0.38
0.26
0.39
0.29
0.34
0.52
0.93
0.58
0.4
Distance from 0
0 | -
1 | 
2 | 0
3 | 
4 | 0
5 | 
6 | 
7 | 
Previous vertex
0 | 0
1 | ∞
2 | 0.26
3 | ∞
4 | 0.38
5 | ∞
6 | ∞
7 | ∞
What can we reach from connected vertices and at what distance (from 0)?
Priority queue
4 (0.38)
queue
top
= 2 (0.26)
20
vertex (distance)

## Slide 21: Shortest Path
0
1
2
3
4
5
6
7
0.35
0.35
0.37
0.1
0.28
0.22
0.38
0.26
0.39
0.29
0.34
0.52
0.93
0.58
0.4
Distance from 0
0 | -
1 | 
2 | 0
3 | 
4 | 0
5 | 
6 | 
7 | 
Previous vertex
0 | 0
1 | ∞
2 | 0.26
3 | ∞
4 | 0.38
5 | ∞
6 | ∞
7 | ∞
Priority queue
4 (0.38)
What can we reach from connected vertices and at what distance (from 0)?
queue
top
= 2 (0.26)
21
vertex (distance)

## Slide 22: Shortest Path
0
1
2
3
4
5
6
7
0.35
0.35
0.37
0.1
0.28
0.22
0.38
0.26
0.39
0.29
0.34
0.52
0.93
0.58
0.4
Distance from 0
0 | -
1 | 
2 | 0
3 | 
4 | 0
5 | 
6 | 
7 | 2
Previous vertex
0 | 0
1 | ∞
2 | 0.26
3 | ∞
4 | 0.38
5 | ∞
6 | ∞
7 | 0.60
Priority queue
4 (0.38)
7 (0.60)
What can we reach from connected vertices and at what distance (from 0)?
queue
top
= 2 (0.26)
22
vertex (distance)

## Slide 23: Shortest Path
0
1
2
3
4
5
6
7
0.35
0.35
0.37
0.1
0.28
0.22
0.38
0.26
0.39
0.29
0.34
0.52
0.93
0.58
0.4
Distance from 0
0 | -
1 | 
2 | 0
3 | 
4 | 0
5 | 
6 | 
7 | 2
Previous vertex
Priority queue
7 (0.60)
Repeat.
queue
top
= 4 (0.38)
0 | 0
1 | ∞
2 | 0.26
3 | ∞
4 | 0.38
5 | ∞
6 | ∞
7 | 0.60
23
vertex (distance)

## Slide 24: Shortest Path
Distance from 0
0 | -
1 | 
2 | 0
3 | 
4 | 0
5 | 
6 | 
7 | 2
Previous vertex
Priority queue
7 (0.60)
Add neighbors to queue/previous.
queue
top
= 4 (0.38)
0
1
2
3
4
5
6
7
0.35
0.35
0.37
0.1
0.28
0.22
0.38
0.26
0.39
0.29
0.34
0.52
0.93
0.58
0.4
0 | 0
1 | ∞
2 | 0.26
3 | ∞
4 | 0.38
5 | ∞
6 | ∞
7 | 0.60
24
vertex (distance)

## Slide 25: Shortest Path
Distance from 0
0 | -
1 | 
2 | 0
3 | 
4 | 0
5 | 4
6 | 
7 | 2
Previous vertex
Priority queue
7 (0.60)
5 (0.73)
Add neighbors to queue/previous.
queue
top
= 4 (0.38)
0
1
2
3
4
5
6
7
0.35
0.35
0.37
0.1
0.28
0.22
0.38
0.26
0.39
0.29
0.34
0.52
0.93
0.58
0.4
0 | 0
1 | ∞
2 | 0.26
3 | ∞
4 | 0.38
5 | 0.73
6 | ∞
7 | 0.60
25
vertex (distance)

## Slide 26: Shortest Path
Distance from 0
0 | -
1 | 
2 | 0
3 | 
4 | 0
5 | 4
6 | 
7 | 2
Previous vertex
Priority queue
7 (0.60)
5 (0.73)
Add neighbors to queue/previous.
We have another route to 7!
queue
top
= 4 (0.38)
0
1
2
3
4
5
6
7
0.35
0.35
0.37
0.1
0.28
0.22
0.38
0.26
0.39
0.29
0.34
0.52
0.93
0.58
0.4
0 | 0
1 | ∞
2 | 0.26
3 | ∞
4 | 0.38
5 | 0.73
6 | ∞
7 | 0.60
26
vertex (distance)

## Slide 27: Shortest Path
Distance from 0
0 | -
1 | 
2 | 0
3 | 
4 | 0
5 | 4
6 | 
7 | 2
Previous vertex
Priority queue
7 (0.60)
5 (0.73)
Add neighbors to queue/previous.
We have another route to 7! Check to see if it is shorter!
queue
top
= 4 (0.38)
0
1
2
3
4
5
6
7
0.35
0.35
0.37
0.1
0.28
0.22
0.38
0.26
0.39
0.29
0.34
0.52
0.93
0.58
0.4
0 | 0
1 | ∞
2 | 0.26
3 | ∞
4 | 0.38
5 | 0.73
6 | ∞
7 | 0.60
27
vertex (distance)

## Slide 28: Shortest Path
Distance from 0
0 | -
1 | 
2 | 0
3 | 
4 | 0
5 | 4
6 | 
7 | 2
Previous vertex
Priority queue
7 (0.60)
5 (0.73)
Add neighbors to queue/previous.
We have another route to 7! Check to see if it is shorter! It’s not (0.38 + 0.37 = 0.75 > 0.60).
queue
top
= 4 (0.38)
0
1
2
3
4
5
6
7
0.35
0.35
0.37
0.1
0.28
0.22
0.38
0.26
0.39
0.29
0.34
0.52
0.93
0.58
0.4
0 | 0
1 | ∞
2 | 0.26
3 | ∞
4 | 0.38
5 | 0.73
6 | ∞
7 | 0.60
28
vertex (distance)

## Slide 29: Shortest Path
Distance from 0
0 | -
1 | 
2 | 0
3 | 
4 | 0
5 | 4
6 | 
7 | 2
Previous vertex
Priority queue
7 (0.60)
5 (0.73)
Rule: When processing vertex v, only add/modify queue for neighbor u if and only if:
distance[v] + weight(v, u) < distance[u]
queue
top
= 4 (0.38)
0
1
2
3
4
5
6
7
0.35
0.35
0.37
0.1
0.28
0.22
0.38
0.26
0.39
0.29
0.34
0.52
0.93
0.58
0.4
0 | 0
1 | ∞
2 | 0.26
3 | ∞
4 | 0.38
5 | 0.73
6 | ∞
7 | 0.60
29
vertex (distance)

## Slide 30: Shortest Path
Distance from 0
0 | -
1 | 
2 | 0
3 | 
4 | 0
5 | 4
6 | 
7 | 2
Previous vertex
Priority queue
7 (0.60)
5 (0.73)
Repeat.
queue
top
=
0
1
2
3
4
5
6
7
0.35
0.35
0.37
0.1
0.28
0.22
0.38
0.26
0.39
0.29
0.34
0.52
0.93
0.58
0.4
0 | 0
1 | ∞
2 | 0.26
3 | ∞
4 | 0.38
5 | 0.73
6 | ∞
7 | 0.60
30
vertex (distance)

## Slide 31: Shortest Path
Distance from 0
0 | -
1 | 
2 | 0
3 | 7
4 | 0
5 | 4
6 | 
7 | 2
Previous vertex
Priority queue
5 (0.73)
3 (0.99)
Repeat.
queue
top
= 7 (0.60)
0
1
2
3
4
5
6
7
0.35
0.35
0.37
0.1
0.28
0.22
0.38
0.26
0.39
0.29
0.34
0.52
0.93
0.58
0.4
0 | 0
1 | ∞
2 | 0.26
3 | 0.99
4 | 0.38
5 | 0.73
6 | ∞
7 | 0.60
31
vertex (distance)

## Slide 32: Shortest Path
Distance from 0
0 | -
1 | 
2 | 0
3 | 7
4 | 0
5 | 4
6 | 
7 | 2
Previous vertex
Priority queue
5 (0.73)
3 (0.99)
Repeat.
We have another route to 5, and at cost 0.7 < 0.73.
queue
top
= 7 (0.60)
0
1
2
3
4
5
6
7
0.35
0.35
0.37
0.1
0.28
0.22
0.38
0.26
0.39
0.29
0.34
0.52
0.93
0.58
0.4
0 | 0
1 | ∞
2 | 0.26
3 | 0.99
4 | 0.38
5 | 0.73
6 | ∞
7 | 0.60
32
vertex (distance)

## Slide 33: Shortest Path
Distance from 0
0 | -
1 | 
2 | 0
3 | 7
4 | 0
5 | 4
6 | 
7 | 2
Previous vertex
Priority queue
5 (0.73)
3 (0.99)
Repeat. We have another route to 5, and at cost 0.7 < 0.73.
i.e., distance[v] + weight(v, u) < distance[u]
queue
top
= 7 (0.60)
0
1
2
3
4
5
6
7
0.35
0.35
0.37
0.1
0.28
0.22
0.38
0.26
0.39
0.29
0.34
0.52
0.93
0.58
0.4
0 | 0
1 | ∞
2 | 0.26
3 | 0.99
4 | 0.38
5 | 0.73
6 | ∞
7 | 0.60
33
vertex (distance)

## Slide 34: Shortest Path
Distance from 0
0 | -
1 | 
2 | 0
3 | 7
4 | 0
5 | 4
6 | 
7 | 2
Previous vertex
Priority queue
5 (0.73)
3 (0.99)
Repeat. We have another route to 5, and at cost 0.7 < 0.73.
So updated queue/previous/distance.
queue
top
= 7 (0.60)
0
1
2
3
4
5
6
7
0.35
0.35
0.37
0.1
0.28
0.22
0.38
0.26
0.39
0.29
0.34
0.52
0.93
0.58
0.4
0.70
7
0 | 0
1 | ∞
2 | 0.26
3 | 0.99
4 | 0.38
5 | 0.73
6 | ∞
7 | 0.60
0.70
34
vertex (distance)

## Slide 35: Shortest Path
Distance from 0
0 | -
1 | 
2 | 0
3 | 7
4 | 0
5 | 7
6 | 
7 | 2
Previous vertex
Priority queue
5 (0.70)
3 (0.99)
Repeat. We have another route to 5, and at cost 0.7 < 0.73.
So updated queue/previous/distance.
queue
top
= 7 (0.60)
0
1
2
3
4
5
6
7
0.35
0.35
0.37
0.1
0.28
0.22
0.38
0.26
0.39
0.29
0.34
0.52
0.93
0.58
0.4
0 | 0
1 | ∞
2 | 0.26
3 | 0.99
4 | 0.38
5 | 0.70
6 | ∞
7 | 0.60
35
vertex (distance)

## Slide 36: Shortest Path
Distance from 0
0 | -
1 | 
2 | 0
3 | 7
4 | 0
5 | 7
6 | 
7 | 2
Previous vertex
Priority queue
5 (0.70)
3 (0.99)
Repeat.
queue
top
= 7 (0.60)
0
1
2
3
4
5
6
7
0.35
0.35
0.37
0.1
0.28
0.22
0.38
0.26
0.39
0.29
0.34
0.52
0.93
0.58
0.4
0 | 0
1 | ∞
2 | 0.26
3 | 0.99
4 | 0.38
5 | 0.70
6 | ∞
7 | 0.60
36
vertex (distance)

## Slide 37: Shortest Path
Distance from 0
0 | -
1 | 
2 | 0
3 | 7
4 | 0
5 | 7
6 | 
7 | 2
Previous vertex
Priority queue
3 (0.99)
Repeat.
queue
top
= 5 (0.70)
0
1
2
3
4
5
6
7
0.35
0.35
0.37
0.1
0.28
0.22
0.38
0.26
0.39
0.29
0.34
0.52
0.93
0.58
0.4
0 | 0
1 | ∞
2 | 0.26
3 | 0.99
4 | 0.38
5 | 0.70
6 | ∞
7 | 0.60
37
vertex (distance)

## Slide 38: Shortest Path
Distance from 0
0 | -
1 | 
2 | 0
3 | 7
4 | 0
5 | 7
6 | 
7 | 2
Previous vertex
Priority queue
3 (0.99)
Repeat.
queue
top
= 5 (0.70)
0
1
2
3
4
5
6
7
0.35
0.35
0.37
0.1
0.28
0.22
0.38
0.26
0.39
0.29
0.34
0.52
0.93
0.58
0.4
0 | 0
1 | ∞
2 | 0.26
3 | 0.99
4 | 0.38
5 | 0.70
6 | ∞
7 | 0.60
38
vertex (distance)

## Slide 39: Shortest Path
Distance from 0
0 | -
1 | 5
2 | 0
3 | 7
4 | 0
5 | 7
6 | 
7 | 2
Previous vertex
Priority queue
1 (0.92)
3 (0.99)
Repeat.
queue
top
= 5 (0.70)
0
1
2
3
4
5
6
7
0.35
0.35
0.37
0.1
0.28
0.22
0.38
0.26
0.39
0.29
0.34
0.52
0.93
0.58
0.4
0 | 0
1 | 0.92
2 | 0.26
3 | 0.99
4 | 0.38
5 | 0.70
6 | ∞
7 | 0.60
39
vertex (distance)

## Slide 40: Shortest Path
Distance from 0
0 | -
1 | 5
2 | 0
3 | 7
4 | 0
5 | 7
6 | 
7 | 2
Previous vertex
Priority queue
1 (0.92)
3 (0.99)
Repeat.
What about neighbor 4?
queue
top
= 5 (0.70)
0
1
2
3
4
5
6
7
0.35
0.35
0.37
0.1
0.28
0.22
0.38
0.26
0.39
0.29
0.34
0.52
0.93
0.58
0.4
0 | 0
1 | 0.92
2 | 0.26
3 | 0.99
4 | 0.38
5 | 0.70
6 | ∞
7 | 0.60
40
vertex (distance)

## Slide 41: Shortest Path
Distance from 0
0 | -
1 | 5
2 | 0
3 | 7
4 | 0
5 | 7
6 | 
7 | 2
Previous vertex
Priority queue
1 (0.92)
3 (0.99)
Repeat.
What about neighbor 4?distance[5] + weight(5, 4) = 0.70 + 0.35 = 1.05 0.38 = distance[4]
queue
top
= 5 (0.70)
0
1
2
3
4
5
6
7
0.35
0.35
0.37
0.1
0.28
0.22
0.38
0.26
0.39
0.29
0.34
0.52
0.93
0.58
0.4
0 | 0
1 | 0.92
2 | 0.26
3 | 0.99
4 | 0.38
5 | 0.70
6 | ∞
7 | 0.60
41
vertex (distance)

## Slide 42: Shortest Path
Distance from 0
0 | -
1 | 5
2 | 0
3 | 7
4 | 0
5 | 7
6 | 
7 | 2
Previous vertex
Priority queue
1 (0.92)
3 (0.99)
Repeat. What about neighbor 7?
distance[5] + weight(5, 7) = 0.70 + 0.28 = 0.98 0.60 = distance[7]
queue
top
= 5 (0.70)
0
1
2
3
4
5
6
7
0.35
0.35
0.37
0.1
0.28
0.22
0.38
0.26
0.39
0.29
0.34
0.52
0.93
0.58
0.4
0 | 0
1 | 0.92
2 | 0.26
3 | 0.99
4 | 0.38
5 | 0.70
6 | ∞
7 | 0.60
vertex (distance)

## Slide 43: Shortest Path
Distance from 0
0 | -
1 | 5
2 | 0
3 | 7
4 | 0
5 | 7
6 | 
7 | 2
Previous vertex
Priority queue
3 (0.99)
Repeat.
queue
top
= 1 (0.92)
0
1
2
3
4
5
6
7
0.35
0.35
0.37
0.1
0.28
0.22
0.38
0.26
0.39
0.29
0.34
0.52
0.93
0.58
0.4
0 | 0
1 | 0.92
2 | 0.26
3 | 0.99
4 | 0.38
5 | 0.70
6 | ∞
7 | 0.60
43
vertex (distance)

## Slide 44: Shortest Path
Distance from 0
0 | -
1 | 5
2 | 0
3 | 7
4 | 0
5 | 7
6 | 
7 | 2
Previous vertex
Priority queue
3 (0.99)
Repeat.
What about neighbor 3? 0.92 + 0.29 = 1.21 > 0.99
queue
top
= 1 (0.92)
0
1
2
3
4
5
6
7
0.35
0.35
0.37
0.1
0.28
0.22
0.38
0.26
0.39
0.29
0.34
0.52
0.93
0.58
0.4
0 | 0
1 | 0.92
2 | 0.26
3 | 0.99
4 | 0.38
5 | 0.70
6 | ∞
7 | 0.60
44
vertex (distance)

## Slide 45: Shortest Path
Distance from 0
0 | -
1 | 5
2 | 0
3 | 7
4 | 0
5 | 7
6 | 
7 | 2
Previous vertex
Priority queue
Repeat.
queue
top
= 3 (0.99)
0
1
2
3
4
5
6
7
0.35
0.35
0.37
0.1
0.28
0.22
0.38
0.26
0.39
0.29
0.34
0.52
0.93
0.58
0.4
0 | 0
1 | 0.92
2 | 0.26
3 | 0.99
4 | 0.38
5 | 0.70
6 | ∞
7 | 0.60
45
vertex (distance)

## Slide 46: Shortest Path
Distance from 0
0 | -
1 | 5
2 | 0
3 | 7
4 | 0
5 | 7
6 | 3
7 | 2
Previous vertex
Priority queue
Repeat.
queue
top
= 3 (0.99)
0
1
2
3
4
5
6
7
0.35
0.35
0.37
0.1
0.28
0.22
0.38
0.26
0.39
0.29
0.34
0.52
0.93
0.58
0.4
6 (1.51)
0 | 0
1 | 0.92
2 | 0.26
3 | 0.99
4 | 0.38
5 | 0.70
6 | 1.51
7 | 0.60
46
vertex (distance)

## Slide 47: Shortest Path
Distance from 0
0 | -
1 | 5
2 | 0
3 | 7
4 | 0
5 | 7
6 | 3
7 | 2
Previous vertex
0 | 0
1 | 0.92
2 | 0.26
3 | 0.99
4 | 0.38
5 | 0.70
6 | 1.51
7 | 0.60
Priority queue
Repeat.
queue
top
= 6 (1.51)
0
1
2
3
4
5
6
7
0.35
0.35
0.37
0.1
0.28
0.22
0.38
0.26
0.39
0.29
0.34
0.52
0.93
0.58
0.4
47
vertex (distance)

## Slide 48: Shortest Path
Distance from 0
0 | -
1 | 5
2 | 0
3 | 7
4 | 0
5 | 7
6 | 3
7 | 2
Previous vertex
0 | 0
1 | 0.92
2 | 0.26
3 | 0.99
4 | 0.38
5 | 0.70
6 | 1.51
7 | 0.60
Priority queue
Repeat?
queue
top
= 6 (1.51)
0
1
2
3
4
5
6
7
0.35
0.35
0.37
0.1
0.28
0.22
0.38
0.26
0.39
0.29
0.34
0.52
0.93
0.58
0.4
48
vertex (distance)

## Slide 49: Shortest Path
Distance from 0
0 | -
1 | 5
2 | 0
3 | 7
4 | 0
5 | 7
6 | 3
7 | 2
Previous vertex
0 | 0
1 | 0.92
2 | 0.26
3 | 0.99
4 | 0.38
5 | 0.70
6 | 1.51
7 | 0.60
Priority queue
Repeat?
Neighbor 4? 1.51 + 0.93 > 0.38
queue
top
= 6 (1.51)
0
1
2
3
4
5
6
7
0.35
0.35
0.37
0.1
0.28
0.22
0.38
0.26
0.39
0.29
0.34
0.52
0.93
0.58
0.4
49
vertex (distance)

## Slide 50: Shortest Path
Distance from 0
0 | -
1 | 5
2 | 0
3 | 7
4 | 0
5 | 7
6 | 3
7 | 2
Previous vertex
0 | 0
1 | 0.92
2 | 0.26
3 | 0.99
4 | 0.38
5 | 0.70
6 | 1.51
7 | 0.60
Priority queue
Repeat?
Neighbor 0? 1.51 + 0.58 > 0
queue
top
= 6 (1.51)
0
1
2
3
4
5
6
7
0.35
0.35
0.37
0.1
0.28
0.22
0.38
0.26
0.39
0.29
0.34
0.52
0.93
0.58
0.4
50
vertex (distance)

## Slide 51: Shortest Path
Distance from 0
0 | -
1 | 5
2 | 0
3 | 7
4 | 0
5 | 7
6 | 3
7 | 2
Previous vertex
0 | 0
1 | 0.92
2 | 0.26
3 | 0.99
4 | 0.38
5 | 0.70
6 | 1.51
7 | 0.60
Priority queue
Repeat?
Neighbor 2? 1.51 + 0.4 > 0.26
queue
top
= 6 (1.51)
0
1
2
3
4
5
6
7
0.35
0.35
0.37
0.1
0.28
0.22
0.38
0.26
0.39
0.29
0.34
0.52
0.93
0.58
0.4
51
vertex (distance)

## Slide 52: Shortest Path
Distance from 0
0 | -
1 | 5
2 | 0
3 | 7
4 | 0
5 | 7
6 | 3
7 | 2
Previous vertex
0 | 0
1 | 0.92
2 | 0.26
3 | 0.99
4 | 0.38
5 | 0.70
6 | 1.51
7 | 0.60
Priority queue
When are we done?
queue
top
= 6 (1.51)
0
1
2
3
4
5
6
7
0.35
0.35
0.37
0.1
0.28
0.22
0.38
0.26
0.39
0.29
0.34
0.52
0.93
0.58
0.4
52
vertex (distance)

## Slide 53: Shortest Path
Distance from 0
0 | -
1 | 5
2 | 0
3 | 7
4 | 0
5 | 7
6 | 3
7 | 2
Previous vertex
0 | 0
1 | 0.92
2 | 0.26
3 | 0.99
4 | 0.38
5 | 0.70
6 | 1.51
7 | 0.60
Priority queue
When are we done?
When the queue is empty!
queue
top
= 6 (1.51)
0
1
2
3
4
5
6
7
0.35
0.35
0.37
0.1
0.28
0.22
0.38
0.26
0.39
0.29
0.34
0.52
0.93
0.58
0.4
53
vertex (distance)

## Slide 54
Routing tables are filled via routing algorithms
There are two types of routing algorithms
Centralized/Global- we know the edge costs of the network
Link State algorithms
(Dijkstra’s Algorithm)
We can compute the shortest path from one node, to all other nodes in polynomial time.
Once we know the shortest path from A to B, we can update routing tables to reflect that shortest path

## Slide 55
Routing tables are filled via routing algorithms
There are two types of routing algorithms
Decentralized- we do not know the edge costs of the entire network.
Only know edge costs to neighbors
Distance Vector algorithms

## Slide 56
Routing tables are filled via routing algorithms
There are two types of routing algorithms
Based on Bellman-Ford (BF) equation (dynamic programming):
Let Dx(y): cost of least-cost path from x to y.
Then:
Dx(y) = minv { cx,v + Dv(y) }
Bellman-Ford equation
min taken over all neighbors v of x
v’s estimated least-cost-path cost to y
direct cost of link from x to v

## Slide 57
 |  |  | Cost | to
 |  | X | Y | Z
Cost | X | 0 | 2 | 7
From | Y |  |  | 
 | Z |  |  | 
 |  |  | Cost | to
 |  | X | Y | Z
Cost | X |  |  | 
From | Y | 2 | 0 | 1
 | Z |  |  | 
 |  |  | Cost | to
 |  | X | Y | Z
Cost | X |  |  | 
From | Y |  |  | 
 | Z | 7 | 1 | 0

## Slide 58
 |  |  | Cost | to
 |  | X | Y | Z
Cost | X | 0 | 2 | 7
From | Y |  |  | 
 | Z |  |  | 
 |  |  | Cost | to
 |  | X | Y | Z
Cost | X |  |  | 
From | Y | 2 | 0 | 1
 | Z |  |  | 
 |  |  | Cost | to
 |  | X | Y | Z
Cost | X |  |  | 
From | Y |  |  | 
 | Z | 7 | 1 | 0
 |  |  | Cost | to
 |  | X | Y | Z
Cost | X | 0 | 2 | 3
From | Y | 2 | 0 | 1
 | Z | 7 | 1 | 0
X learns that Y can reach Z with only a cost of 1
Meaning:
The cost to get to Y from X (2) plus the cost to get from Y to Z (1) is lower than my direct path to Y (7), so I have now learned a new shortest path!

## Slide 59
 |  |  | Cost | to
 |  | X | Y | Z
Cost | X | 0 | 2 | 7
From | Y |  |  | 
 | Z |  |  | 
 |  |  | Cost | to
 |  | X | Y | Z
Cost | X |  |  | 
From | Y | 2 | 0 | 1
 | Z |  |  | 
 |  |  | Cost | to
 |  | X | Y | Z
Cost | X |  |  | 
From | Y |  |  | 
 | Z | 7 | 1 | 0
 |  |  | Cost | to
 |  | X | Y | Z
Cost | X | 0 | 2 | 3
From | Y | 2 | 0 | 1
 | Z | 7 | 1 | 0
 |  |  | Cost | to
 |  | X | Y | Z
Cost | X | 0 | 2 | 7
From | Y | 2 | 0 | 1
 | Z | 7 | 1 | 0
 |  |  | Cost | to
 |  | X | Y | Z
Cost | X | 0 | 2 | 7
From | Y | 2 | 0 | 1
 | Z | 3 | 1 | 0

## Slide 60
 |  |  | Cost | to
 |  | X | Y | Z
Cost | X | 0 | 2 | 7
From | Y |  |  | 
 | Z |  |  | 
 |  |  | Cost | to
 |  | X | Y | Z
Cost | X |  |  | 
From | Y | 2 | 0 | 1
 | Z |  |  | 
 |  |  | Cost | to
 |  | X | Y | Z
Cost | X |  |  | 
From | Y |  |  | 
 | Z | 7 | 1 | 0
 |  |  | Cost | to
 |  | X | Y | Z
Cost | X | 0 | 2 | 3
From | Y | 2 | 0 | 1
 | Z | 7 | 1 | 0
 |  |  | Cost | to
 |  | X | Y | Z
Cost | X | 0 | 2 | 7
From | Y | 2 | 0 | 1
 | Z | 7 | 1 | 0
 |  |  | Cost | to
 |  | X | Y | Z
Cost | X | 0 | 2 | 7
From | Y | 2 | 0 | 1
 | Z | 3 | 1 | 0
 |  |  | Cost | to
 |  | X | Y | Z
Cost | X | 0 | 2 | 3
From | Y | 2 | 0 | 1
 | Z | 3 | 1 | 0
 |  |  | Cost | to
 |  | X | Y | Z
Cost | X | 0 | 2 | 3
From | Y | 2 | 0 | 1
 | Z | 3 | 1 | 0
 |  |  | Cost | to
 |  | X | Y | Z
Cost | X | 0 | 2 | 3
From | Y | 2 | 0 | 1
 | Z | 3 | 1 | 0

## Slide 61
 |  |  | Cost | to
 |  | X | Y | Z
Cost | X | 0 | 2 | 7
From | Y |  |  | 
 | Z |  |  | 
 |  |  | Cost | to
 |  | X | Y | Z
Cost | X |  |  | 
From | Y | 2 | 0 | 1
 | Z |  |  | 
 |  |  | Cost | to
 |  | X | Y | Z
Cost | X |  |  | 
From | Y |  |  | 
 | Z | 7 | 1 | 0
 |  |  | Cost | to
 |  | X | Y | Z
Cost | X | 0 | 2 | 3
From | Y | 2 | 0 | 1
 | Z | 7 | 1 | 0
 |  |  | Cost | to
 |  | X | Y | Z
Cost | X | 0 | 2 | 7
From | Y | 2 | 0 | 1
 | Z | 7 | 1 | 0
 |  |  | Cost | to
 |  | X | Y | Z
Cost | X | 0 | 2 | 7
From | Y | 2 | 0 | 1
 | Z | 3 | 1 | 0
 |  |  | Cost | to
 |  | X | Y | Z
Cost | X | 0 | 2 | 3
From | Y | 2 | 0 | 1
 | Z | 3 | 1 | 0
 |  |  | Cost | to
 |  | X | Y | Z
Cost | X | 0 | 2 | 3
From | Y | 2 | 0 | 1
 | Z | 3 | 1 | 0
 |  |  | Cost | to
 |  | X | Y | Z
Cost | X | 0 | 2 | 3
From | Y | 2 | 0 | 1
 | Z | 3 | 1 | 0
We can update our routing table and then make sure we forward packets to the correct destination in the path

## Slide 62
Routing tables are filled via routing algorithms
There are two types of routing algorithms
Centralized/Global- we know the edge costs of the network
Link State algorithms
(Dijkstra’s Algorithm)
Decentralized- we do not know the edge costs of the entire network.
Only know edge costs to neighbors
Distance Vector algorithms

## Slide 63: Distance vector algorithm:
iterative, asynchronous: each local iteration caused by:
local link cost change
DV update message from neighbor
wait for (change in local link cost or msg from neighbor)
each node:
distributed, self-stopping: each node notifies neighbors only when its DV changes
  neighbors then notify their neighbors – only if necessary
  no notification received, no actions taken!
recompute DV estimates using DV received from neighbor
if DV to any destination has changed, notify neighbors

## Slide 64: Distance vector: example
DV in a: Da(a)=0
Da(b) = 8
Da(c) = ∞
Da(d) = 1
Da(e) = ∞
Da(f) = ∞
Da(g) = ∞
Da(h) = ∞
Da(i) = ∞
g
h
i
1
1
1
1
1
1
1
1
1
8
1
t=0
All nodes have distance estimates to nearest neighbors (only)
A few asymmetries:
missing link
larger cost
d
e
f
a
b
c
All nodes send their local distance vector to their neighbors

## Slide 65: Distance vector example: iteration
All nodes:
receive distance vectors from neighbors
compute their new local distance vector
send their new local distance vector to neighbors
t=1
g
h
i
1
1
1
1
1
1
1
1
1
8
1
d
e
f
a
b
c

## Slide 66: Distance vector example: iteration
g
h
i
1
1
1
1
1
1
1
1
1
8
1
d
e
f
a
b
c
All nodes:
receive distance vectors from neighbors
compute their new local distance vector
send their new local distance vector to neighbors
t=1
compute
compute
compute
compute
compute
compute
compute
compute
compute

## Slide 67: Distance vector example: iteration
g
h
i
1
1
1
1
1
1
1
1
1
8
1
d
e
f
a
b
c
All nodes:
receive distance vectors from neighbors
compute their new local distance vector
send their new local distance vector to neighbors
t=1

## Slide 68: Distance vector example: iteration
g
h
i
1
1
1
1
1
1
1
1
1
8
1
d
e
f
a
b
c
All nodes:
receive distance vectors from neighbors
compute their new local distance vector
send their new local distance vector to neighbors
t=2

## Slide 69: Distance vector example: iteration
g
h
i
1
1
1
1
1
1
1
8
1
2
1
d
e
f
a
b
c
All nodes:
receive distance vectors from neighbors
compute their new local distance vector
send their new local distance vector to neighbors
t=2
compute
compute
compute
compute
compute
compute
compute
compute
compute

## Slide 70: Distance vector example: iteration
g
h
i
1
1
1
1
1
1
1
1
1
8
1
d
e
f
a
b
c
All nodes:
receive distance vectors from neighbors
compute their new local distance vector
send their new local distance vector to neighbors
t=2

## Slide 71
Routing tables are filled via routing algorithms
There are two types of routing algorithms
Centralized/Global- we know the edge costs of the network
Link State algorithms
(Dijkstra’s Algorithm)
Decentralized- we do not know the edge costs of the entire network.
Only know edge costs to neighbors
Distance Vector algorithms
These are not network protocols, these are simply general routing/shortest path algorithms

## Slide 72
Routing tables are filled via routing algorithms
There are two types of routing algorithms
Centralized/Global- we know the edge costs of the network
Link State algorithms
(Dijkstra’s Algorithm)
Decentralized- we do not know the edge costs of the entire network.
Only know edge costs to neighbors
Distance Vector algorithms
OSPF
BGP

## Slide 73
Intra-AS Routing: OSPF
An autonomous system is a group of routers that are under the same administrative control
AS 1
AS 2
AS 3

## Slide 74
Intra-AS Routing: OSPF
An autonomous system is a group of routers that are under the same administrative control
AS 1
OSPF is a link-state protocol that uses flooding of link-state information and Dijkstra’s least-cost algorithm
Open Shortest Path First

## Slide 75
Intra-AS Routing: OSPF
An autonomous system is a group of routers that are under the same administrative control
AS 1
OSPF is a link-state protocol that uses flooding of link-state information and Dijkstra’s least-cost algorithm
Open Shortest Path First
1. Each router constructors a topological map of the AS

## Slide 76
Intra-AS Routing: OSPF
An autonomous system is a group of routers that are under the same administrative control
AS 1
OSPF is a link-state protocol that uses flooding of link-state information and Dijkstra’s least-cost algorithm
Open Shortest Path First
1. Each router constructors a topological map of the AS
2. Run Dijikstra’s to determine shortest path to each subnet
(Edge costs will be set by a network administrator)
If I wanted to find the path with the shortest amount of hops, what should edge cost be?

## Slide 77
Intra-AS Routing: OSPF
An autonomous system is a group of routers that are under the same administrative control
AS 1
OSPF is a link-state protocol that uses flooding of link-state information and Dijkstra’s least-cost algorithm
Open Shortest Path First
1. Each router constructors a topological map of the AS
2. Run Dijikstra’s to determine shortest path to each subnet
(Edge costs will be set by a network administrator)
(could set all edges to be a cost of 1)
3. Fill in routing table
A | 1
B | 2
C | 3
… | …

## Slide 78
Routing Among the ISPs: BGP
Inter-AS routing protocol involves coordination amongst multiple AS’s, a common protocol needs to be used
AS 1
Border Gateway Protocol (BGP) is used for exchanging routing information between AS
?
?
?
?
?
?
?

## Slide 79
Routing Among the ISPs: BGP
Inter-AS routing protocol involves coordination amongst multiple AS’s, a common protocol needs to be used
AS 1
Border Gateway Protocol (BGP) is used for exchanging routing information between AS
BGP allows a router to tell other AS’s that it exists and needs to be connected

## Slide 80
Routing Among the ISPs: BGP
Inter-AS routing protocol involves coordination amongst multiple AS’s, a common protocol needs to be used
AS 1
Border Gateway Protocol (BGP) is used for exchanging routing information between AS
BGP allows a router to tell other AS’s that it exists and needs to be connected
AS2
AS3
AS4
AS5
AS6
AS6
AS consists of gateway routers and internal routers

## Slide 81
Routing Among the ISPs: BGP
Inter-AS routing protocol involves coordination amongst multiple AS’s, a common protocol needs to be used
AS 1
Border Gateway Protocol (BGP) is used for exchanging routing information between AS
BGP allows a router to tell other AS’s that it exists and needs to be connected
AS2
AS3
AS4
AS5
AS6
AS6
AS consists of gateway routers and internal routers

## Slide 82
Routing Among the ISPs: BGP
Inter-AS routing protocol involves coordination amongst multiple AS’s, a common protocol needs to be used
AS 1
AS2
AS3
AS4
AS5
AS6
AS6
AS consists of gateway routers and internal routers
“I am AS1 AND I EXIST!”

## Slide 83
Routing Among the ISPs: BGP
Inter-AS routing protocol involves coordination amongst multiple AS’s, a common protocol needs to be used
AS 1
AS2
AS3
AS4
AS5
AS6
AS6
AS consists of gateway routers and internal routers
“I am AS1 AND I EXIST!”
“A1 EXISTS AND FOUND THROUGH AS2”

## Slide 84: Internet inter-AS routing: BGP
BGP (Border Gateway Protocol): the de facto inter-domain routing protocol
  “glue that holds the Internet together”
allows subnet to advertise its existence, and the destinations it can reach, to rest of Internet: “I am here, here is who I can reach, and how”
BGP provides each AS a means to:
  obtain destination network reachability info from neighboring ASes (eBGP)
  determine routes to other networks based on reachability information and policy
  propagate reachability information to all AS-internal routers (iBGP)
  advertise (to neighboring networks) destination reachability info

## Slide 85
Routing Among the ISPs: BGP
BGP is the routing protocol used for routing amongst different ISPs + AS
Two important functions
Obtain prefix reachability information from neighboring ASs (CIDR)
 Determine the “best” routes to the prefixes
eBGP connectivity
iBGP connectivity
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS 2
AS 3
AS 1
1c
∂
gateway routers run both eBGP and iBGP protools

## Slide 86
Routing Among the ISPs: BGP
BGP is the routing protocol used for routing amongst different ISPs + AS
Two important functions
Obtain prefix reachability information from neighboring ASs
 Determine the “best” routes to the prefixes
eBGP connectivity
iBGP connectivity
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS 2
AS 3
AS 1
1c
gateway routers run both eBGP and iBGP protools
X
Prefix X connect
3a  2c “Hey I have X”
2a  1c “Hey AS 3 has X and I have AS3”
External BGP (eBGP)
Internal BGP (iBGP)
2c  2b
2c  2d
2c  2a

## Slide 87: BGP basics
when AS3 gateway router 3a advertises path AS3,X to AS2 gateway router 2c:
  AS3 promises to AS2 it will forward datagrams towards X
BGP session: two BGP routers (“peers”) exchange BGP messages over semi-permanent TCP connection:
  advertising paths to different destination network prefixes (BGP is a “path vector” protocol)
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS 2
AS 3
AS 1
X
BGP advertisement:
AS3, X

## Slide 88: BGP protocol messages
BGP messages exchanged between peers over TCP connection
BGP messages [RFC 4371]:
  OPEN: opens TCP connection to remote BGP peer and authenticates sending BGP peer
  UPDATE: advertises new path (or withdraws old)
  KEEPALIVE: keeps connection alive in absence of UPDATES; also ACKs OPEN request
  NOTIFICATION: reports errors in previous msg; also used to close connection

## Slide 89
Path attributes and BGP routes
BGP advertised route: prefix + attributes
  prefix: destination being advertised
  two important attributes:
  AS-PATH: list of ASes through which prefix advertisement has passed
  NEXT-HOP: indicates specific internal-AS router to next-hop AS
policy-based routing:
  gateway receiving route advertisement uses import policy to accept/decline path (e.g., never route through AS Y).
  AS policy also determines whether to advertise path to other other neighboring ASes

## Slide 90: BGP path advertisement
2b
2d
2c
2a
AS 2
3b
3d
3c
3a
AS 3
1b
1d
1c
1a
AS 1
X
based on AS2 policy, AS2 router 2c accepts path AS3,X, propagates (via iBGP) to all AS2 routers
AS2,AS3,X
AS2 router 2c receives path advertisement AS3,X (via eBGP) from AS3 router 3a
based on AS2 policy, AS2 router 2a advertises (via eBGP) path AS2, AS3, X to AS1 router 1c
AS3, X

## Slide 92
https://www.routeviews.org/routeviews/index.php/collectors/
Lots of network and path entries on this BGP router
The list of neighbors it interacts with

## Slide 93
ICMP (Internet Control Message Protocol)
used by hosts & routers to communicate network-level information
  error reporting: unreachable host, network, port, protocol
  echo request/reply (used by ping)
network-layer “above” IP:
  ICMP msgs carried in IP datagrams
ICMP message: type, code plus first 8 bytes of IP datagram causing error
Type Code description
0 0 echo reply (ping)
3 0 dest. network unreachable
3 1 dest host unreachable
3 2 dest protocol unreachable
3 3 dest port unreachable
3 6 dest network unknown
3 7 dest host unknown
4 0 source quench (congestion
control - not used)
8 0 echo request (ping)
9 0 route advertisement
10 0 router discovery
11 0 TTL expired
12 0 bad IP header