## Slide 1: CSCI 466: Networks Link Layer: Error Detection, Multiple Access Protocols
Reese Pearsall Fall 2024
https://www.cs.montana.edu/pearsall/classes/fall2024/466/main.html
1
*All images are stolen from the internet

## Slide 2: Announcements
Quiz on Friday
No class on Quiz days
Next Wireshark lab will be posted later today

## Slide 3
Application Layer
Presentation Layer
Session Layer
Transport Layer
Network Layer
Data Link Layer
Physical Layer
OSI Model
Messages from Network Applications
Application Layer
Physical Layer
Bits being transmitted over a copper wire
*In the textbook, they condense it to a 5-layer model, but 7 layers is what is most used
*
*

## Slide 4
Data Link Layer
The link layer is responsible for the actual node-to-node delivery of data and ensure error-free transmission of information
terminology:
hosts and routers: nodes
communication channels that connect adjacent nodes along communication path: links
  wired links
  wireless links
  LANs
layer-2 packet: frame, encapsulates datagram
data-link layer has responsibility of
transferring datagram from one node
to physically adjacent node over a link
We have not addressed how we will overcome various transmission mediums!

## Slide 5
Data Link Layer
Princeton
JFK
Geneva
Lausanne
transportation analogy:
trip from Princeton to Lausanne
  limo: Princeton to JFK
  plane: JFK to Geneva
  train: Geneva to Lausanne

## Slide 6
Data Link Layer
Princeton
JFK
Geneva
Lausanne
transportation analogy:
trip from Princeton to Lausanne
  limo: Princeton to JFK
  plane: JFK to Geneva
  train: Geneva to Lausanne
tourist = datagram
transport segment = communication link
transportation mode = link-layer protocol
travel agent = routing algorithm

## Slide 7
Data Link Layer
Services offered by the Link Layer
Framing
       Encapsulate a network layer Datagram in another header
Link access
 LL dictate the rules and process of transmitting a frame over a link
Reliable Delivery
 For unreliable link, some reliable delivery mechanisms may need to be used
Error Detection and Correction
 Bits can get messed up as the are transmitted through a medium
Why do we need RDT and error detection in the link layer when it is also offered in the transport layer?

## Slide 8
Data Link Layer
…
…
Cable access
cellular
WiFi
Ethernet LANs
flow control:
  pacing between adjacent sending and receiving nodes
error detection:
  errors caused by signal attenuation, noise.
  receiver detects errors, signals retransmission, or drops frame
error correction:
  receiver identifies and corrects bit error(s) without retransmission
half-duplex and full-duplex:
  with half duplex, nodes at both ends of link can transmit, but not at same time

## Slide 9
Data Link Layer
Services offered by the Link Layer
Framing
       Encapsulate a network layer Datagram in another header
Link access
 LL dictate the rules and process of transmitting a frame over a link
Reliable Delivery
 For unreliable link, some reliable delivery mechanisms may need to be used
Error Detection and Correction
 Bits can get messed up as the are transmitted through a medium
Why do we need RDT and error detection in the link layer when it is also offered in the transport layer?
Some packets of data don’t even travel through the transport layer…

## Slide 10
Data Link Layer
Implementation of Link Layer
Implemented within the hardware of your computer
NIC (Network Interface Controller)- Integrated into the motherboard and allows the machine to use LL services such as ethernet (combination of hardware, software, and some firmware)
controller
physical
transmission
cpu
memory
host
bus
(e.g., PCI)
network adapter
card
application
transport
network
link
link
physical
Wireshark uses your NIC to determine which packets should be sniffed!

## Slide 11
Data Link Layer
sending side:
  encapsulates datagram in frame
  adds error checking bits, rdt, flow control, etc.
receiving side
  looks for errors, rdt, flow control, etc.
  extracts datagram, passes to upper layer at receiving side
controller
controller
sending host
receiving host
datagram
datagram
datagram
frame
6-11
Link Layer and LANs

## Slide 12
Data Link Layer
6-12
Link Layer and LANs
Bits can get messed during the physical layer and link layer
Faulty wires
NIC issues
Unreliable mediums
EDC: error detection and correction bits
D: data protected by error checking, may include header fields
Error detection not 100% reliable!
  protocol may miss some errors, but rarely
  larger EDC field yields better detection and correction
datagram
D
EDC
d data bits
bit-error prone link
D’
EDC’
all
bits in D’
OK
?
N
detected
error
otherwise
datagram

## Slide 13
Data Link Layer
6-13
Link Layer and LANs
0111000110101011
1
parity bit
d data bits
Even/odd parity: set parity bit so there is an even/odd number of 1’s
At receiver:
compute parity of d received bits
compare with received parity bit – if different than error detected

## Slide 14
Data Link Layer
6-14
Link Layer and LANs
0111000110101011
1
parity bit
d data bits
Even/odd parity: set parity bit so there is an even/odd number of 1’s
At receiver:
compute parity of d received bits
compare with received parity bit – if different than error detected
Can detect and correct errors (without retransmission!)
two-dimensional parity: detect and correct single bit errors
d1,1
d2,1
di,1
. . .
d1,j+1
d2,j+1
di,j+1
. . .
. . .
d1,j
d2,j
di,j
. . .
di+1,1
di+1,j+1
di+1,j
. . .
. . .
. . .
. . .
row parity
column
parity
1 0 1 0 1
0 1 1 1 0
1 0 1 0 1
1 1 1 1 0
1
0
1
0
no errors:
parity
error
0 1 1 1 0 1
1 0 1 0 1 1
1 0 1 1 0 0
1 0 1 0 1 0
detected
and
correctable
single-bit
error:

## Slide 15
Data Link Layer
Checksum
0110011001100000
0101010101010101
1000111100001100
0100101011000010
1011010100111101
(one’s complement)
Binary sum of words
Checksum!
(Sender)
(Receiver)
0110011001100000
0101010101010101
1000111100001100
0100101011000010
(Binary Sum  One’s Complement)
= 1111111111111111
All 1s = No error!

## Slide 16
Data Link Layer
6-16
more powerful error-detection coding
D: data bits (given, think of these as a binary number)
G: bit pattern (generator), of r+1 bits (given, specified in CRC standard)
sender: compute r CRC bits, R, such that <D,R> exactly divisible by G (mod 2)
  receiver knows G, divides <D,R> by G. If non-zero remainder: error detected!
  can detect all burst errors less than r+1 bits
  widely used in practice (Ethernet, 802.11 WiFi)
<D,R> = D 2r XOR R
*
formula for these bits
r CRC bits
d data bits
D
R
bits to send
Sender/Receiver has D and G. Need to compute R

## Slide 17
Data Link Layer
6-17
Sender wants to compute R such that:
  D . 2r XOR R = nG
D.2r
G
R = remainder [ ]
... or equivalently (XOR R both sides):
  D . 2r = nG XOR R
... which says:
if we divide D . 2r by G, we want remainder R to satisfy:
1 0 0 1
1 0 1 0
1 0 1
0 0 0
1 0 0 1
1 0 0 1
1 0 0 1
0 0 0
1 1 0
1 1 0 0
1 0 1 0
0 1 1
0 1 1
D
R
1 0 0 1
G
0 0 0
1 0 1 1 1 0
2r (here, r=3)
*
1
0
1
algorithm for
computing R

## Slide 18
Data Link Layer
6-18
(Do some algebra to find R)
R = remainder[ ]
D.2r
G
Sender sends D + R bits.
Receiver divides D + R bits by G. Result should always be Zero if no errors occurred

## Slide 19
Data Link Layer
6-19
Access links
Point to Point – Single sender, Single Receiver at each end of link
Broadcast – shared medium
shared wire (e.g.,
cabled Ethernet)
shared RF
(e.g., 802.11 WiFi)
shared RF
(satellite)
humans at a
cocktail party
(shared air, acoustical)

## Slide 20: Multiple Access Links
Shared medium = possibility for receivers to get two frame at the same time, AKA a collision
Frame X
Frame y
Frames get tangled together, and neither frame can be read clearly by receiver

## Slide 21: Multiple Access Links
Shared medium = possibility for receivers to get two frame at the same time, AKA a collision
Frame X
Frame y
Frames get tangled together, and neither frame can be read clearly by receiver
In English, we have some rules to prevent collisions from happening
In the link layer, we will discuss 3 multiple access protocols:
Channel Partitioning, Random Access, and Taking Turns

## Slide 22: Channel Partitioning
A
B
C
D
N nodes
A
B
C
D
Links total bandwidth = D
Divide channel into N slots
Each node gets (on average) D/N bandwidth
Get to transmit data for a fixed amount of time, and then next node gets to transmit

## Slide 23: Channel Partitioning
A
B
C
D
N nodes
A
B
C
D
Links total bandwidth = D
Divide channel into N slots
Each node gets (on average) D/N bandwidth
Get to transmit data for a fixed amount of time, and then next node gets to transmit

## Slide 24: Channel Partitioning
A
B
C
D
N nodes
A
B
C
D
Links total bandwidth = D
Divide channel into N slots
Each node gets (on average) D/N bandwidth
Get to transmit data for a fixed amount of time, and then next node gets to transmit

## Slide 25: Channel Partitioning
A
B
C
D
N nodes
A
B
C
D
Links total bandwidth = D
Divide channel into N slots
Each node gets (on average) D/N bandwidth
Get to transmit data for a fixed amount of time, and then next node gets to transmit

## Slide 26: Channel Partitioning
A
B
C
D
N nodes
A
B
C
D
Links total bandwidth = D
Divide channel into N slots
Each node gets (on average) D/N bandwidth
Get to transmit data for a fixed amount of time, and then next node gets to transmit

## Slide 27: Channel Partitioning
A
B
C
D
N nodes
A
B
C
D
Links total bandwidth = D
Divide channel into N slots
Each node gets (on average) D/N bandwidth
Get to transmit data for a fixed amount of time, and then next node gets to transmit

## Slide 28: Channel Partitioning
A
B
C
D
N nodes
A
B
C
D
Links total bandwidth = D
Divide channel into N slots
Each node gets (on average) D/N bandwidth
Get to transmit data for a fixed amount of time, and then next node gets to transmit

## Slide 29: Channel Partitioning
A
B
C
D
N nodes
A
B
C
D
Links total bandwidth = D
Divide channel into N slots
Each node gets (on average) D/N bandwidth
Get to transmit data for a fixed amount of time, and then next node gets to transmit

## Slide 30: Channel Partitioning
A
B
C
D
N nodes
A
B
C
D
Links total bandwidth = D
Divide channel into N slots
Each node gets (on average) D/N bandwidth
Get to transmit data for a fixed amount of time, and then next node gets to transmit

## Slide 31: Random Access
Collisions will occur, but we will try to recover from them
Slotted ALOHA: Divide up time into discrete L/R “slots”
L = size of frame
R = Bandwidth
L/R = Time needed to transmit one frame
L/R
2 L/R
3 L/R
…
If collisions occur, the colliding nodes will flip a coin to see who should retransmit
Can only transmit frames at beginning of slots. If collision occurs, the nodes can detect collision before the slot ends

## Slide 32: Random Access
Collisions will occur, but we will try to recover from them
Slotted ALOHA: Divide up time into discrete L/R “slots”
L = size of frame
R = Bandwidth
L/R = Time needed to transmit one frame
L/R
2 L/R
3 L/R
…
If collisions occur, the colliding nodes will flip a coin to see who should retransmit
Collision

## Slide 33: Random Access
Collisions will occur, but we will try to recover from them
Slotted ALOHA: Divide up time into discrete L/R “slots”
L = size of frame
R = Bandwidth
L/R = Time needed to transmit one frame
L/R
2 L/R
3 L/R
…
If collisions occur, the colliding nodes will flip a coin to see who should retransmit
Collision
Do some probability p and retransmit if needed

## Slide 34: Random Access
Collisions will occur, but we will try to recover from them
Slotted ALOHA: Divide up time into discrete L/R “slots”
L = size of frame
R = Bandwidth
L/R = Time needed to transmit one frame
L/R
2 L/R
3 L/R
…
If collisions occur, the colliding nodes will flip a coin to see who should retransmit
Collision
Empty
Collision
Waiting a random delay

## Slide 35: Random Access
Collisions will occur, but we will try to recover from them
Slotted ALOHA: Divide up time into discrete L/R “slots”
L = size of frame
R = Bandwidth
L/R = Time needed to transmit one frame
L/R
2 L/R
3 L/R
…
If collisions occur, the colliding nodes will flip a coin to see who should retransmit
Collision
Empty
Collision
Waiting a random delay
Waiting a random delay
Success

## Slide 36: Random Access
Collisions will occur, but we will try to recover from them
Slotted ALOHA: Divide up time into discrete L/R “slots”
L = size of frame
R = Bandwidth
L/R = Time needed to transmit one frame
L/R
2 L/R
3 L/R
…
If collisions occur, the colliding nodes will flip a coin to see who should retransmit
Collision
Empty
Collision
Waiting a random delay
Waiting a random delay
Success
Empty
Collision
Waiting a random delay

## Slide 37: Random Access
Collisions will occur, but we will try to recover from them
Slotted ALOHA: Divide up time into discrete L/R “slots”
L = size of frame
R = Bandwidth
L/R = Time needed to transmit one frame
L/R
2 L/R
3 L/R
…
If collisions occur, the colliding nodes will flip a coin to see who should retransmit
Collision
Empty
Collision
Waiting a random delay
Waiting a random delay
Success
Empty
Collision
Waiting a random delay
Success

## Slide 38: Random Access
Collisions will occur, but we will try to recover from them
Slotted ALOHA: Divide up time into discrete L/R “slots”
L = size of frame
R = Bandwidth
L/R = Time needed to transmit one frame
L/R
2 L/R
3 L/R
…
If collisions occur, the colliding nodes will flip a coin to see who should retransmit
Collision
Empty
Collision
Waiting a random delay
Waiting a random delay
Success
Empty
Collision
Waiting a random delay
Success
Success

## Slide 39
polling:
centralized controller “invites” other nodes to transmit in turn
typically used with “dumb” devices
concerns:
  polling overhead
  latency
  single point of failure (master)
Bluetooth uses polling
centralized controller
client devices
poll
data
data

## Slide 40: Taking Turns
Token Passing
Nodes are connected in a circular manner, and pass a special frame (token) between each other
Can only transmit messages if you have the token

## Slide 41: LAN
Local Area Network (LAN)- A collection of devices in one physical location, typically that share a centralized internet connection
Router
Switch
(Within a LAN, we could have several Subnets)

## Slide 42: MAC addresses
32-bit IP address:
  network-layer address for interface
  used for layer 3 (network layer) forwarding
  e.g.: 128.119.40.136
MAC (or LAN or physical or Ethernet) address:
  function: used “locally” to get frame from one interface to another physically-connected interface (same subnet, in IP-addressing sense)
  48-bit MAC address (for most LANs) burned in NIC ROM, also sometimes software settable
hexadecimal (base 16) notation
(each “numeral” represents 4 bits)
  e.g.: 1A-2F-BB-76-09-AD

## Slide 43
Why do we need MAC addresses?
We need a way to physically identify a device on a network
IP addresses change frequently, but a MAC address will always be the same
An IP address is used to locate a device, a MAC address is used to identify a device
IP Address = Street Address, MAC Address = Name of person living in House
We need both an IP address and a MAC address to transmit a message
Additionally, Ethernet and WiFi are all designed to use MAC address, not IP address

## Slide 44
192.168.0.4
01-08-4C-42-1B-52
192.168.0.2
00-04-5A-63-A1-66
192.168.0.3
02-06-1B-45-A2-12
192.168.0.1
04-06-2C-58-C5-78

## Slide 45
192.168.0.4
01-08-4C-42-1B-52
192.168.0.2
00-04-5A-63-A1-66
192.168.0.3
02-06-1B-45-A2-12
192.168.0.1
04-06-2C-58-C5-78
DST IP: 192.168.0.3

## Slide 46
192.168.0.4
01-08-4C-42-1B-52
192.168.0.2
00-04-5A-63-A1-66
192.168.0.3
02-06-1B-45-A2-12
192.168.0.1
04-06-2C-58-C5-78
DST IP: 192.168.0.3
A
B
C
We need Computer B’s MAC address!

## Slide 47: ARP
Protocol for mapping IP Addresses to MAC addresses
Used only for hosts and router interfaces on the same subnet
If the entry does not exist in the table, construct and send an ARP packet
First the machine checks its ARP table
Broadcasts the ARP packet to all interfaces on the LAN (255.255.255.255)
These tables are self-updated, and do not require manual entry*

## Slide 48: ARP
A wants to send datagram to B
  B’s MAC address not in A’s ARP table.
A broadcasts ARP query packet, containing B's IP address
  destination MAC address = FF-FF-FF-FF-FF-FF
  all nodes on LAN receive ARP query
B receives ARP packet, replies to A with its (B's) MAC address
  frame sent to A’s MAC address (unicast)
A caches (saves) IP-to-MAC address pair in its ARP table until information becomes old (times out)
  soft state: information that times out (goes away) unless refreshed
ARP is “plug-and-play”:
  nodes create their ARP tables without intervention from net administrator

## Slide 49
192.168.0.4
01-08-4C-42-1B-52
192.168.0.2
00-04-5A-63-A1-66
192.168.0.3
02-06-1B-45-A2-12
192.168.0.1
04-06-2C-58-C5-78
DST IP: 192.168.0.3
A
B
C
Computer A see’s that this IP is in its “group”, so it knows that Computer B must be in the same subnet!

## Slide 50
192.168.0.4
01-08-4C-42-1B-52
192.168.0.2
00-04-5A-63-A1-66
192.168.0.3
02-06-1B-45-A2-12
192.168.0.1
04-06-2C-58-C5-78
DST IP: 192.168.0.3
A
B
C
Broadcast an ARP request to the subnet, and hope that we get a response back

## Slide 51
192.168.0.4
01-08-4C-42-1B-52
192.168.0.2
00-04-5A-63-A1-66
192.168.0.3
02-06-1B-45-A2-12
192.168.0.1
04-06-2C-58-C5-78
DST IP: 192.168.0.3
A
B
C
Broadcast an ARP request to the subnet, and hope that we get a response back
Who is 192.168.0.3?
I need your MAC Address

## Slide 52
192.168.0.4
01-08-4C-42-1B-52
192.168.0.2
00-04-5A-63-A1-66
192.168.0.3
02-06-1B-45-A2-12
192.168.0.1
04-06-2C-58-C5-78
DST IP: 192.168.0.3
A
B
C
Broadcast an ARP request to the subnet, and hope that we get a response back
Who is 192.168.0.3?
I need your MAC Address
!!!
My MAC Address is:
02-06-1B-45-A2-12

## Slide 53
192.168.0.4
01-08-4C-42-1B-52
192.168.0.2
00-04-5A-63-A1-66
192.168.0.3
02-06-1B-45-A2-12
192.168.0.1
04-06-2C-58-C5-78
DST IP: 192.168.0.3
DST MAC: 02-06-1B-45-A2-12
A
B
C
Broadcast an ARP request to the subnet, and hope that we get a response back
!!!
My MAC Address is:
02-06-1B-45-A2-12

## Slide 54
192.168.0.2
00-04-5A-63-A1-66
192.168.0.1
04-06-2C-58-C5-78
DST IP: 12.56.78.34
A
G
34.11.16.58
23.44.76.81
12.56.78.34
Google.com
Home LAN

## Slide 55
192.168.0.2
00-04-5A-63-A1-66
192.168.0.1
04-06-2C-58-C5-78
DST IP: 12.56.78.34
A
G
34.11.16.58
23.44.76.81
12.56.78.34
Google.com
Home LAN
This IP address is not in its “group”, so it forwards it to the default gateway
(In most cases, we will need to issue an ARP request to get the MAC address of the default gateway)

## Slide 56
192.168.0.2
00-04-5A-63-A1-66
192.168.0.1
04-06-2C-58-C5-78
DST IP: 12.56.78.34
A
G
34.11.16.58
23.44.76.81
12.56.78.34
Google.com
Home LAN
The gateway router will look at the IP address of the packet, and determine the best route to get to google.com (network layer)

## Slide 57
192.168.0.2
00-04-5A-63-A1-66
192.168.0.1
04-06-2C-58-C5-78
DST IP: 12.56.78.34
A
G
34.11.16.58
23.44.76.81
12.56.78.34
Google.com
Home LAN
It now needs to forward the packet to 34.11.16.58, but it does not know its MAC address

## Slide 58
192.168.0.2
00-04-5A-63-A1-66
192.168.0.1
04-06-2C-58-C5-78
DST IP: 12.56.78.34
A
G
34.11.16.58
23.44.76.81
12.56.78.34
Google.com
Home LAN
It now needs to forward the packet to 34.11.16.58, but it does not know its MAC address
Issue another ARP request!
Who is 34.11.16.58?
I need your MAC Address

## Slide 59
192.168.0.2
00-04-5A-63-A1-66
192.168.0.1
04-06-2C-58-C5-78
DST IP: 12.56.78.34
A
G
34.11.16.58
23.44.76.81
12.56.78.34
Google.com
Home LAN
It now needs to forward the packet to 34.11.16.58, but it does not know its MAC address
Issue another ARP request!
Who is 34.11.16.58?
I need your MAC Address
My MAC address is:
05-52-3F-10-C5-57
05-52-3F-10-C5-57

## Slide 60
192.168.0.2
00-04-5A-63-A1-66
192.168.0.1
04-06-2C-58-C5-78
DST IP: 12.56.78.34
A
G
34.11.16.58
23.44.76.81
12.56.78.34
Google.com
Home LAN
The next destination is 23.44.76.81, but we need its MAC address!
05-52-3F-10-C5-57

## Slide 61
192.168.0.2
00-04-5A-63-A1-66
192.168.0.1
04-06-2C-58-C5-78
DST IP: 12.56.78.34
A
G
34.11.16.58
23.44.76.81
12.56.78.34
Google.com
Home LAN
The next destination is 23.44.76.81, but we need its MAC address!
Do another ARP!
05-52-3F-10-C5-57
My MAC address is:
09-12-0D-25-D8-74
(Remember that ARP gets broadcasted to all direct neighbors)

## Slide 62
192.168.0.2
00-04-5A-63-A1-66
192.168.0.1
04-06-2C-58-C5-78
DST IP: 12.56.78.34
A
G
34.11.16.58
23.44.76.81
12.56.78.34
Google.com
Home LAN
05-52-3F-10-C5-57
09-12-0D-25-D8-74

## Slide 63
192.168.0.2
00-04-5A-63-A1-66
192.168.0.1
04-06-2C-58-C5-78
DST IP: 12.56.78.34
A
G
34.11.16.58
23.44.76.81
12.56.78.34
Google.com
Home LAN
05-52-3F-10-C5-57
09-12-0D-25-D8-74
My MAC address is:
01-33-2F-84-B8-55
Who is 12.56.78.34?
I need your MAC Address
We need to issue one final ARP request, and get the MAC address of our final destination

## Slide 64
192.168.0.2
00-04-5A-63-A1-66
192.168.0.1
04-06-2C-58-C5-78
DST IP: 12.56.78.34
A
G
34.11.16.58
23.44.76.81
12.56.78.34
Google.com
Home LAN
05-52-3F-10-C5-57
09-12-0D-25-D8-74
We need to issue one final ARP request, and get the MAC address of our final destination
01-33-2F-84-B8-55

## Slide 66
Finding your MAC Address
Ipconfig/all

## Slide 67: Ethernet
“dominant” wired LAN technology:
single chip, multiple speeds (e.g., Broadcom BCM5761)
first widely used LAN technology
simpler, cheap
kept up with speed race: 10 Mbps – 10 Gbps
Metcalfe’s Ethernet sketch

## Slide 68: Ethernet
switch
bus: coaxial cable
star
Link Layer and LANs
Ethernet Topology
(outdated)

## Slide 69
Ethernet frame structure
sending adapter encapsulates IP datagram (or other network layer protocol packet) in Ethernet frame
preamble:
7 bytes with pattern 10101010 followed by one byte with pattern 10101011
used to synchronize receiver, sender clock rates
dest.
address
source
address
data (payload)
CRC
preamble
type

## Slide 70: Ethernet frame structure (more)
addresses: 6 byte source, destination MAC addresses
  if adapter receives frame with matching destination address, or with broadcast address (e.g. ARP packet), it passes data in frame to network layer protocol
  otherwise, adapter discards frame
type: indicates higher layer protocol (mostly IP but others possible, e.g., Novell IPX, AppleTalk)
CRC: cyclic redundancy check at receiver
  error detected: frame is dropped
dest.
address
source
address
data (payload)
CRC
preamble
type

## Slide 71
Ethernet switch
Switches will store and forward ethernet frames
Hosts have dedicated, direct connection to switch
Ethernet protocol used on each incoming link, but no collisions between links
Switching: A-A’ and B-B’ can transmit simultaneously, without collisions
Transparent: Hosts are not aware
they are connected to a switch
Plug and play; self-learning
A
A’
B
B’
C
C’
1
2
3
4
5
6
= ethernet cable

## Slide 72
Switches vs. routers
both are store-and-forward:
routers: network-layer devices (examine network-layer headers)
switches: link-layer devices (examine link-layer headers)
both have forwarding tables:
routers: compute tables using routing algorithms, IP addresses
switches: learn forwarding table using flooding, learning, MAC addresses
application
transport
network
link
physical
network
link
physical
link
physical
switch
datagram
application
transport
network
link
physical
frame
frame
frame
datagram

## Slide 73
https://www.youtube.com/watch?v=1z0ULvg_pW8