## Slide 1: CSCI 466: Networks Link Layer
Reese Pearsall Fall 2024
https://www.cs.montana.edu/pearsall/classes/fall2024/466/main.html
1
*All images are stolen from the internet

## Slide 2: Announcements
Quiz 4 on Friday (no lecture)
IP Addresses
Subnets
NAT
Routing (LS, DV, OSPF, BGP)
Link Layer
Mac Addresses
Multiple Access Protocols
ARP
Ethernet
Switches
Wireshark Lab 3 due on Monday (10/21)

## Slide 3
Application Layer
Presentation Layer
Session Layer
Transport Layer
Network Layer
Data Link Layer
Physical Layer
OSI Model
Messages from Network Applications
Application Layer
Physical Layer
Bits being transmitted over a copper wire
*In the textbook, they condense it to a 5-layer model, but 7 layers is what is most used
*
*

## Slide 4
Application Layer
Presentation Layer
Session Layer
Transport Layer
Network Layer
Data Link Layer
Physical Layer
OSI Model
Messages from Network Applications
Application Layer
Physical Layer
Bits being transmitted over a copper wire
*In the textbook, they condense it to a 5-layer model, but 7 layers is what is most used
*
*
We will cover these briefly in the coming weeks

## Slide 5
Bob
School
Network
Comcast
Network
Google
Network
Web Server
DNS Server
Bob joins MSU’s school network for the first time, and wants to visit google.com on his web browser, what happens?

## Slide 6
Bob
School
Network
Comcast
Network
Google
Network
Web Server
DNS Server
Bob joins MSU’s school network for the first time, and wants to visit google.com on his web browser, what happens? Bob needs an IP address!

## Slide 7
Bob
School
Network
Comcast
Network
Google
Network
Web Server
DNS Server
The operating system on Bob’s laptop creates a DHCP request message and puts this message within a UDP segment with destination port 67 and source port 68. The UDP segment is then placed within an IP datagram with a broadcast IP destination address (255.255.255.255) and a source IP address of 0.0.0.0, since Bob’s laptop doesn’t yet have an IP address.

## Slide 8
Bob
School
Network
Comcast
Network
Google
Network
Web Server
DNS Server
The IP datagram containing the DHCP request message is then placed within an Ethernet frame. The Ethernet frame has a destination MAC addresses of FF:FF:FF:FF:FF:FF so that the frame will be broadcast to all devices connected to the switch (hopefully including a DHCP server); the frame’s source MAC address is that of Bob’s laptop, 00:16:D3:23:68:8A
00:16:D3:23:68:8A

## Slide 9
Bob
School
Network
Comcast
Network
Google
Network
Web Server
DNS Server
00:16:D3:23:68:8A
The broadcast Ethernet frame containing the DHCP request is the first frame sent by Bob’s laptop to the Ethernet switch. The switch broadcasts the incoming frame on all outgoing ports, including the port connected to the router.

## Slide 10
Bob
School
Network
Comcast
Network
Google
Network
Web Server
DNS Server
00:16:D3:23:68:8A
The router receives the broadcast Ethernet frame containing the DHCP request on its interface and the IP datagram is extracted from the Ethernet frame. The datagram’s broadcast IP destination address indicates that this IP datagram should be processed by upper layer protocols at this node, so the datagram’s payload (a UDP segment) is thus demultiplexed up to UDP, and the DHCP request message is extracted from the UDP segment. The DHCP server now has the DHCP request message.

## Slide 11
Bob
School
Network
Comcast
Network
Google
Network
Web Server
DNS Server
00:16:D3:23:68:8A
Let’s suppose the DHCP server allocates address 10.5.5.5 to Bob’s laptop. The DHCP server creates a DHCP ACK message containing this IP address, as well as the IP address of the DNS server (68.87.71.226), the IP address for the default gateway router (68.85.2.1), and the subnet block. The DHCP message is put inside a UDP segment, which is put inside an IP datagram, which is put inside an Ethernet frame. The Ethernet frame has a a destination MAC address of Bob’s laptop (00:16:D3:23:68:8A).
68.87.71.226
68.85.2.1

## Slide 12
Bob
School
Network
Comcast
Network
Google
Network
Web Server
DNS Server
00:16:D3:23:68:8A
68.87.71.226
68.85.2.1
The Ethernet frame containing the DHCP ACK is sent (unicast) by the router to the switch. Because the switch is self-learning (Section 6.4.3) and previously received an Ethernet frame (containing the DHCP request) from Bob’s laptop, the switch knows to forward a frame addressed to 00:16:D3:23:68:8A only to the output port leading to Bob’s laptop
The Ethernet frame containing the DHCP ACK is sent (unicast) by the router to the switch. Because the switch is self-learning and previously received an Ethernet frame (containing the DHCP request) from Bob’s laptop, the switch knows to forward a frame addressed to 00:16:D3:23:68:8A only to the output port leading to Bob’s laptop
10.5.5.5

## Slide 13
Bob
School
Network
Comcast
Network
Google
Network
Web Server
DNS Server
00:16:D3:23:68:8A
68.87.71.226
68.85.2.1
The Ethernet frame containing the DHCP ACK is sent (unicast) by the router to the switch. Because the switch is self-learning (Section 6.4.3) and previously received an Ethernet frame (containing the DHCP request) from Bob’s laptop, the switch knows to forward a frame addressed to 00:16:D3:23:68:8A only to the output port leading to Bob’s laptop
10.5.5.5
Bob’s laptop receives the Ethernet frame containing the DHCP ACK, extracts the IP datagram from the Ethernet frame, extracts the UDP segment from the IP datagram, and extracts the DHCP ACK message from the UDP segment. Bob’s DHCP client then records its IP address and the IP address of its DNS server. It also installs the address of the default gateway into its IP forwarding table. Bob’s laptop will send all datagrams with destination address outside of its subnet to the default gateway.

## Slide 14
Bob
School
Network
Comcast
Network
Google
Network
Web Server
DNS Server
00:16:D3:23:68:8A
68.87.71.226
68.85.2.1
The Ethernet frame containing the DHCP ACK is sent (unicast) by the router to the switch. Because the switch is self-learning (Section 6.4.3) and previously received an Ethernet frame (containing the DHCP request) from Bob’s laptop, the switch knows to forward a frame addressed to 00:16:D3:23:68:8A only to the output port leading to Bob’s laptop
10.5.5.5
What’s next?

## Slide 15
Bob
School
Network
Comcast
Network
Google
Network
Web Server
DNS Server
00:16:D3:23:68:8A
68.87.71.226
68.85.2.1
10.5.5.5
The operating system on Bob’s laptop thus creates a DNS query message, putting the string “www.google.com” in the question section of the DNS message. This DNS message is then placed within a UDP segment with a destination port of 53 (DNS server). The UDP segment is then placed within an IP datagram with an IP destination address of 68.87.71.226 and a source IP address of 10.5.5.5

## Slide 16
Bob
School
Network
Comcast
Network
Google
Network
Web Server
DNS Server
00:16:D3:23:68:8A
68.87.71.226
68.85.2.1
10.5.5.5
Bob’s laptop then places the datagram containing the DNS query message in an Ethernet frame. This frame will be sent (addressed, at the link layer) to the gateway router in Bob’s school’s network. However, even though Bob’s laptop knows the IP address of the school’s gateway router (68.85.2.1) via the DHCP ACK message, it doesn’t know the gateway router’s MAC address. In order to obtain the MAC address of the gateway router, Bob’s laptop will need to use the ARP protocol

## Slide 17
Bob
School
Network
Comcast
Network
Google
Network
Web Server
DNS Server
00:16:D3:23:68:8A
68.87.71.226
68.85.2.1
10.5.5.5
Bob’s laptop creates an ARP query message with a target IP address of 68.85.2.1 (the default gateway), places the ARP message within an Ethernet frame with a broadcast destination address (FF:FF:FF:FF:FF:FF) and sends the Ethernet frame to the switch, which delivers the frame to all connected devices, including the gateway router

## Slide 18
Bob
School
Network
Comcast
Network
Google
Network
Web Server
DNS Server
00:16:D3:23:68:8A
68.87.71.226
68.85.2.1
10.5.5.5
The gateway router receives the frame containing the ARP query message on the interface to the school network, and finds that the target IP address of 68.85.2.1 in the ARP message matches the IP address of its interface. The gateway router thus prepares an ARP reply, indicating that its MAC address of 00:22:6B:45:1F:1B corresponds to IP address 68.85.2.1. It places the ARP reply message in an Ethernet frame, with a destination address of 00:16:D3:23:68:8A (Bob’s laptop) and sends the frame to the switch, which delivers the frame to Bob’s laptop

## Slide 19
Bob
School
Network
Comcast
Network
Google
Network
Web Server
DNS Server
00:16:D3:23:68:8A
68.87.71.226
68.85.2.1
10.5.5.5
Bob’s laptop receives the frame containing the ARP reply message and extracts the MAC address of the gateway router (00:22:6B:45:1F:1B) from the ARP reply message.
00:22:6B:45:1F:1B

## Slide 20
Bob
School
Network
Comcast
Network
Google
Network
Web Server
DNS Server
00:16:D3:23:68:8A
68.87.71.226
68.85.2.1
10.5.5.5
00:22:6B:45:1F:1B
Bob’s laptop can now (finally!) address the Ethernet frame containing the DNS query to the gateway router’s MAC address. Note that the IP datagram in this frame has an IP destination address of 68.87.71.226 (the DNS server), while the frame has a destination address of 00:22:6B:45:1F:1B (the gateway router). Bob’s laptop sends this frame to the switch, which delivers the frame to the gateway router.

## Slide 21
Bob
School
Network
Comcast
Network
Google
Network
Web Server
DNS Server
00:16:D3:23:68:8A
68.87.71.226
68.85.2.1
10.5.5.5
00:22:6B:45:1F:1B
The gateway router receives the frame and extracts the IP datagram containing the DNS query. The router looks up the destination address of this datagram (68.87.71.226) and determines from its forwarding table that the datagram should be sent to the leftmost router in the Comcast network. The IP datagram is placed inside a link-layer frame appropriate for the link connecting the school’s router to the leftmost Comcast router and the frame is sent over this link.
NAT
(NAT will translate any private IP address to public IP address)

## Slide 22
Bob
School
Network
Comcast
Network
Google
Network
Web Server
DNS Server
00:16:D3:23:68:8A
68.87.71.226
68.85.2.1
10.5.5.5
00:22:6B:45:1F:1B
NAT
The leftmost router in the Comcast network receives the frame, extracts the IP datagram, examines the datagram’s destination address (68.87.71.226) and determines the outgoing interface on which to forward the datagram toward the DNS server from its forwarding table, which has been filled in by Comcast’s intra-domain protocol (such as) as well as the Internet’s inter-domain protocol, BGP

## Slide 23
Bob
School
Network
Comcast
Network
Google
Network
Web Server
DNS Server
00:16:D3:23:68:8A
68.87.71.226
68.85.2.1
10.5.5.5
00:22:6B:45:1F:1B
NAT
Eventually the IP datagram containing the DNS query arrives at the DNS server. The DNS server extracts the DNS query message, looks up the name www.google.com in its DNS database and finds the DNS resource record that contains the IP address (64.233.169.105) for www.google.com. (assuming that it is currently cached in the DNS server). Recall that this cached data originated in the authoritative DNS server for google.com. The DNS server forms a DNS reply message containing this hostname-to-IP-address mapping, and places the DNS reply message in a UDP segment, and the segment within an IP datagram addressed to Bob’s public IP (68.85.2.1). This datagram will be forwarded back through the Comcast network to the school’s router and from there, via the Ethernet switch to Bob’s laptop

## Slide 24
Bob
School
Network
Comcast
Network
Google
Network
Web Server
DNS Server
00:16:D3:23:68:8A
68.87.71.226
68.85.2.1
10.5.5.5
00:22:6B:45:1F:1B
NAT
Bob’s laptop extracts the IP address of the server www.google.com from the DNS message. Finally, after a lot of work, Bob’s laptop is now ready to contact the www.google.com server!
64.233.169.105

## Slide 25
Bob
School
Network
Comcast
Network
Google
Network
Web Server
DNS Server
00:16:D3:23:68:8A
68.87.71.226
68.85.2.1
10.5.5.5
00:22:6B:45:1F:1B
NAT
Now what?
64.233.169.105

## Slide 26
Bob
School
Network
Comcast
Network
Google
Network
Web Server
DNS Server
00:16:D3:23:68:8A
68.87.71.226
68.85.2.1
10.5.5.5
00:22:6B:45:1F:1B
NAT
64.233.169.105
Now that Bob’s laptop has the IP address of www.google.com, it can create the TCP socket that will be used to send the HTTP GET message to www.google.com. When Bob creates the TCP socket, the TCP in Bob’s laptop must first perform a three-way handshake with the TCP in www.google.com. Bob’s laptop thus first creates a TCP SYN segment with destination port 80 (for HTTP), places the TCP segment inside an IP datagram with a destination IP address of 64.233.169.105 (www.google.com), places the datagram inside a frame with a destination MAC address of 00:22:6B:45:1F:1B (the gateway router) and sends the frame to the switch

## Slide 27
Bob
School
Network
Comcast
Network
Google
Network
Web Server
DNS Server
00:16:D3:23:68:8A
68.87.71.226
68.85.2.1
10.5.5.5
00:22:6B:45:1F:1B
NAT
64.233.169.105
The routers in the school network, Comcast’s network, and Google’s network forward the datagram containing the TCP SYN toward www.google.com, using the forwarding table in each router. Recall that the router forwarding table entries governing forwarding of packets over the inter-domain link between the Comcast and Google networks are determined by the BGP protocol

## Slide 28
Bob
School
Network
Comcast
Network
Google
Network
Web Server
DNS Server
00:16:D3:23:68:8A
68.87.71.226
68.85.2.1
10.5.5.5
00:22:6B:45:1F:1B
NAT
64.233.169.105
The routers in the school network, Comcast’s network, and Google’s network forward the datagram containing the TCP SYN toward www.google.com, using the forwarding table in each router. Recall that the router forwarding table entries governing forwarding of packets over the inter-domain link between the Comcast and Google networks are determined by the BGP protocol

## Slide 29
Bob
School
Network
Comcast
Network
Google
Network
Web Server
DNS Server
00:16:D3:23:68:8A
68.87.71.226
68.85.2.1
10.5.5.5
00:22:6B:45:1F:1B
NAT
64.233.169.105
Eventually, the datagram containing the TCP SYN arrives at www.google.com. The TCP SYN message is extracted from the datagram and demultiplexed to the welcome socket associated with port 80. A connection socket is created for the TCP connection between the Google HTTP server and Bob’s laptop. A TCP SYNACK segment is generated, placed inside a datagram addressed to Bob’s laptop, and finally placed inside a link-layer frame appropriate for the link connecting www.google.com to its first-hop router.

## Slide 30
Bob
School
Network
Comcast
Network
Google
Network
Web Server
DNS Server
00:16:D3:23:68:8A
68.87.71.226
68.85.2.1
10.5.5.5
00:22:6B:45:1F:1B
NAT
64.233.169.105
The datagram containing the TCP SYNACK segment is forwarded through the Google, Comcast, and school networks, eventually arriving at the Ethernet controller in Bob’s laptop. The datagram is demultiplexed within the operating system to the TCP socket

## Slide 31
Bob
School
Network
Comcast
Network
Google
Network
Web Server
DNS Server
00:16:D3:23:68:8A
68.87.71.226
68.85.2.1
10.5.5.5
00:22:6B:45:1F:1B
NAT
64.233.169.105
The datagram containing the TCP SYNACK segment is forwarded through the Google, Comcast, and school networks, eventually arriving at the Ethernet controller in Bob’s laptop. The datagram is demultiplexed within the operating system to the TCP socket

## Slide 32
Bob
School
Network
Comcast
Network
Google
Network
Web Server
DNS Server
00:16:D3:23:68:8A
68.87.71.226
68.85.2.1
10.5.5.5
00:22:6B:45:1F:1B
NAT
64.233.169.105
The datagram containing the TCP SYNACK segment is forwarded through the Google, Comcast, and school networks, eventually arriving at the Ethernet controller in Bob’s laptop. The datagram is demultiplexed within the operating system to the TCP socket

## Slide 33
Bob
School
Network
Comcast
Network
Google
Network
Web Server
DNS Server
00:16:D3:23:68:8A
68.87.71.226
68.85.2.1
10.5.5.5
00:22:6B:45:1F:1B
NAT
64.233.169.105
The datagram containing the TCP SYNACK segment is forwarded through the Google, Comcast, and school networks, eventually arriving at the Ethernet controller in Bob’s laptop. The datagram is demultiplexed within the operating system to the TCP socket

## Slide 34
Bob
School
Network
Comcast
Network
Google
Network
Web Server
DNS Server
00:16:D3:23:68:8A
68.87.71.226
68.85.2.1
10.5.5.5
00:22:6B:45:1F:1B
NAT
64.233.169.105
Bob’s laptop then sends an TCP ACK back to google’s web server to complete the TCP handshake

## Slide 35
Bob
School
Network
Comcast
Network
Google
Network
Web Server
DNS Server
00:16:D3:23:68:8A
68.87.71.226
68.85.2.1
10.5.5.5
00:22:6B:45:1F:1B
NAT
64.233.169.105
Bob’s laptop then sends an TCP ACK back to google’s web server to complete the TCP handshake

## Slide 36
Bob
School
Network
Comcast
Network
Google
Network
Web Server
DNS Server
00:16:D3:23:68:8A
68.87.71.226
68.85.2.1
10.5.5.5
00:22:6B:45:1F:1B
NAT
64.233.169.105
Bob’s laptop then sends an TCP ACK back to google’s web server to complete the TCP handshake

## Slide 37
Bob
School
Network
Comcast
Network
Google
Network
Web Server
DNS Server
00:16:D3:23:68:8A
68.87.71.226
68.85.2.1
10.5.5.5
00:22:6B:45:1F:1B
NAT
64.233.169.105
Bob’s laptop then sends an TCP ACK back to google’s web server to complete the TCP handshake

## Slide 38
Bob
School
Network
Comcast
Network
Google
Network
Web Server
DNS Server
00:16:D3:23:68:8A
68.87.71.226
68.85.2.1
10.5.5.5
00:22:6B:45:1F:1B
NAT
64.233.169.105
Now what?
TCP
TCP

## Slide 39
Bob
School
Network
Comcast
Network
Google
Network
Web Server
DNS Server
00:16:D3:23:68:8A
68.87.71.226
68.85.2.1
10.5.5.5
00:22:6B:45:1F:1B
NAT
64.233.169.105
TCP
TCP
With the socket on Bob’s laptop now (finally!) ready to send bytes to www.google.com, Bob’s browser creates the HTTP GET message containing the URL to be fetched. The HTTP GET message is then written into the socket, with the GET message becoming the payload of a TCP segment. The TCP segment is placed in a datagram and sent and delivered to www.google.com.

## Slide 40
Bob
School
Network
Comcast
Network
Google
Network
Web Server
DNS Server
00:16:D3:23:68:8A
68.87.71.226
68.85.2.1
10.5.5.5
00:22:6B:45:1F:1B
NAT
64.233.169.105
TCP
TCP

## Slide 41
Bob
School
Network
Comcast
Network
Google
Network
Web Server
DNS Server
00:16:D3:23:68:8A
68.87.71.226
68.85.2.1
10.5.5.5
00:22:6B:45:1F:1B
NAT
64.233.169.105
TCP
TCP

## Slide 42
Bob
School
Network
Comcast
Network
Google
Network
Web Server
DNS Server
00:16:D3:23:68:8A
68.87.71.226
68.85.2.1
10.5.5.5
00:22:6B:45:1F:1B
NAT
64.233.169.105
TCP
TCP
The HTTP server at www.google.com reads the HTTP GET message from the TCP socket, creates an HTTP response message places the requested Web page content in the body of the HTTP response message, and sends the message into the TCP socket
This is only one web object…

## Slide 43
Bob
School
Network
Comcast
Network
Google
Network
Web Server
DNS Server
00:16:D3:23:68:8A
68.87.71.226
68.85.2.1
10.5.5.5
00:22:6B:45:1F:1B
NAT
64.233.169.105
TCP
TCP
The datagram containing the HTTP reply message is forwarded through the Google, Comcast, and school networks, and arrives at Bob’s laptop. Bob’s Web browser program reads the HTTP response from the socket, extracts the html for the Web page from the body of the HTTP response, and finally (finally!) displays the Web page!

## Slide 44
Bob
School
Network
Comcast
Network
Google
Network
Web Server
DNS Server
00:16:D3:23:68:8A
68.87.71.226
68.85.2.1
10.5.5.5
00:22:6B:45:1F:1B
NAT
64.233.169.105
TCP
TCP