## Slide 1: CSCI 466: Networks
Lecture 2: Network Edge, Network Core, OSI Model
Reese Pearsall
Fall 2022
https://www.cs.montana.edu/pearsall/classes/fall2022/466/main.html

## Slide 2
Announcements
D2L Only used for submitting assignments and for posting grades
You can always email me to arrange a time to meet (in person or virtually)
Lectures will be recorded (but I am currently figuring out new recording software)

## Slide 3
End to End Communication
Devices that are connected to network are called hosts or end systems
A typical home network
Wireless endpoints
Wired endpoints
How does out network get access through other networks?

## Slide 4
End to End Communication
Devices that are connected to network are called hosts or end systems
A typical home network
End systems are connected together by a network of communication links and packet switches
wireless access
point (54 Mbps)
Packet Switch
Communication Link

## Slide 5
End to End Communication
Devices that are connected to network are called hosts or end systems
A typical home network
End systems are connected together by a network of communication links and packet switches
wireless access
point (54 Mbps)
Packet Switch
Communication Link
The most common packet switch we see is called a router

## Slide 6
End to End Communication
Devices that are connected to network are called hosts or end systems
A typical home network
End systems are connected together by a network of communication links and packet switches
Packet Switch
The most common packet switch we see is called a router
A packet switch takes a packet arriving on one of its incoming communication links and forwards that packet on one of its outgoing communication links

## Slide 7
End to End Communication
End systems gain access to the internet through Internet Service Providers (ISPs)

## Slide 8
End to End Communication
End systems gain access to the internet through Internet Service Providers (ISPs)

## Slide 9
End to End Communication
End systems gain access to the internet through Internet Service Providers (ISPs)

## Slide 10
End to End Communication
End systems gain access to the internet through Internet Service Providers (ISPs)

## Slide 11
End to End Communication
“End-to-end communication”
Most hosts can be classified into two categories:
Clients
Servers

## Slide 12
End to End Communication
“End-to-end communication”
Most hosts can be classified into two categories:
Clients (Desktops, Laptops, Phones)
Servers (Powerful computers that store web pages, videos, emails, etc)

## Slide 13
End to End Communication
“End-to-end communication”
Servers typically reside in large datacenters

## Slide 14
Network Edge
The network edge consists of end systems

## Slide 15
Network Edge
An access network is the network that physically connects an end system to the first router
The way that homes and enterprises get connected to the internet

## Slide 16
Network Edge
An access network is the network that physically connects an end system to the first router
The way that homes and enterprises get connected to the internet

## Slide 17
End to End Communication
“Edge Routers” act as the boundary between a private network and a public network

## Slide 18
Home Network Access
Uses existing telephone line to connect to internet and transmit data
Digital Subscriber Line (DSL)

## Slide 19
Home Network Access
Uses existing television cable lines to connect to internet and transmit data
Cable Internet Access
Homes will require a modem, which connects to a home PC with an Ethernet cable
*Shared broadcast medium

## Slide 20
Home Network Access
Uses existing television cable lines to connect to internet and transmit data
Cable Internet Access
Homes will require a modem, which connects to a home PC with an Ethernet cable
(WLAN)

## Slide 21
Home Network Access
Connects homes to a shared fiber cable
Fiber Internet Access (FTTH)

## Slide 22
Home Network Access
Ethernet Internet Access

## Slide 23
Ok, but like how ?

## Slide 24
Ok, but like how ?
Twisted-Pair Copper Wire, Coaxial Cable, Fiber Optics

## Slide 25
Ok, but like how ?
Radio
Microwave
Infrared
Satellite

## Slide 26
Ok, but like how ?
Guided Medium
Unguided Medium

## Slide 27
The Network Core
End systems are connected together by a network of communication links and packet switches
A packet switch takes a packet arriving on one of its incoming communication links and forwards that packet on one of its outgoing communication links
Each communication link has its own transmission rate (bits/sec)
10 Mbps
500 kbps
100 kbps

## Slide 28
The Network Core
Messages going from A to B are split into packets
“Good morning, I hope you are having a good day!”
Good morning, I hope you are having a good day!
To: Host A
John Paxton
192.42.98.11
From: Host B
Reese Pearsall
192.5.223.42
1500 Bytes
Generated Packet

## Slide 29
The Network Core
Messages going from A to B are split into packets
“Good morning, I hope you are having a good day!”
Good morning, I hope you are having a good day!
To: Host A
John Paxton
192.42.98.11
From: Host B
Reese Pearsall
192.5.223.42
1500 Bytes
Generated Packet
P

## Slide 30
The Network Core
Messages going from A to B are split into packets
“Good morning, I hope you are having a good day!”
Good morning, I hope you are having a good day!
To: Host A
John Paxton
192.42.98.11
From: Host B
Reese Pearsall
192.5.223.42
1500 Bytes
Generated Packet
P

## Slide 31
The Network Core
Messages going from A to B are split into packets
“Good morning, I hope you are having a good day!”
Good morning, I hope you are having a good day!
To: Host A
John Paxton
192.42.98.11
From: Host B
Reese Pearsall
192.5.223.42
1500 Bytes
Generated Packet
P

## Slide 32
The Network Core
Messages going from A to B are split into packets
“Good morning, I hope you are having a good day!”
Good morning, I hope you are having a good day!
To: Host A
John Paxton
192.42.98.11
From: Host B
Reese Pearsall
192.5.223.42
1500 Bytes
Generated Packet
P

## Slide 33
The Network Core
Messages going from A to B are split into packets
“Good morning, I hope you are having a good day!”
Good morning, I hope you are having a good day!
To: Host A
John Paxton
192.42.98.11
From: Host B
Reese Pearsall
192.5.223.42
1500 Bytes
Generated Packet
P

## Slide 34
The Network Core
Messages going from A to B are split into packets
“Good morning, I hope you are having a good day!”
Good morning, I hope you are having a good day!
To: Host A
John Paxton
192.42.98.11
From: Host B
Reese Pearsall
192.5.223.42
1500 Bytes
Generated Packet
P

## Slide 35
The Network Core
Messages going from A to B are split into packets
“Good morning, I hope you are having a good day!”
Good morning, I hope you are having a good day!
To: Host A
John Paxton
192.42.98.11
From: Host B
Reese Pearsall
192.5.223.42
1500 Bytes
Generated Packet
P

## Slide 36
The Network Core
Messages going from A to B are split into packets
“Good morning, I hope you are having a good day!”
Good morning, I hope you are having a good day!
To: Host A
John Paxton
192.42.98.11
From: Host B
Reese Pearsall
192.5.223.42
1500 Bytes
Generated Packet
P

## Slide 37
The Network Core
Messages going from A to B are split into packets
P
Packets are generally small, and cannot exceed a certain size

## Slide 38
The Network Core
Messages going from A to B are split into packets
Packets are generally small, and cannot exceed a certain size
What if we are transmitting large pieces of data?

## Slide 39
The Network Core
Messages going from A to B are split into packets
Packets are generally small, and cannot exceed a certain size
What if we are transmitting large pieces of data?
We must split it up!

## Slide 40
The Network Core
Messages going from A to B are split into packets
Packets are generally small, and cannot exceed a certain size
What if we are transmitting large pieces of data?
We must split it up!
To: Host A
John Paxton
192.42.98.11
To: Host A
John Paxton
192.42.98.11
To: Host A
John Paxton
192.42.98.11
From: Host B
Reese Pearsall
192.5.223.42
From: Host B
Reese Pearsall
192.5.223.42
From: Host B
Reese Pearsall
192.5.223.42
P1
P2
P3

## Slide 41
The Network Core
Messages going from A to B are split into packets
Packets are generally small, and cannot exceed a certain size
What if we are transmitting large pieces of data?
We must split it up!
To: Host A
John Paxton
192.42.98.11
To: Host A
John Paxton
192.42.98.11
To: Host A
John Paxton
192.42.98.11
From: Host B
Reese Pearsall
192.5.223.42
From: Host B
Reese Pearsall
192.5.223.42
From: Host B
Reese Pearsall
192.5.223.42
P1
P2
P3
P1
P2
P3

## Slide 42
The Network Core
Messages going from A to B are split into packets
Packets are generally small, and cannot exceed a certain size
What if we are transmitting large pieces of data?
We must split it up!
To: Host A
John Paxton
192.42.98.11
To: Host A
John Paxton
192.42.98.11
To: Host A
John Paxton
192.42.98.11
From: Host B
Reese Pearsall
192.5.223.42
From: Host B
Reese Pearsall
192.5.223.42
From: Host B
Reese Pearsall
192.5.223.42
P1
P2
P3
P1
P2
P3

## Slide 43
The Network Core
Messages going from A to B are split into packets
Packets are generally small, and cannot exceed a certain size
What if we are transmitting large pieces of data?
We must split it up!
To: Host A
John Paxton
192.42.98.11
To: Host A
John Paxton
192.42.98.11
To: Host A
John Paxton
192.42.98.11
From: Host B
Reese Pearsall
192.5.223.42
From: Host B
Reese Pearsall
192.5.223.42
From: Host B
Reese Pearsall
192.5.223.42
P1
P2
P3
P1
P2
P3

## Slide 44
The Network Core
Messages going from A to B are split into packets
Packets are generally small, and cannot exceed a certain size
What if we are transmitting large pieces of data?
We must split it up!
To: Host A
John Paxton
192.42.98.11
To: Host A
John Paxton
192.42.98.11
To: Host A
John Paxton
192.42.98.11
From: Host B
Reese Pearsall
192.5.223.42
From: Host B
Reese Pearsall
192.5.223.42
From: Host B
Reese Pearsall
192.5.223.42
P1
P2
P3
P1
P2
P3

## Slide 45
The Network Core
Messages going from A to B are split into packets
Packets are generally small, and cannot exceed a certain size
What if we are transmitting large pieces of data?
We must split it up!
To: Host A
John Paxton
192.42.98.11
To: Host A
John Paxton
192.42.98.11
To: Host A
John Paxton
192.42.98.11
From: Host B
Reese Pearsall
192.5.223.42
From: Host B
Reese Pearsall
192.5.223.42
From: Host B
Reese Pearsall
192.5.223.42
P1
P2
P3
P1
P2
P3

## Slide 46
The Network Core
Messages going from A to B are split into packets
Packets are generally small, and cannot exceed a certain size
What if we are transmitting large pieces of data?
We must split it up!
To: Host A
John Paxton
192.42.98.11
To: Host A
John Paxton
192.42.98.11
To: Host A
John Paxton
192.42.98.11
From: Host B
Reese Pearsall
192.5.223.42
From: Host B
Reese Pearsall
192.5.223.42
From: Host B
Reese Pearsall
192.5.223.42
P1
P2
P3
P1
P2
P3

## Slide 47
The Network Core
Messages going from A to B are split into packets
Packets are generally small, and cannot exceed a certain size
What if we are transmitting large pieces of data?
We must split it up!
To: Host A
John Paxton
192.42.98.11
To: Host A
John Paxton
192.42.98.11
To: Host A
John Paxton
192.42.98.11
From: Host B
Reese Pearsall
192.5.223.42
From: Host B
Reese Pearsall
192.5.223.42
From: Host B
Reese Pearsall
192.5.223.42
P1
P2
P3
P1
P2
P3

## Slide 48
The Network Core
Messages going from A to B are split into packets
Packets are generally small, and cannot exceed a certain size
What if we are transmitting large pieces of data?
We must split it up!
To: Host A
John Paxton
192.42.98.11
To: Host A
John Paxton
192.42.98.11
To: Host A
John Paxton
192.42.98.11
From: Host B
Reese Pearsall
192.5.223.42
From: Host B
Reese Pearsall
192.5.223.42
From: Host B
Reese Pearsall
192.5.223.42
P1
P2
P3
P1
P2
P3

## Slide 49
The Network Core
Messages going from A to B are split into packets
Packets are generally small, and cannot exceed a certain size
What if we are transmitting large pieces of data?
We must split it up!
To: Host A
John Paxton
192.42.98.11
To: Host A
John Paxton
192.42.98.11
To: Host A
John Paxton
192.42.98.11
From: Host B
Reese Pearsall
192.5.223.42
From: Host B
Reese Pearsall
192.5.223.42
From: Host B
Reese Pearsall
192.5.223.42
P1
P2
P3
P1
P2
P3

## Slide 50
The Network Core
Messages going from A to B are split into packets
Packets are generally small, and cannot exceed a certain size
What if we are transmitting large pieces of data?
We must split it up!
To: Host A
John Paxton
192.42.98.11
To: Host A
John Paxton
192.42.98.11
To: Host A
John Paxton
192.42.98.11
From: Host B
Reese Pearsall
192.5.223.42
From: Host B
Reese Pearsall
192.5.223.42
From: Host B
Reese Pearsall
192.5.223.42
P1
P2
P3
P1
P2
P3

## Slide 51
The Network Core
Messages going from A to B are split into packets
Packets are generally small, and cannot exceed a certain size
What if we are transmitting large pieces of data?
We must split it up!
To: Host A
John Paxton
192.42.98.11
To: Host A
John Paxton
192.42.98.11
To: Host A
John Paxton
192.42.98.11
From: Host B
Reese Pearsall
192.5.223.42
From: Host B
Reese Pearsall
192.5.223.42
From: Host B
Reese Pearsall
192.5.223.42
P1
P2
P3
P1
P2
P3

## Slide 52
The Network Core
Messages going from A to B are split into packets
Packets are generally small, and cannot exceed a certain size
What if we are transmitting large pieces of data?
We must split it up!
To: Host A
John Paxton
192.42.98.11
To: Host A
John Paxton
192.42.98.11
To: Host A
John Paxton
192.42.98.11
From: Host B
Reese Pearsall
192.5.223.42
From: Host B
Reese Pearsall
192.5.223.42
From: Host B
Reese Pearsall
192.5.223.42
P1
P2
P3
P1
P2
P3

## Slide 53
The Network Core
Messages going from A to B are split into packets
Packets are generally small, and cannot exceed a certain size
What if we are transmitting large pieces of data?
We must split it up!
To: Host A
John Paxton
192.42.98.11
To: Host A
John Paxton
192.42.98.11
To: Host A
John Paxton
192.42.98.11
From: Host B
Reese Pearsall
192.5.223.42
From: Host B
Reese Pearsall
192.5.223.42
From: Host B
Reese Pearsall
192.5.223.42
P1
P2
P3
P1
P2
P3

## Slide 54
The Network Core
Messages going from A to B are split into packets
Packets are generally small, and cannot exceed a certain size
To: Host A
John Paxton
192.42.98.11
To: Host A
John Paxton
192.42.98.11
To: Host A
John Paxton
192.42.98.11
From: Host B
Reese Pearsall
192.5.223.42
From: Host B
Reese Pearsall
192.5.223.42
From: Host B
Reese Pearsall
192.5.223.42
P2
P3
P1
P1
P2
P3
Final Result:

## Slide 55
The Network Core
Messages going from A to B are split into packets
Packets are generally small, and cannot exceed a certain size
To: Host A
John Paxton
192.42.98.11
To: Host A
John Paxton
192.42.98.11
From: Host B
Reese Pearsall
192.5.223.42
From: Host B
Reese Pearsall
192.5.223.42
P1
P2
P3
P1
P2
P3
Lost, Discarded, Corrupt

## Slide 56
The Network Core
Messages going from A to B are split into packets
Packets are generally small, and cannot exceed a certain size
To: Host A
John Paxton
192.42.98.11
To: Host A
John Paxton
192.42.98.11
To: Host A
John Paxton
192.42.98.11
From: Host B
Reese Pearsall
192.5.223.42
From: Host B
Reese Pearsall
192.5.223.42
From: Host B
Reese Pearsall
192.5.223.42
P2
P3
P1
P1
P2
P3
Final Result:
Solution?

## Slide 57
The Network Core
Messages going from A to B are split into packets
Packets are generally small, and cannot exceed a certain size
To: Host A
John Paxton
192.42.98.11
To: Host A
John Paxton
192.42.98.11
To: Host A
John Paxton
192.42.98.11
From: Host B
Reese Pearsall
192.5.223.42
From: Host B
Reese Pearsall
192.5.223.42
From: Host B
Reese Pearsall
192.5.223.42
P2
P3
P1
P1
P2
P3
Final Result:
Solution?
1/3
2/3
3/3

## Slide 58
The Network Core
Messages going from A to B are split into packets
Packets are generally small, and cannot exceed a certain size
To: Host A
John Paxton
192.42.98.11
To: Host A
John Paxton
192.42.98.11
To: Host A
John Paxton
192.42.98.11
From: Host B
Reese Pearsall
192.5.223.42
From: Host B
Reese Pearsall
192.5.223.42
From: Host B
Reese Pearsall
192.5.223.42
P2
P3
P1
P1
P2
P3
Final Result:
Solution?
1/3
2/3
3/3

## Slide 59
The Network Core
Messages going from A to B are split into packets
Packets are generally small, and cannot exceed a certain size
To: Host A
John Paxton
192.42.98.11
To: Host A
John Paxton
192.42.98.11
To: Host A
John Paxton
192.42.98.11
From: Host B
Reese Pearsall
192.5.223.42
From: Host B
Reese Pearsall
192.5.223.42
From: Host B
Reese Pearsall
192.5.223.42
P2
P3
P1
P1
P2
P3
Final Result:
Solution?
1/3
2/3
3/3

## Slide 60
Anatomy of a Packet

## Slide 61
Anatomy of a Packet
Along the way, more information is appended to the packet!

## Slide 62
Anatomy of a Packet
Along the way, more information is appended to the packet!
It’s a complicated system!

## Slide 63
Application Layer
Presentation Layer
Session Layer
Transport Layer
Network Layer
Data Link Layer
Physical Layer
OSI Model
Open Systems Interconnection Model

## Slide 64
Application Layer
Presentation Layer
Session Layer
Transport Layer
Network Layer
Data Link Layer
Physical Layer
OSI Model
Messages from Network Applications
Application Layer
Physical Layer
Bits being transmitted over a copper wire

## Slide 66
Questions?