## Slide 1: CSCI 466: Networks Network Layer – Data Plane
Reese Pearsall Fall 2022
https://www.cs.montana.edu/pearsall/classes/fall2022/466/main.html
1
*All images are stolen from the internet

## Slide 2: Announcements
NO CLASS this Friday (10/14) and next Monday (10/17)
You can always email/DM me if you have questions
Extra Credit survey still available !!
Wireshark Lab 1 due TONIGHT @ 11:59 PM
If you work with a partner, both need to submit to D2L!

## Slide 3: Application Layer
Presentation Layer
Session Layer
Transport Layer
Network Layer
Data Link Layer
Messages from Network Applications
Application Layer
Physical Layer
Physical Layer
*In the textbook, they condense it to a 5-layer model,
but 7 layers is what is most used
Bits being transmitted over a medium
*
*

## Slide 4: Application Layer
Presentation Layer
Session Layer
Transport Layer
Network Layer
Data Link Layer
Messages from Network Applications
Application Layer
Physical Layer
Bits being transmitted over a medium
*
*
Physical Layer
*In the textbook, they condense it to a 5-layer model,
but 7 layers is what is most used

## Slide 5: Application Layer
Transport Layer
Message
Transport Layer Header
“Segment”
Application Layer Protocol (ex. HTPP)
Transport Layer Protocol
(ex. TCP)
Our packet of information so far…

## Slide 6: Application Layer
Transport Layer
Message
Transport Layer Header
“Segment”
Application Layer Protocol (ex. DNS)
Transport Layer Protocol
(ex. UDP)
Our packet of information so far…

## Slide 7
Application Layer
Transport Layer
???
Network Layer
We’ve only looked at protocols that are running on some host

## Slide 8: We will now shift our focus towards routers, or packet switches
In the network layer, we finally get to leave the host and adventure into the network

## Slide 9
Routers do not have functionality for application & transport layer protocols

## Slide 10: We will now shift our focus towards routers, or packet switches
Routing: determine route taken by packets from source to destination

## Slide 11
We will now shift our focus towards routers, or packet switches
Routing: determine route taken by packets from source to destination
There is likely very many paths from one host to another! Which is the most efficient path?

## Slide 12: We will now shift our focus towards routers, or packet switches
Forwarding: move packets from router’s input to appropriate router output
?
?
?
Which path should be taken?

## Slide 13: Network Layer
Responsible for the delivery of data through a network
Routing
Forwarding

## Slide 14: Router Architecture Overview
Destination-based forwarding
  Forwarding decisions are based on the destination of the packet
Generalized forwarding
  Forwarding decisions based on any set of header field values

## Slide 15: Router Architecture Overview
Bit-level reception (physical layer)
Link Layer Protocol
Lookup, forwarding, queueing
Bits received
…
…
Such as over the wire or through the air
Next layer of OSI
model
Ex. Ethernet
Evaluate header field values, lookup output port using forwarding table in memory
Queueing will occur if datagrams arrive faster
than forwarding rate into the switching fabric
“Switching Fabric”
INPUT PORT

## Slide 16: Router Architecture Overview
Storing, ready for send off
Link Layer Protocol
Send bits
“Switching Fabric”
…
…
To destination
OUTPUT PORT

## Slide 17: Forwarding Techniques
Lookup, forwarding, queueing
…
…
Address range | Interface (output link)
128.11.52.0 – 128.11.52.255 | 1
153.90.2.0 – 153.90.2.255 | 2
153.90.2.87 – 153.90.2.89 | 3
Routing Table
Connection-less
does not require startup,
Has no idea where the final destination is
This routing table could get very big…
IP addresses need 32/64 bits of memory each

## Slide 18: Forwarding Techniques
Lookup, forwarding, queueing
…
…
Address range | Interface (output link)
128.11.52.0 – 128.11.52.255 | 1
153.90.2.0 – 153.90.2.255 | 2
153.90.2.87 – 153.90.2.89 | 3
Routing Table
Connection-less
does not require startup,
Has no idea where the final destination is
Virtual Circuit Networks
VC identifier | Interface (output link)
22 | 1
13 | 2
5 | 3
Connection-oriented
Requires startup
Costly 

## Slide 19: Forwarding Techniques
Lookup, forwarding, queueing
…
…
Address range | Interface (output link)
11001000 00010111 00010*** ********* | 1
11001000 00010111 00011000 ********* | 2
11001000 00010111 00011*** ******** | 3
otherwise | 4
Longest prefix matching
when looking for forwarding table entry for given destination address, use longest address prefix that matches destination address
examples:
DA: 11001000 00010111 000
11000 10101010
DA: 11001000 00010111 000
10110 10100001
which interface? which interface?

## Slide 20: Forwarding Techniques
Lookup, forwarding, queueing
…
…
Address range | Interface (output link)
11001000 00010111 00010*** ********* | 1
11001000 00010111 00011000 ********* | 2
11001000 00010111 00011*** ******** | 3
otherwise | 4
Longest prefix matching
when looking for forwarding table entry for given destination address, use longest address prefix that matches destination address
These lookups need to happen in nanoseconds for our network to function
Ternary content addressable memories (TCAMs) are used in modern routers to do LPM
Cisco routers can carry millions of TCAM entries in their routers

## Slide 21: Fabric Switch and Switching
Switching fabric: Mechanism that forwards data from an input port to output port
Switching via memory:
Handled by a CPU (routing processor) Cannot forward data in parallel

## Slide 22: Fabric Switch and Switching
Switching fabric: Mechanism that forwards data from an input port to output port
Switching via memory:
Handled by a CPU (routing processor) Cannot forward data in parallel
Switching via bus:
Datagrams are prepended with a header
A “bus” transports input port datagrams to output ports
“keep going around the roundabout until you find your port”

## Slide 23: Fabric Switch and Switching
Switching fabric: Mechanism that forwards data from an input port to output port
Switching via memory:
Handled by a CPU (routing processor) Cannot forward data in parallel
Switching via bus:
Datagrams are prepended with a header
A “bus” transports input port datagrams to output ports
Switching via network:
A network of buses
“keep going around the roundabout until you find your port”
One shared bus, but can only fit one datagram

## Slide 24: Input Queueing
fabric slower than input ports combined  queueing may occur at input queues
Input ports
Input ports
Output ports
Output ports
Head-of-the-Line (HOL) blocking: queued datagram at front of queue prevents others in queue from moving forward

## Slide 25: Output Queueing
Storing, ready
for send off
Link Layer Protocol
Send bits
OUTPUT PORT
Input
port
Input port
Input port
Input
port
Switching Fabric
Incoming packets will have to wait for buffer space to become available
Possible solutions:
Remove a packet
  Tail drop: drop arriving packet
  Priority: drop/remove on a priority basis
  Random: drop/remove randomly

## Slide 26: Packet Scheduling
Scheduling is used to determine the next packet to send on the link
FIFO (first in first out): Send in order of arrival to queue

## Slide 27: Packet Scheduling
Scheduling is used to determine the next packet to send on the link
Priority: packets are classified into priority classes. High priority = sent over link first

## Slide 28: Packet Scheduling
Scheduling is used to determine the next packet to send on the link
Round robin weighted fair queueing: packets are classified into priority classes. Each class gets to send one packet during a “cycle”
Packet from the priority group gets sent
Packet from the middle class gets sent Packet from the plebian class gets sent

## Slide 29: IP addressing, IPv4, and IPv6
https://www.rfc-editor.org/rfc/rfc791

## Slide 30: IPv4: 32-bit addresses (decimal)
Packets traversing through the network layer are referred to as a datagram. Each packet gets an IPv4/IPv6 header
Message
Transport
Layer Header
IP Header
Transport Layer Header
Message
IPv4 Header
192.149.252.76
IPv6: 64-bit addresses (hexademical)
3ffe:1900:fe21:4545::
Why do we need IPv6?

## Slide 31: Announcements
NO CLASS this Friday (10/14) and next Monday (10/17)
You can always email/DM me if you have questions
PA2 due in one week (10/19)
Put time.sleep() commands after you send() to prevent weird timing errors

## Slide 32: Packets traversing through the network layer are referred to as a datagram. Each packet gets an IPv4/IPv6 header
Message
Transport
Layer Header
IP Header
Transport Layer Header
Message
IPv4 Header
TCP header = 20 bytes IP header = 20 bytes

## Slide 33
IP Address: Globally unique* 32 bit (4 byte) dotted decimal number assigned to interfaces on hosts and routers
193.32.216.9

## Slide 34: IP Address: Globally unique* 32 bit (4 byte) dotted decimal number assigned to interfaces on hosts and routers
193.32.216.9
4 bytes
4 bytes 4 bytes
4 bytes
(1 byte = 8 bits)
128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
1 | 1 | 0 | 0 | 0 | 0 | 0 | 1
128 + 64 + 1 = 193
193 = 11000001 in binary

## Slide 35
IP Address: Globally unique* 32 bit (4 byte) dotted decimal number assigned to interfaces on hosts and routers
193.32.216.9
=
11000001 00100000 11011000 00001001
(1 byte = 8 bits)
How many addresses are possible with a 32 bit number? ~4 billion possible IPv4 addresses

## Slide 36: 223.1.2.1
223.1.1.4
223.1.2.9
223.1.3.27
223.1.2.2
223.1.1.2
223.1.1.1
Subnet is a logical subdivision of an IP network
223.1.1.3
223.1.3.2
223.1.3.1

## Slide 37: 223.1.2.1
223.1.1.4
223.1.1.3
223.1.3.2
223.1.3.1
223.1.2.9
223.1.3.27
223.1.2.2
223.1.1.2
223.1.1.1
Subnet is a logical subdivision of an IP network In this network, we have 3 subnets

## Slide 38
223.1.1.4
223.1.2.9
223.1.3.27
223.1.2.1
223.1.2.2
223.1.3.1
223.1.3.2
223.1.1.3
223.1.1.2
223.1.1.1
IP addresses on the same subnet share a common prefix
38
Hosts on the same subnet can reach each other without going through a router
Subnet is a logical subdivision of an IP network In this network, we have 3 subnets
Computers usually have 1
interface. Routers have many
Devices usually have a private IP address, and a public IP address

## Slide 39
223.1.1.253
223.1.1.2
223.1.1.1
…
It is very common to have a range of IP addresses assigned to you (random assignment would be chaos)
Subnet mask
223.1.1.0/24
The leftmost 24 bits represent the prefix of the subnet
11111111 11111111 11111111 XXXXXXXX = 255.255.255.0
223.1.1.67
223.2.1.67
223.2.1.255
193.32.216.9
11000001 00100000 11011000 00001001
Host bits
Network bits

## Slide 40: Computers usually have 1 interface. Routers have many
223.1.1.0/24 223.1.2.0/24
223.1.3.0/24
Subnet is a logical subdivision of an IP network In this network, we have 3 subnets

## Slide 41: 6 subnets
1. 223.1.1.0/24
2. 223.1.7.0/24
3. 223.1.3.0/24
4. 223.1.8.0/24
5. 223.1.2.0/24
6. 223.1.9.0/23

## Slide 42: 223.1.1.0/24
Managing and Assigning Subnets
The subnet
contains the following addresses
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.1.5
…
223.1.1.252
223.1.1.253
223.1.1.254
How many addresses does a /24 subnet provide?
0 and 255 are reserved for special services (?)

## Slide 43: 223.1.1.0/24
Managing and Assigning Subnets
The subnet
contains the following addresses
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.1.5
…
223.1.1.252
223.1.1.253
223.1.1.254
How many addresses does a /24 subnet provide?
2^8 – 2 = 253
Class C network
0 and 255 are reserved for special services (?)

## Slide 44: Managing and Assigning Subnets
Subnet Type | Slash | Subnet Mask | Available Addresses
Class A | /8 | 255.0.0.0 | 2^24 – 2 = 16777216
Class B | /16 | 255.255.0.0 | 2^16 – 2 = 65,634
Class C | /24 | 255.255.255.0 | 2^8 – 2 = 254
Issues with this type of assignment?

## Slide 45: Managing and Assigning Subnets
Subnet Type | Slash | Subnet Mask | Available Addresses
Class A | /8 | 255.0.0.0 | 2^24 – 2 = 16777216
Class B | /16 | 255.255.0.0 | 2^16 – 2 = 65,634
Class C | /24 | 255.255.255.0 | 2^8 – 2 = 254
If I have 2000 devices, I will either need 8 class C subnets or 1 class B
subnet (but waste 63,000ish IP addresses)
We need a better way to subnet!

## Slide 46: Managing and Assigning Subnets
Our only available subnet masks have been:
255.255.255.0 | 11111111 11111111 11111111 00000000
255.255.0.0 | 11111111 11111111 00000000 00000000
255.0.0.0 | 11111111 00000000 00000000 00000000
CIDR introduces a more flexible way for subnetting We can any number of bits for our mask
Host bits!
200.23.16.0/20 = 11001000.00010111.00010000.00000000
Mask = 11111111.11111111.11110000.00000000
/24
/16
/8

## Slide 47: ISPs can now group and advertise organizations by IP blocks
We once again have another hierarchy 

## Slide 48
ISP’s block | 200.23.16.0/20 | 11001000 00010111 00010000 00000000
Organization 0 | 200.23.16.0/23 | 11001000 00010111 00010000 00000000
Organization 1 | 200.23.18.0/23 | 11001000 00010111 00010010 00000000
Organization 2 | 200.23.20.0/23 | 11001000 00010111 00010100 00000000
… |  | 
Organization 7 | 200.23.30.0.23 | 11001000 00010111 00011110 00000000
One possible way an ISP could organize IP blocks

## Slide 49: Devices on the same subnet communicate with each other by broadcasting a special message
223.1.3.27
223.1.1.2
223.1.1.3
223.1.3.2
223.1.3.1
223.1.1.1
This special message is when the source IP address of some packet is 255.255.255.255
223.1.1.4

## Slide 50: Devices on the same subnet communicate with each other by broadcasting a special message
223.1.1.4
223.1.3.27
223.1.1.2
223.1.1.1
This special message is when the source IP address of some packet is 255.255.255.255
255.255.255.255
(This request can sometimes be echoed to
neighboring subnets)
223.1.1.3
223.1.3.2
223.1.3.1

## Slide 51: How do IPs get obtained/assigned?
The Internet Corporation for Assigned Names and Numbers (ICANN) is responsible for managing and allocating IP address space for ISPs and organizations
(they also manage the DNS root servers!)
When an organization gets a range of IP addresses to use, how to we give assign them to devices?
Do we do it manually?
we could….

## Slide 52: DHCP
Dynamic Host Configuration Protocol (DHCP) is a plug-and-play, client-server protocol that allows a host to obtain an IP address automatically
When a host is automatically assigned an IP address, it might keep that one forever, or the IP addresses can be temporary
(more common)

## Slide 53: This process is similar to a TCP handshake!
Broadcast gets sent to all devices on the subnet!!
But devices that are not the dhcp server will ignore it

## Slide 54
This process is similar to a TCP handshake!

## Slide 55
This process is similar to a TCP handshake!

## Slide 56
Announcements
If I haven’t responded to a DM/email, please poke me about it
PA2 due on Friday 10/21
I will allow you to submit it any time this weekend with no late penalty (no late pass required!)
Lecture will be asynchronous (recorded) on Monday
PA2: Flow Demo, FIN ACKs

## Slide 57
NAT (Network Address Translation)
NAT is a translation of multiple private IP addresses to one single public IP address

## Slide 58
NAT (Network Address Translation)
NAT is a translation of multiple private IP addresses to one single public IP address
Hides details of inner home network from outside world
All incoming traffic will have same public IP, all outgoing will have same public IP
Routers get assigned their one public IP address through DHCP!

## Slide 59: Packets traversing through the network layer are referred to as a datagram. Each packet gets an IPv4/IPv6 header
Message
Transport
Layer Header
IP Header
Transport Layer Header
Message
IPv6 Header
TCP header = 20 bytes IP header = 20 bytes
IPv6 = 128 bits
(not 64)
(128 bits)
(128 bits)
The goal is for our internet to be only using IPv6 in the near future? Issues?

## Slide 60
flow: X
src: A
dest: F
data
A-to-B:
IPv6
Flow: X
Src: A
Dest: F
data
src:B
dest: E
B-to-C:
IPv6 inside
IPv4
physical view:
A
B
IPv6
IPv6
E
IPv6
IPv6
F
C
D
logical view:
IPv4 tunnel
connecting IPv6 routers
E
IPv6
IPv6
F
A
B
IPv6
IPv6
Tunneling
IPv4
IPv4
4-60
E-to-F:
IPv6
flow: X
src: A
dest: F
data
B-to-C:
IPv6 inside
IPv4
Flow: X
Src: A
Dest: F
data
src:B
dest: E

## Slide 61: Generalized Forwarding and Software Defines Network (SDN)
So far, a router takes input from input port, and then outputs on some output port
What else might a router need to do?

## Slide 62: Generalized Forwarding and Software Defines Network (SDN)
So far, a router takes input from input port, and then outputs on some output port
What else might a router need to do?
Forward, Drop stuff, Modify, Load balance
We need more flexibility and functionality with our forwarding!!

## Slide 63: Generalized Forwarding and Software Defines Network (SDN)
OpenFlow standard
We need headers/rules, which are going to the values the remote controller is going to evaluate
We need actions to do based on some pattern match

## Slide 64: Generalized Forwarding and Software Defines Network (SDN)

## Slide 65: Generalized Forwarding and Software Defines Network (SDN)

## Slide 66: Generalized Forwarding and Software Defines Network (SDN)

## Slide 67: Generalized Forwarding and Software Defines Network (SDN)

## Slide 68: Generalized Forwarding and Software Defines Network (SDN)
22