## Slide 1: CSCI 466: Networks Link Layer
Reese Pearsall Fall 2022
https://www.cs.montana.edu/pearsall/classes/fall2022/466/main.html
1
*All images are stolen from the internet

## Slide 2: Announcements
NO CLASS next Friday 11/11
Might have to also cancel next Monday (11/7)*

## Slide 3
Application Layer
Presentation Layer
Session Layer
Transport Layer
Network Layer
Data Link Layer
Physical Layer
OSI Model
Messages from Network Applications
Application Layer
Physical Layer
Bits being transmitted over a copper wire
*In the textbook, they condense it to a 5-layer model, but 7 layers is what is most used
*
*

## Slide 4
Data Link Layer
The link layer is responsible for the actual node-to-node delivery of data and ensure error-free transmission of information
terminology:
hosts and routers: nodes
communication channels that connect adjacent nodes along communication path: links
  wired links
  wireless links
  LANs
layer-2 packet: frame, encapsulates datagram
data-link layer has responsibility of
transferring datagram from one node
to physically adjacent node over a link
We have not addressed how we will overcome various transmission mediums!

## Slide 5
Data Link Layer
Ways to get form US to Paris?
We can visit a travel agent that will give us a travel plan
Take a car to the airport
Take a plane to France
Take a train from Airport to Paris
Take a bus from the train stop to the Eifel tower

## Slide 6
Data Link Layer
Ways to get form US to Paris?
We can visit a travel agent that will give us a travel plan
Take a car to the airport
Take a plane to France
Take a train from Airport to Paris
Take a bus from the train stop to the Eifel tower
Tourist = Datagram
Transportation Segment = Link
Airport, Bus Stop, Train Stop = Node
Transport Mode = Link Layer Protocol
Travel Agent = Routing Protocol (Network Layer)

## Slide 7
Data Link Layer
Services offered by the Link Layer
Framing
       Encapsulate a network layer Datagram in another header
Link access
 LL dictate the rules and process of transmitting a frame over a link
Reliable Delivery
 For unreliable link, some reliable delivery mechanisms may need to be used
Error Detection and Correction
 Bits can get messed up as the are transmitted through a medium
Why do we need RDT and error detection in the link layer when it is also offered in the transport layer?

## Slide 8
Data Link Layer
Services offered by the Link Layer
Framing
       Encapsulate a network layer Datagram in another header
Link access
 LL dictate the rules and process of transmitting a frame over a link
Reliable Delivery
 For unreliable link, some reliable delivery mechanisms may need to be used
Error Detection and Correction
 Bits can get messed up as the are transmitted through a medium
Why do we need RDT and error detection in the link layer when it is also offered in the transport layer?
Some packets of data don’t even travel through the transport layer…

## Slide 9
Data Link Layer
Implementation of Link Layer
Implemented within the hardware of your computer
NIC (Network Interface Controller)- Integrated into the motherboard and allows the machine to use LL services such as ethernet (combination of hardware, software, and some firmware)
controller
physical
transmission
cpu
memory
host
bus
(e.g., PCI)
network adapter
card
application
transport
network
link
link
physical
Wireshark uses your NIC to determine which packets should be sniffed!

## Slide 10
Data Link Layer
sending side:
  encapsulates datagram in frame
  adds error checking bits, rdt, flow control, etc.
receiving side
  looks for errors, rdt, flow control, etc.
  extracts datagram, passes to upper layer at receiving side
controller
controller
sending host
receiving host
datagram
datagram
datagram
frame
6-10
Link Layer and LANs

## Slide 11
Data Link Layer
6-11
Link Layer and LANs
Bits can get messed during the physical layer and link layer
Faulty wires
NIC issues
Unreliable mediums
The Data Link Layer implements services for detecting and correcting errors
EDC= Error Detection and Correction bits D = Data protected by error checking, may include header fields
Error detection not 100% reliable!
  protocol may miss some errors, but rarely
  larger EDC field yields better detection and correction
otherwise

## Slide 12
Data Link Layer
6-12
Link Layer and LANs
Single bit parity:
Detect single bit errors
Is the number of 1s odd (0) or even (1) ? (Including the parity bit)
Data
01110001001010110
The receiver counts eight 1s, but the parity bit tells us it should be an odd number of 1s  ERROR DETECTED

## Slide 13
Data Link Layer
6-13
Link Layer and LANs
Single bit parity:
Detect single bit errors
Is the number of 1s odd (0) or even (1) ? (Including the parity bit)
Data
01110001001010110
The receiver counts eight 1s, but the parity bit tells us it should be an odd number of 1s  ERROR DETECTED
Two-dimensional bit parity:
Detect and correct single bit errors

## Slide 14
Data Link Layer
Checksum
0110011001100000
0101010101010101
1000111100001100
0100101011000010
1011010100111101
(one’s complement)
Binary sum of words
Checksum!
(Sender)
(Receiver)
0110011001100000
0101010101010101
1000111100001100
0100101011000010
(Binary Sum  One’s Complement)
= 1111111111111111
All 1s = No error!

## Slide 15
Data Link Layer
6-15
more powerful error-detection coding
view data bits, D, as a binary number
choose r+1 bit pattern (generator), G
goal: choose r CRC bits, R, such that
  <D,R> exactly divisible by G (modulo 2)
  receiver knows G, divides <D,R> by G. If non-zero remainder: error detected!
  can detect all burst errors less than r+1 bits
widely used in practice (Ethernet, 802.11 WiFi, ATM)
Sender/Receiver has D and G. Need to compute R

## Slide 16
Data Link Layer
6-16
more powerful error-detection coding
view data bits, D, as a binary number
choose r+1 bit pattern (generator), G
goal: choose r CRC bits, R, such that
  <D,R> exactly divisible by G (modulo 2)
  receiver knows G, divides <D,R> by G. If non-zero remainder: error detected!
  can detect all burst errors less than r+1 bits
widely used in practice (Ethernet, 802.11 WiFi, ATM)
Sender/Receiver has D and G. Need to compute R

## Slide 17
Data Link Layer
6-17
(Do some algebra to find R)
R = remainder[ ]
D.2r
G
Sender sends D + R bits.
Receiver divides D + R bits by G. Result should always be Zero if no errors occured

## Slide 18
Data Link Layer
6-18
Access links
Point to Point – Single sender, Single Receiver at each end of link
Broadcast – shared medium
shared wire (e.g.,
cabled Ethernet)
shared RF
(e.g., 802.11 WiFi)
shared RF
(satellite)
humans at a
cocktail party
(shared air, acoustical)

## Slide 19
Data Link Layer
6-19
MAC (Media Access Control) Addresses
32-bit IP address:
  network-layer address for interface
  used for layer 3 (network layer) forwarding
MAC (or LAN or physical or Ethernet) address:
  function: used ‘locally” to get frame from one interface to another physically-connected interface (same network, in IP-addressing sense)
  48 bit MAC address (for most LANs) burned in NIC ROM, also sometimes software settable
  e.g.: 1A-2F-BB-76-09-AD
hexadecimal (base 16) notation
(each “numeral” represents 4 bits)
MAC Address is your SSN, IP address is your Postal code 
How do we know two NICs wont have the same MAC address?

## Slide 20
Data Link Layer
6-20
adapter
1A-2F-BB-76-09-AD
58-23-D7-FA-20-B0
0C-C4-11-6F-E3-98
71-65-F7-2B-08-53
LAN
(wired or
wireless)

## Slide 21: Announcements
NO CLASS next Friday 11/11
Monday November 4th = WORK DAY (No lecture)
Input files + sample output for PA3 are on the website

## Slide 22: Multiple Access Links
Shared medium = possibility for receivers to get two frame at the same time, AKA a collision
Frame X
Frame y
Frames get tangled together, and neither frame can be read clearly by receiver

## Slide 23: Multiple Access Links
Shared medium = possibility for receivers to get two frame at the same time, AKA a collision
Frame X
Frame y
Frames get tangled together, and neither frame can be read clearly by receiver
In English, we have some rules to prevent collisions from happening
In the link layer, we will discuss 3 multiple access protocols:
Channel Partitioning, Random Access, and Taking Turns

## Slide 24: Multiple Access Links
Shared medium = possibility for receivers to get two frame at the same time, AKA a collision
Frame X
Frame y
Frames get tangled together, and neither frame can be read clearly by receiver
In English, we have some rules to prevent collisions from happening
In the link layer, we will discuss 3 multiple access protocols:
Channel Partitioning, Random Access, and Taking Turns
  1. When one node wants to transmit, it can send at rate R:
  2. When M nodes want to transmit, each can send at average rate R/M
  3. Fully decentralized:
    no special node to coordinate transmissions
    no synchronization of clocks, slots
  4. simple
Ideally

## Slide 25: Channel Partitioning
A
B
C
D
N nodes
A
B
C
D
Links total bandwidth = D
Divide channel into N slots
Each node gets (on average) D/N bandwidth
Get to transmit data for a fixed amount of time, and then next node gets to transmit

## Slide 26: Channel Partitioning
A
B
C
D
N nodes
A
B
C
D
Links total bandwidth = D
Divide channel into N slots
Each node gets (on average) D/N bandwidth
Get to transmit data for a fixed amount of time, and then next node gets to transmit

## Slide 27: Channel Partitioning
A
B
C
D
N nodes
A
B
C
D
Links total bandwidth = D
Divide channel into N slots
Each node gets (on average) D/N bandwidth
Get to transmit data for a fixed amount of time, and then next node gets to transmit

## Slide 28: Channel Partitioning
A
B
C
D
N nodes
A
B
C
D
Links total bandwidth = D
Divide channel into N slots
Each node gets (on average) D/N bandwidth
Get to transmit data for a fixed amount of time, and then next node gets to transmit

## Slide 29: Channel Partitioning
A
B
C
D
N nodes
A
B
C
D
Links total bandwidth = D
Divide channel into N slots
Each node gets (on average) D/N bandwidth
Get to transmit data for a fixed amount of time, and then next node gets to transmit

## Slide 30: Channel Partitioning
A
B
C
D
N nodes
A
B
C
D
Links total bandwidth = D
Divide channel into N slots
Each node gets (on average) D/N bandwidth
Get to transmit data for a fixed amount of time, and then next node gets to transmit

## Slide 31: Channel Partitioning
A
B
C
D
N nodes
A
B
C
D
Links total bandwidth = D
Divide channel into N slots
Each node gets (on average) D/N bandwidth
Get to transmit data for a fixed amount of time, and then next node gets to transmit

## Slide 32: Channel Partitioning
A
B
C
D
N nodes
A
B
C
D
Links total bandwidth = D
Divide channel into N slots
Each node gets (on average) D/N bandwidth
Get to transmit data for a fixed amount of time, and then next node gets to transmit

## Slide 33: Channel Partitioning
A
B
C
D
N nodes
A
B
C
D
Links total bandwidth = D
Divide channel into N slots
Each node gets (on average) D/N bandwidth
Get to transmit data for a fixed amount of time, and then next node gets to transmit

## Slide 34: Random Access
Collisions will occur, but we will try to recover from them
Slotted ALOHA: Divide up time into discrete L/R “slots”
L = size of frame
R = Bandwidth
L/R = Time needed to transmit one frame
L/R
2 L/R
3 L/R
…
If collisions occur, the colliding nodes will flip a coin to see who should retransmit
Can only transmit frames at beginning of slots. If collision occurs, the nodes can detect collision before the slot ends

## Slide 35: Random Access
Collisions will occur, but we will try to recover from them
Slotted ALOHA: Divide up time into discrete L/R “slots”
L = size of frame
R = Bandwidth
L/R = Time needed to transmit one frame
L/R
2 L/R
3 L/R
…
If collisions occur, the colliding nodes will flip a coin to see who should retransmit
Collision

## Slide 36: Random Access
Collisions will occur, but we will try to recover from them
Slotted ALOHA: Divide up time into discrete L/R “slots”
L = size of frame
R = Bandwidth
L/R = Time needed to transmit one frame
L/R
2 L/R
3 L/R
…
If collisions occur, the colliding nodes will flip a coin to see who should retransmit
Collision
Do some probability p and retransmit if needed

## Slide 37: Random Access
Collisions will occur, but we will try to recover from them
Slotted ALOHA: Divide up time into discrete L/R “slots”
L = size of frame
R = Bandwidth
L/R = Time needed to transmit one frame
L/R
2 L/R
3 L/R
…
If collisions occur, the colliding nodes will flip a coin to see who should retransmit
Collision
Empty
Collision
Waiting a random delay

## Slide 38: Random Access
Collisions will occur, but we will try to recover from them
Slotted ALOHA: Divide up time into discrete L/R “slots”
L = size of frame
R = Bandwidth
L/R = Time needed to transmit one frame
L/R
2 L/R
3 L/R
…
If collisions occur, the colliding nodes will flip a coin to see who should retransmit
Collision
Empty
Collision
Waiting a random delay
Waiting a random delay
Success

## Slide 39: Random Access
Collisions will occur, but we will try to recover from them
Slotted ALOHA: Divide up time into discrete L/R “slots”
L = size of frame
R = Bandwidth
L/R = Time needed to transmit one frame
L/R
2 L/R
3 L/R
…
If collisions occur, the colliding nodes will flip a coin to see who should retransmit
Collision
Empty
Collision
Waiting a random delay
Waiting a random delay
Success
Empty
Collision
Waiting a random delay

## Slide 40: Random Access
Collisions will occur, but we will try to recover from them
Slotted ALOHA: Divide up time into discrete L/R “slots”
L = size of frame
R = Bandwidth
L/R = Time needed to transmit one frame
L/R
2 L/R
3 L/R
…
If collisions occur, the colliding nodes will flip a coin to see who should retransmit
Collision
Empty
Collision
Waiting a random delay
Waiting a random delay
Success
Empty
Collision
Waiting a random delay
Success

## Slide 41: Random Access
Collisions will occur, but we will try to recover from them
Slotted ALOHA: Divide up time into discrete L/R “slots”
L = size of frame
R = Bandwidth
L/R = Time needed to transmit one frame
L/R
2 L/R
3 L/R
…
If collisions occur, the colliding nodes will flip a coin to see who should retransmit
Collision
Empty
Collision
Waiting a random delay
Waiting a random delay
Success
Empty
Collision
Waiting a random delay
Success
Success

## Slide 42: Taking Turns
Token Passing
Nodes are connected in a circular manner, and pass a special frame (token) between each other
Can only transmit messages if you have the token

## Slide 43: LAN
Local Area Network (LAN)- A collection of devices in one physical location, typically that share a centralized internet connection
Router
Switch

## Slide 44: ARP
Protocol for mapping IP Addresses to MAC addresses
Used only for hosts and router interfaces on the same subnet
If the entry does not exist in the table, construct and send an ARP packet
First the machine checks its ARP table
Broadcasts the ARP packet to all interfaces on the LAN (255.255.255.255)
These tables are self-updated, and do not require manual entry*

## Slide 45: ARP
A wants to send datagram to B
  B’s MAC address not in A’s ARP table.
A broadcasts ARP query packet, containing B's IP address
  destination MAC address = FF-FF-FF-FF-FF-FF
  all nodes on LAN receive ARP query
B receives ARP packet, replies to A with its (B's) MAC address
  frame sent to A’s MAC address (unicast)
A caches (saves) IP-to-MAC address pair in its ARP table until information becomes old (times out)
  soft state: information that times out (goes away) unless refreshed
ARP is “plug-and-play”:
  nodes create their ARP tables without intervention from net administrator

## Slide 46: Putting it Together: Sending from LAN to LAN
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
IP
Eth
Phy
IP src: 111.111.111.111
IP dest: 222.222.222.222
A creates IP datagram with IP source A, destination B
A creates link-layer frame with R's MAC address as destination address, frame contains A-to-B IP datagram
MAC src: 74-29-9C-E8-FF-55
MAC dest: E6-E9-00-17-BB-4B
6-48
Link Layer and LANs

## Slide 47: Putting it Together: Sending from LAN to LAN
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
IP
Eth
Phy
IP src: 111.111.111.111
IP dest: 222.222.222.222
A creates IP datagram with IP source A, destination B
A creates link-layer frame with R's MAC address as destination address, frame contains A-to-B IP datagram
MAC src: 74-29-9C-E8-FF-55
MAC dest: E6-E9-00-17-BB-4B
6-47
Link Layer and LANs

## Slide 48: Putting it Together: Sending from LAN to LAN
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
IP src: 111.111.111.111
IP dest: 222.222.222.222
R forwards datagram with IP source A, destination B
R creates link-layer frame with B's MAC address as destination address, frame contains A-to-B IP datagram
MAC src: 1A-23-F9-CD-06-9B
MAC dest: 49-BD-D2-C7-56-2A
IP
Eth
Phy
IP
Eth
Phy
Link Layer and LANs

## Slide 49: Putting it Together: Sending from LAN to LAN
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
R forwards datagram with IP source A, destination B
R creates link-layer frame with B's MAC address as dest, frame contains A-to-B IP datagram
IP src: 111.111.111.111
IP dest: 222.222.222.222
MAC src: 1A-23-F9-CD-06-9B
MAC dest: 49-BD-D2-C7-56-2A
IP
Eth
Phy

## Slide 50: Ethernet
“dominant” wired LAN technology:
single chip, multiple speeds (e.g., Broadcom BCM5761)
first widely used LAN technology
simpler, cheap
kept up with speed race: 10 Mbps – 10 Gbps
Metcalfe’s Ethernet sketch

## Slide 51: Ethernet
switch
bus: coaxial cable
star
Link Layer and LANs
Ethernet Topology
(outdated)

## Slide 52
Ethernet frame structure
sending adapter encapsulates IP datagram (or other network layer protocol packet) in Ethernet frame
preamble:
7 bytes with pattern 10101010 followed by one byte with pattern 10101011
used to synchronize receiver, sender clock rates
dest.
address
source
address
data (payload)
CRC
preamble
type

## Slide 53: Ethernet frame structure (more)
addresses: 6 byte source, destination MAC addresses
  if adapter receives frame with matching destination address, or with broadcast address (e.g. ARP packet), it passes data in frame to network layer protocol
  otherwise, adapter discards frame
type: indicates higher layer protocol (mostly IP but others possible, e.g., Novell IPX, AppleTalk)
CRC: cyclic redundancy check at receiver
  error detected: frame is dropped
dest.
address
source
address
data (payload)
CRC
preamble
type

## Slide 54
Ethernet switch
Switches will store and forward ethernet frames
Hosts have dedicated, direct connection to switch
Ethernet protocol used on each incoming link, but no collisions between links
Switching: A-A’ and B-B’ can transmit simultaneously, without collisions
Transparent: Hosts are not aware
they are connected to a switch
Plug and play; self-learning
A
A’
B
B’
C
C’
1
2
3
4
5
6
= ethernet cable

## Slide 55
Switches vs. routers
both are store-and-forward:
routers: network-layer devices (examine network-layer headers)
switches: link-layer devices (examine link-layer headers)
both have forwarding tables:
routers: compute tables using routing algorithms, IP addresses
switches: learn forwarding table using flooding, learning, MAC addresses
application
transport
network
link
physical
network
link
physical
link
physical
switch
datagram
application
transport
network
link
physical
frame
frame
frame
datagram

## Slide 56
Multiprotocol
Label
Switching
Label Switch Router = LSR
This is a layer 2.5 protocol (between network layer and link layer)

## Slide 57: The End of the OSI Model…
We have reached the end of the OSI, now lets review…

## Slide 63
OK.. So that was just DHCP

## Slide 68
Whew… ok we can now address something to the DNS server

## Slide 72
We are finally ready to contact the google server!