## Slide 1: CSCI 466: Networks Review
Reese Pearsall Fall 2022
https://www.cs.montana.edu/pearsall/classes/fall2022/466/main.html
1
*All images are stolen from the internet

## Slide 2: Announcements
No lecture on Wednesday. Workday for PA4. I’ll be in Reid 202 during class time if you need help
Homework 4 due Friday @ 11:59 PM
PA4 due Sunday @ 11:59 PM (We are currently at 49% response rate)
Final Exam: Wednesday December 14th 12:00 – 1:50 PM (same room)

## Slide 3: Final Exam Structure
No notes allowed
A curve won’t be applied (unless needed)
15% of your grade
Please show up
Part I. OSI Model
For each layer
Name the layer (Ex. Network Layer)
Provide a primary responsibility/functionality (Ex. Forwarding and Routing)
Provide the unit of data that is being transmitted (Ex. Datagram)
Part II. Short answer questions (~18)
I will pull some of these questions straight from the homeworks (HW1, HW2, HW3)
You can expect 2-4 questions from each the following sections
Internet Structure
Application Layer
Transport Layer
Network Layer (Data Plane)
Network Layer (Control Plane)
Link Layer
Network Security

## Slide 4: Internet Structure
Devices that are connected to network are called hosts or end systems
Two types: Clients and Servers
End systems are connected together by a network of communication links and packet switches/routers
The network edge consists of end systems
The network core consists routers and other packet switches (usually owned by an ISP)

## Slide 5: Internet Structure
Devices that are connected to network are called hosts or end systems
Two types: Clients and Servers
End systems are connected together by a network of communication links and packet switches/routers
The network edge consists of end systems
The network core consists routers and other packet switches (usually owned by an ISP)

## Slide 6: Internet Structure
Devices that are connected to network are called hosts or end systems
Two types: Clients and Servers
End systems are connected together by a network of communication links and packet switches/routers
The network edge consists of end systems
The network core consists routers and other packet switches (usually owned by an ISP)

## Slide 7: Internet Structure
Devices that are connected to network are called hosts or end systems
Two types: Clients and Servers
End systems are connected together by a network of communication links and packet switches/routers
The network edge consists of end systems
The network core consists routers and other packet switches (usually owned by an ISP)

## Slide 8: Internet Structure
Devices that are connected to network are called hosts or end systems
Two types: Clients and Servers
End systems are connected together by a network of communication links and packet switches/routers
The network edge consists of end systems
The network core consists routers and other packet switches (usually owned by an ISP)

## Slide 9: Internet Structure
The internet is hierarchical. We access the internet through an ISP, which typically belong to a larger network
Big ISP : 192.xxx.xxx.xxx
Sub ISP: 192.42.xxx.xxx
Sub ISP: 192.42.221.xxx

## Slide 10: Internet Structure
“Client”
“Server”
Client-server architecture
Clients do not directly interact with each other.
Hosts communicate with a dedicated, always online server that acts as a middleman between two hosts. Servers are usually hosted in a data center
P2P Architecture
No reliance on a dedicated server
Each endpoint has same power and responsibilities.
Endpoints can be both a server and an endpoint
+ Easier to administer
+ More secure
+ Ability to back up data
Potential single point of failure
Expensive
Distance
+ No central server + Availability
+ Self Scaling
Less Secure - ISP Friendliness
More difficult to administer

## Slide 11: Internet Structure
A protocol defines the format and the order of messages exchanges between two or more communicating entities, as well as the actions taken on the transmission and/or receipt of the message or event
The rules and details are always specific in an RFC

## Slide 12: Internet Structure
(A lot of factors affect throughput)
You won’t need to calculate these values on the final exam, but you should have an understanding of what they measure and the meaning of that value
Round time trip

## Slide 13: Application Layer
The layer which interacts directly with applications and provide necessary protocols and services for web applications. Specifies the shared commination protocol(s) that will be used by hosts in a communication protocol
Humans interact through the application layer. Application layer also provides engineers an interface and methods for web communication
HyperText Transfer Protocol (HTTP)- protocol that dictates the transmitting of hypermedia documents, such as HTML and other webpage objects

## Slide 14: Application Layer
HyperText Transfer Protocol (HTTP)- protocol that dictates the transmitting of hypermedia documents, such as HTML and other webpage objects
On the final exam, you should be able to describe (from a high level) how HTTP works)
We provide the URL for the web resource that we want
HTTP is built on TCP, so an HTTP client will first initiate A TCP connection (port 80) and establish a connection socket and does the TCP handshake
TCP
TCP
The HTTP client sends an HTTP Request to the server via its socket
HTTP Request
HTTP Request

## Slide 15: Application Layer
HyperText Transfer Protocol (HTTP)- protocol that dictates the transmitting of hypermedia documents, such as HTML and other webpage objects
On the final exam, you should be able to describe (from a high level) how HTTP works)
We provide the URL for the web resource that we want
HTTP is built on TCP, so an HTTP client will first initiate A TCP connection (port 80) and establish a connection socket and does the TCP handshake
TCP
TCP
The HTTP client sends an HTTP Request to the server via its socket
HTTP Request
The HTTP server process the request, retrieves the object, and sends it back to the client as an HTTP response
Informational Responses (100s)
Successful Responses (200s)
Redirection messages (300s)
Client error response (400s)
Server error response (500s)
HTTP Response

## Slide 16: Application Layer
HyperText Transfer Protocol (HTTP)- protocol that dictates the transmitting of hypermedia documents, such as HTML and other webpage objects
On the final exam, you should be able to describe (from a high level) how HTTP works)
When you graduate and get your job as a software engineer/web developer, the application you are writing, or the API you are working with will be using HTTP to communicate with other hosts.
It’s important to have an understanding and intuition about what’s going on under the head, and to quickly remember the structure of an HTTP request (GET, URL) and the structure of an HTTP response (200 OK)
Probably someone in this class: Who cares??

## Slide 17: Application Layer
HyperText Transfer Protocol (HTTP)- protocol that dictates the transmitting of hypermedia documents, such as HTML and other webpage objects
On the final exam, you should be able to describe (from a high level) how HTTP works)
Cookies are pieces of information that are exchanged between browsers and web servers to identify users in active connections
Authentication
Tracking & Advertisement
Session Management

## Slide 18: Application Layer
HyperText Transfer Protocol (HTTP)- protocol that dictates the transmitting of hypermedia documents, such as HTML and other webpage objects
On the final exam, you should be able to describe (from a high level) how HTTP works)
A web cache– also called a proxy server– is a network entity that satisfies HTTP requests on the behalf of an origin Web server
* Improves response time (especially if the the cache has the object that is requested)
* The connection from the client to the cache is typically much faster than the connection from client to host server
1. Browser/Client establishes a TCP connection to the Web cache and sends an HTTP request
2. Web cache checks its local storage for the requested object
3. If the web cache does not have the object, establish TCP with an origin server and issue an HTTP request
4. Web cache stores a local copy of the object, then issues an HTTP response with the object

## Slide 19: Application Layer
File Transfer Protocol (FTP)- protocol used for transferring files from server to client
FTP
client
FTP
server
TCP control connection,
server port 21
TCP data connection,
server port 20
FTP communicates over two connections
  Port 21 for control information
  Port 20 for data
Differences from HTTP
  Control communication “out-of-band”
  Server maintains per client state: authentication, current directory
FTP procedure:
  FTP client contacts FTP server at port 21, using TCP
  Client authorized over control connection
  Client browses remote directory, sends commands over control connection
  When server receives file transfer command, server opens 2nd TCP data connection (for file) to client
  After transferring one file, server closes data connection

## Slide 20: Application Layer
DNS is a distributed, hierarchical database used for mapping hostnames to IP address (no DNS server has all the records!)
Prior to creating a TCP connection and sending an HTTP request, we first need to issue a DNS request!
Hierarchy consists of different types of DNS servers:
facebook.com DNS
amazon.com DNS
montana.edu DNS
harvard.edu DNS
Authoritative DNS servers- Organization’s own DNS with up-to-date records
Top-level domain (TLD) servers- responsible for keeping IP addresses for authoritative DNS servers for each top-level domain (.com, .edu, .jp, etc)
.com TLD DNS server
.edu TLD DNS server
root DNS server
(Built on UDP, lookups happen on port 53)
On the final exam, you should be able to describe (from a high level) how DNS works

## Slide 21: Application Layer
DNS is a distributed, hierarchical database used for mapping hostnames to IP address (no DNS server has all the records!)
Prior to creating a TCP connection and sending an HTTP request, we first need to issue a DNS request!
Authoritative DNS servers- Organization’s own DNS with up-to-date records
Top-level domain (TLD) servers- responsible for keeping IP addresses for authoritative DNS servers for each top-level domain (.com, .edu, .jp, etc)
(Built on UDP, lookups happen on port 53)
On the final exam, you should be able to describe (from a high level) what DNS is and how DNS works
example.com
authoritative DNS server
Root DNS servers- responsible for maintaining IP addresses for TLD servers
There are also local DNS servers, and local DNS entries on your machine

## Slide 22: Transport Layer
- Provides host-to-host, reliable data transfer, and dictates the flow of data
Our messages from the application are now divided up into transport layer segments
HTTP Request
DNS Query
TCP Header
Payload
TCP Header
Payload
TCP Header
Payload
TCP Header
Payload
TCP Header
Payload
TCP Header
Payload
UDP Header
Payload
UDP Header
Payload
UDP Header
Payload
UDP Header
Payload
UDP Header
Payload
UDP Header
Payload

## Slide 23: Transport Layer
- Provides host-to-host, reliable data transfer, and dictates the flow of data
Multiplexing is the process of gathering chunks from sockets, encapsulating chunks with header information, and passing the segment into the network layer
Socket
data
data
data
data
data
data
header
header
header
Segment
Demultiplexing is the receiving segments from the transport layer and delivering the segment to the correct socket.
Socket
data
data
data
header
header
header
Socket
Socket

## Slide 24: Transport Layer
- Provides host-to-host, reliable data transfer, and dictates the flow of data
Segments are delivered to a port (which a socket is linked to)
Port 1
Port 2
Port 3
….
Port 80
Port N
80
Different services/protocols are linked to different ports
Service | Port
HTTP | 80
HTTPS | 443
DNS | 53
FTP | 20 and 21
SSH | 22
BGP | 179
These are some common ports you should really know for the final exam 

## Slide 25: Transport Layer
- Provides host-to-host, reliable data transfer, and dictates the flow of data

## Slide 26: Transport Layer
- Provides host-to-host, reliable data transfer, and dictates the flow of data

## Slide 27: Transport Layer
- Provides host-to-host, reliable data transfer, and dictates the flow of data
It would be very helpful for you to review these 

## Slide 28: Transport Layer
- Provides host-to-host, reliable data transfer, and dictates the flow of data

## Slide 29: Transport Layer
- Provides host-to-host, reliable data transfer, and dictates the flow of data
TCP sends back amount of available buffer space in the receiver
This helps make sure we don’t overwhelm the receiver
TCP is self-clocking, which means it will control itself if it notices congestion in a network
-See how many dropped packets we are getting
-Amount of duplicate ACKs received
-Amount of UnAcked packets
The timeout value for TCP is dynamically calculated by looking at RTT values for packets

## Slide 30: Transport Layer
- Provides host-to-host, reliable data transfer, and dictates the flow of data
Given a scenario and application requirements, you should be able to pick between UDP and TCP and give a reasonable justification for your choice

## Slide 31: Network Layer
- Provides Routing and Forwarding Functionality
Routing: determine route taken by packets from source to destination
Forwarding: move packets from router’s input to appropriate router output
Our segments from the transport layer are now encapsulated into network layer datagrams
TCP Header
Payload
IP Header

## Slide 32: Network Layer
- Provides Routing and Forwarding Functionality
Destination-based forwarding
  Forwarding decisions are based on the destination of the packet
Generalized forwarding
  Forwarding decisions based on any set of header field values

## Slide 33: Network Layer
- Provides Routing and Forwarding Functionality
Destination-based forwarding
  Forwarding decisions are based on the destination of the packet
Lookup, forwarding, queueing
…
…
Address range | Interface (output link)
128.11.52.0 – 128.11.52.255 | 1
153.90.2.0 – 153.90.2.255 | 2
153.90.2.87 – 153.90.2.89 | 3
Routing Table
Routing Tables are maintained internally, and help make forwarding decisions
Address range | Interface (output link)
11001000 00010111 00010*** ********* | 1
11001000 00010111 00011000 ********* | 2
11001000 00010111 00011*** ******** | 3
otherwise | 4
Longest prefix matching
when looking for forwarding table entry for given destination address, use longest address prefix that matches destination address

## Slide 34: Network Layer
- Provides Routing and Forwarding Functionality
Address range | Interface (output link)
128.28.XXX.XXX | 1
128.27.XXX.XXX | 2
Longest prefix matching
when looking for forwarding table entry for given destination address, use longest address prefix that matches destination address
Address range | Interface (output link)
128.28.113.XXX | 1
128.28.114.XXX | 2
Address range | Interface (output link)
128.27.1.XXX | 1
128.27.2.XXX | 2
BIG ISP
Smaller ISP
Smaller ISP
Address range | Interface (output link)
128.28.114.23 | 1
128.27.114.16 | 2
128.27.114.44 | 3
Address range | Interface (output link)
128.28.113.1 | 1
128.27.113.2 | 2
128.27.113.3 | 3
Even Smaller ISP
Even Smaller ISP

## Slide 35: Network Layer
- Provides Routing and Forwarding Functionality
IP Address: Globally unique* 32 bit (4 byte) dotted decimal number assigned to interfaces on hosts and routers
193.32.216.9
=
11000001 00100000 11011000 00001001
128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
1 | 1 | 0 | 0 | 0 | 0 | 0 | 1
128 + 64 + 1 = 193
193 = 11000001 in binary
(Think of this as your ZIP code)

## Slide 36: Network Layer
- Provides Routing and Forwarding Functionality
IP Protocol
IPv4
IPv6
IPv4: 32-bit addresses (decimal)
192.149.252.76
IPv6: 128-bit addresses (hexademical)
3ffe:1900:fe21:4545::
On the final exam, you should know the difference between IPv4 and IPv6, and why we need IPv6

## Slide 37: Network Layer
- Provides Routing and Forwarding Functionality
223.1.1.4
223.1.2.9
223.1.3.27
223.1.2.1
223.1.2.2
223.1.1.2
223.1.1.1
Subnet is a logical subdivision of an IP network
223.1.1.3
223.1.3.2
223.1.3.1

## Slide 38
223.1.1.4
223.1.2.9
223.1.3.27
223.1.2.1
223.1.2.2
223.1.3.1
223.1.3.2
223.1.1.3
223.1.1.2
223.1.1.1
IP addresses on the same subnet share a common prefix
Hosts on the same subnet can reach each other without going through a router
Subnet is a logical subdivision of an IP network In this network, we have 3 subnets
Computers usually have 1
interface. Routers have many
Devices usually have a private IP address, and a public IP address

## Slide 39: Network Layer
223.1.1.253
223.1.1.2
223.1.1.1
…
It is very common to have a range of IP addresses assigned to you (random assignment would be chaos)
Subnet mask
223.1.1.0/24
The leftmost 24 bits represent the prefix of the subnet
11111111 11111111 11111111 XXXXXXXX = 255.255.255.0
223.1.1.67
223.2.1.67
223.2.1.255
193.32.216.9
11000001 00100000 11011000 00001001
Host bits
Network bits
- Provides Routing and Forwarding Functionality
(We can have /8, /16, /1, /2, /3, etc)
The number of host bits available controls the amount of IP addresses available to you
(more host bits = more available IP addresses)

## Slide 40: Network Layer
Dynamic Host Configuration Protocol (DHCP) is a plug-and-play, client-server protocol that allows a host to obtain an IP address automatically
When a host is automatically assigned an IP address, it might keep that one forever, or the IP addresses can be temporary
(more common)
On the final exam, you should know what DHCP is, and when it is used

## Slide 41: Network Layer
NAT is a translation of multiple private IP addresses to one single public IP address
Hides details of inner home network from outside world
All incoming traffic will have same public IP, all outgoing will have same public IP
Routers get assigned their one public IP address through DHCP!

## Slide 42: Network Layer
We need headers/rules, which are going to the values the remote controller is going to evaluate
We need actions to do based on some pattern match
Generalized Forwarding and Software Defines Network (SDN)
OpenFlow Standard

## Slide 43: Network Layer (Routing)
Routing Algorithms
Link State
AKA Dijkstra’s algorithm
Centralized Algorithm (requires edge costs of entire network)
Updates are event triggered
Distance Vector
Frequently exchange routing table information between neighbors
Not centralized (does not requires edge costs of entire network beforehand)
Updates happen frequently
On the final exam, you should know the differences between these two algorithms, and from a high-level how they work

## Slide 44: Network Layer (Routing)
An autonomous system is a group of routers that are under the same administrative control
AS 1
OSPF is a link-state protocol that uses flooding of link-state information and Dijkstra’s least-cost algorithm
 Used for routing within an AS
Border Gateway Protocol (BGP) is used for exchanging routing information between AS
On the final exam, you should know when BGP is used, and when OSPF is used

## Slide 45: Network Layer (Routing)
ICMP (Internet Control Message Protocol)
used by hosts & routers to communicate network-level information
  error reporting: unreachable host, network, port, protocol
  echo request/reply (used by ping)
network-layer “above” IP:
  ICMP msgs carried in IP datagrams
ICMP message: type, code plus first 8 bytes of IP datagram causing error
Type Code description
0 0 echo reply (ping)
3 0 dest. network unreachable
3 1 dest host unreachable
3 2 dest protocol unreachable
3 3 dest port unreachable
3 6 dest network unknown
3 7 dest host unknown
4 0 source quench (congestion
control - not used)
8 0 echo request (ping)
9 0 route advertisement
10 0 router discovery
11 0 TTL expired
12 0 bad IP header

## Slide 46: Link Layer
The link layer is responsible for the actual node-to-node delivery of data and ensure error-free transmission of information (handles a variety of mediums)
MAC (Media Access Control) Addresses
MAC (or LAN or physical or Ethernet) address:
  function: used ‘locally” to get frame from one interface to another physically-connected interface (same network, in IP-addressing sense)
  48 bit MAC address (for most LANs) burned in NIC ROM, also sometimes software settable
NIC (Network Interface Controller)- Integrated into the motherboard and allows the machine to use LL services such as ethernet (combination of hardware, software, and some firmware)
Datagrams get encapsulated into frames
MAC Address is your SSN, IP address is your Postal code 

## Slide 47: Link Layer
Protocol for mapping IP Addresses to MAC addresses
Used only for hosts and router interfaces on the same subnet
If the entry does not exist in the table, construct and send an ARP packet
First the machine checks its ARP table
Broadcasts the ARP packet to all interfaces on the LAN (255.255.255.255)
These tables are self-updated, and do not require manual entry*
On the final exam, you should know what ARP is, and when it is used

## Slide 48: Link Layer
Local Area Network (LAN)- A collection of devices in one physical location, typically that share a centralized internet connection
Router
Switch
Challenge: Some devices in a LAN will be transmitted data at the same time, thus a collision can occur at a receiver

## Slide 49: Link Layer
Channel Partitioning
Dealing with Collision: Multiple Access Control Protocols
Token Passing

## Slide 50: Link Layer
Ethernet: Dominant wired LAN technology
(mac addresses)
(error checking bits)
(ip datagram)
(synchronization)
Ethernet switches will store and forward ethernet frames
Hosts have dedicated, direct connection to switch
Ethernet protocol used on each incoming link, but no collisions between links
= ethernet cable
Transparent: Hosts are not aware
they are connected to a switch
Plug and play; self-learning

## Slide 51: Link Layer

## Slide 52: Network Security
Confidentiality- Making sure that only the sender and receiver can read the message (encryption)
Authentication- Making sure that you are communicating with the person you think you are (encryption + hashing)
Integrity- Making sure the message does not get tampered with during transmission (hashing)
On the final exam, you should know the definition of these three terms

## Slide 53: Network Security
Same key used for encrypting and decrypting
Using block ciphers (AES), we can encrypt an arbitrary size of data
Issue: How to securely share secret keys with each other?
Two keys: Public Key (a lock), and a price key (the key)
Public key is used to encrypt. Private key used to decrypt message
Using math, we can securely send messages over an unsecure channel without sharing any sensitive information (Diffie Hellman)
Issue: We can not encrypt stuff bigger than our key (2048 bits)
Often times, symmetric and asymmetric cryptography are used together
(use RSA to send the key for symmetric crypto!)
On the final exam, you should know the differences and limitations between SCrypto, and ACrypto

## Slide 54: Network Security
Append a message with a shared secret (m + s)
Compute hash of (m+s)  H(m+s)
Send H(m+s) with message m
Sender sends: ( H(m+s), m)
Receiver gets ( H(m+s), m)
Append m with shared secret s (m + s)
Compute H(m+s)
The value receiver computed should match the H(m+s) he received
No encryption required!
Used for message integrity!

## Slide 55: Network Security
Bob encrypts his hashed message using his private key, and sends the signed hash, along with message to Alice. Alice decrypts using his public key and verifies that the hashes match
Sending a digital Signature
Verifying a digital signature
Digital Signatures used both hashing and encryption for authentication

## Slide 56: Network Security
Symmetric Crypto, Asymmetric Crypto, and Hashing all work together to send secure, authentic messages

## Slide 57: Network Security
Transport Layer Security (TLS) is a protocol used to provide communication security over a TCP connection
This exists somewhere between the application layer and transport layer
TLS will always be running if you are doing web communication with https
https = Hypertext Transfer Protocol Secure
HTTPS/TLS will handle all the encryption, key generation, certificate checking, authentication for you!
Port 443
UDP does not use TLS

## Slide 58: Network Security
Endpoint Security
A firewall is a combination of hardware and software that isolates an organizations internal network form the internet at large, allowing some packets to pass, and blocking others
An intrusion detection system (IDS) will generate an alert when potentially malicious traffic is observed
An intrusion prevention system (IPS) filters out suspicious traffic, prior to traffic arriving to network
(Looks at packet information)
(Looks at packet information and other signatures)
Types of Endpoint Intrusion Systems
Signature Based
Anomaly-Based

## Slide 59: OSI MODEL
Application Layer
Provides protocols for sending and receiving data between services and web applications (HTTP)
Messages

## Slide 60: OSI MODEL
Application Layer
Presentation Layer
Provides protocols for sending and receiving data between services and web applications (HTTP)
Encoding, Compressing, and Encrypting Data
Messages
Messages

## Slide 61: OSI MODEL
Application Layer
Presentation Layer
Session Layer
Provides protocols for sending and receiving data between services and web applications (HTTP)
Encoding, Compressing, and Encrypting Data
Authentication. Manages, monitors, “sessions” between endpoints
Messages
Messages
Messages

## Slide 62: OSI MODEL
Application Layer
Presentation Layer
Session Layer
Transport Layer
Provides protocols for sending and receiving data between services and web applications (HTTP)
Encoding, Compressing, and Encrypting Data
Authentication. Manages, monitors, “sessions” between endpoints
Provides host-to-host, reliable data transfer, and dictates the flow of data
Messages
Messages
Messages
Segments

## Slide 63: OSI MODEL
Application Layer
Presentation Layer
Session Layer
Transport Layer
Network Layer
Provides protocols for sending and receiving data between services and web applications (HTTP)
Encoding, Compressing, and Encrypting Data
Authentication. Manages, monitors, “sessions” between endpoints
Provides host-to-host, reliable data transfer, and dictates the flow of data
Forwarding and Routing of Data. Logical Addressing
Messages
Messages
Messages
Segments
Datagrams

## Slide 64: OSI MODEL
Application Layer
Presentation Layer
Session Layer
Transport Layer
Network Layer
Data Link Layer
Provides protocols for sending and receiving data between services and web applications (HTTP)
Encoding, Compressing, and Encrypting Data
Authentication. Manages, monitors, “sessions” between endpoints
Provides host-to-host, reliable data transfer, and dictates the flow of data
Forwarding and Routing of Data. Logical Addressing
Handles the formatting and physical addressing of the data before transmitting bits
Messages
Messages
Messages
Segments
Datagrams
Frames

## Slide 65: OSI MODEL
Application Layer
Presentation Layer
Session Layer
Transport Layer
Network Layer
Data Link Layer
Physical Layer
Provides protocols for sending and receiving data between services and web applications (HTTP)
Encoding, Compressing, and Encrypting Data
Authentication. Manages, monitors, “sessions” between endpoints
Provides host-to-host, reliable data transfer, and dictates the flow of data
Forwarding and Routing of Data. Logical Addressing
Handles the formatting and physical addressing of the data before transmitting bits
Transmits bits into physical signals over some medium
Messages
Messages
Messages
Segments
Datagrams
Frames
Bits

## Slide 66: OSI MODEL
Application Layer
Presentation Layer
Session Layer
Transport Layer
Network Layer
Data Link Layer
Physical Layer
A
Penguin
Said
That
Nobody
Drinks
Pepsi
Away
Pizza
Sausage
Throw
Not
Do
Please

## Slide 67: OSI MODEL
Application Layer
Presentation Layer
Session Layer
Data
Data
Data
Transport Layer
Data
TCP Header
Network Layer
Data
TCP Header
IP Header
Data Link Layer
Data
TCP Header
IP Header
MAC Header
Physical Layer
0101010101111010100110101010101010
(TLS header might also happen here)

## Slide 68: Any Questions?

## Slide 69: Thank You!
Thank you for your patience, flexibility, and kindness 
This was a class that I never expected to teach 
There were a lot of long nights, and I know things were not perfect, but I am happy with how things went
I hope you enjoyed this class, and I hope the stuff you learned will be helpful in your career. Networks concepts are your veggies (boring but important)
Connect with me on LinkedIn!
Congrats to those that are graduating next weekend! I hope you find a job that you love!
If I can be of assistance to you for anything in the future, please let me know!
I will be teaching 476 and 132 next semester