## Slide 1: CSCI 466: Networks Subnets, NAT, IPv6, SDN
Reese Pearsall Fall 2023
https://www.cs.montana.edu/pearsall/classes/fall2023/466/main.html
1
*All images are stolen from the internet

## Slide 2: Announcements
PA2 due Friday (10/20)
Final Ack cannot be corrupted
Friday will be a work day for PA2 (no lecture)

## Slide 3: Application Layer
Presentation Layer
Session Layer
Transport Layer
Network Layer
Data Link Layer
Messages from Network Applications
Application Layer
Physical Layer
Physical Layer
*In the textbook, they condense it to a 5-layer model,
but 7 layers is what is most used
Bits being transmitted over a medium
*
*

## Slide 4: Application Layer
Presentation Layer
Session Layer
Transport Layer
Network Layer
Data Link Layer
Messages from Network Applications
Application Layer
Physical Layer
Bits being transmitted over a medium
*
*
Physical Layer
*In the textbook, they condense it to a 5-layer model,
but 7 layers is what is most used

## Slide 5: IPv4: 32-bit addresses (decimal)
Packets traversing through the network layer are referred to as a datagram. Each packet gets an IPv4/IPv6 header
Message
Transport
Layer Header
IP Header
Transport Layer Header
Application Layer Message
IPv4 Header
192.149.252.76
IPv6: 64-bit addresses (hexademical)
3ffe:1900:fe21:4545::
Why do we need IPv6?

## Slide 6
IP Address: Globally unique* 32 bit (4 byte) dotted decimal number assigned to interfaces on hosts and routers
193.32.216.9
=
11000001 00100000 11011000 00001001
(1 byte = 8 bits)
How many addresses are possible with a 32 bit number? ~4 billion possible IPv4 addresses
Used to identify a host on a network

## Slide 7: 223.1.2.1
223.1.1.4
223.1.1.3
223.1.3.2
223.1.3.1
223.1.2.9
223.1.3.27
223.1.2.2
223.1.1.2
223.1.1.1
Subnet is a logical subdivision of an IP network In this network, we have 3 subnets

## Slide 8
223.1.1.253
223.1.1.2
223.1.1.1
…
It is very common to have a range of IP addresses assigned to you (random assignment would be chaos)
Subnet mask
223.1.1.0/24
The leftmost 24 bits represent the prefix of the subnet
11111111 11111111 11111111 XXXXXXXX = 255.255.255.0
223.1.1.67
223.2.1.67
223.2.1.255
193.32.216.9
11000001 00100000 11011000 00001001
Host bits
Network bits

## Slide 9
A subnet mask can be used to reveal which bits are the host bits

## Slide 10
A subnet mask can be used to reveal which bits are the host bits
172.16.1.0
255.255.0.0
10101100.00010000.00000001.00000000
11111111.11111111.00000000.00000000

## Slide 11
A subnet mask can be used to reveal which bits are the host bits
172.16.1.0
255.255.0.0
10101100.00010000.00000001.00000000
11111111.11111111.00000000.00000000

## Slide 12
A subnet mask can be used to reveal which bits are the host bits
172.16.1.0
255.255.0.0
10101100.00010000.00000001.00000000
11111111.11111111.00000000.00000000
The last two octets do not match 1s, so they are the host bits

## Slide 13
A subnet mask can be used to reveal which bits are the host bits
172.16.1.0
255.255.0.0
10101100.00010000.00000001.00000000
11111111.11111111.00000000.00000000
The last two octets do not match 1s, so they are the host bits
172.16.0.0 /16
This IP address would fall under the range of:

## Slide 14
A subnet mask can be used to reveal which bits are the host bits
172.16.1.0
255.255.224.0
10101100.00010000.00000001.00000000
11111111.11111111.11100000.00000000

## Slide 15
A subnet mask can be used to reveal which bits are the host bits
172.16.1.0
255.255.224.0
10101100.00010000.00000001.00000000
11111111.11111111.11100000.00000000
The last 13 bits are the host bits, the first 19 bits are the network bits

## Slide 16
A subnet mask can be used to reveal which bits are the host bits
172.16.1.0
255.255.224.0
10101100.00010000.00000001.00000000
11111111.11111111.11100000.00000000
The last 13 bits are the host bits, the first 19 bits are the network bits
This IP address would fall under the range of
172.16.0.0/19
CIDR

## Slide 17
A subnet mask can be used to reveal which bits are the host bits
172.16.1.0
255.255.224.0
10101100.00010000.00000001.00000000
11111111.11111111.11100000.00000000
The last 13 bits are the host bits, the first 19 bits are the network bits
This IP address would fall under the range of
172.16.0.0/19
CIDR

## Slide 18
A subnet mask can be used to reveal which bits are the host bits
172.0.0.0/9
CIDR
Subnet Mask?

## Slide 19
A subnet mask can be used to reveal which bits are the host bits
172.0.0.0/9
CIDR
Subnet Mask?
11111111.10000000.00000000.00000000

## Slide 20
A subnet mask can be used to reveal which bits are the host bits
172.0.0.0/9
CIDR
Subnet Mask?
11111111.10000000.00000000.00000000
255.128.0.0

## Slide 21
One Subnet

## Slide 22
When communicating on a subnet, the message gets broadcasted to every device on the network

## Slide 23
If there are many devices on a subnet, then this might cause some problems (congestion, lag, delay)

## Slide 24
Six Subnets

## Slide 25
Six Subnets

## Slide 26
Suppose that a packet needs to be sent to another subnet

## Slide 27
We broadcast to our subnet, but we won’t find our destination

## Slide 28
So, the packet will get sent to the default gateway, which is typically the router

## Slide 29
And the router will send it the correct subnet

## Slide 30
Subnets
Suppose we have a class c network
X.X.X.0/24
11111111.11111111.11111111.00000000
Subnet Mask

## Slide 31
Subnets
Suppose we have a class c network
X.X.X.0/24
11111111.11111111.11111111.00000000
Subnet Mask
1 network with 253* hosts
What if we wanted to divide this network into multiple subnets?

## Slide 32
Subnets
Suppose we have a class c network
X.X.X.0/24
11111111.11111111.11111111.00000000
Subnet Mask
1 network with 253* hosts
What if we wanted to divide this network into multiple subnets?
We sacrifice one of our host bits, and give it to the network bits

## Slide 33
Subnets
Suppose we have a class c network
X.X.X.0/24
11111111.11111111.11111111.00000000
Subnet Mask
1 network with 253* hosts
What if we wanted to divide this network into multiple subnets?
We sacrifice one of our host bits, and give it to the network bits
11111111.11111111.11111111.00000000
Subnet 1:
Subnet 2:
11111111.11111111.11111111.10000000
2 Networks with 126 hosts

## Slide 34
Subnets
Suppose we have a class c network
X.X.X.0/24
11111111.11111111.11111111.00000000
Subnet Mask
1 network with 253* hosts
What if we wanted to divide this network into multiple subnets?
We sacrifice one of our host bits, and give it to the network bits
11111111.11111111.11111111.00000000
Subnet 1:
Subnet 2:
11111111.11111111.11111111.10000000
4 Networks with 62 hosts
11111111.11111111.11111111.01000000
Subnet 3:
Subnet 4:
11111111.11111111.11111111.11000000

## Slide 35
Subnets
Suppose we have a class c network
X.X.X.0/24
11111111.11111111.11111111.00000000
Subnet Mask
1 network with 253* hosts
What if we wanted to divide this network into four subnets?
We sacrifice one of our host bits, and give it to the network bits
11111111.11111111.11111111.00000000
Subnet 1:
Subnet 2:
11111111.11111111.11111111.10000000
4 Networks with 62 hosts
11111111.11111111.11111111.01000000
Subnet 3:
Subnet 4:
11111111.11111111.11111111.11000000

## Slide 36
Subnets
Suppose we have a class c network
X.X.X.0/24
11111111.11111111.11111111.00000000
Subnet Mask
1 network with 253* hosts
What if we wanted to divide this network into four subnets?
We sacrifice one of our host bits, and give it to the network bits
11111111.11111111.11111111.11000000
New Subnet Mask
255.255.255.192

## Slide 37
Issue: IPv4 can only support ~4 billion devices
If every device on the internet gets an IP address, we are going to run out of IP addresses to use

## Slide 38
Issue: IPv4 can only support ~4 billion devices
If every device on the internet gets an IP address, we are going to run out of IP addresses to use
Solution: IPv6 (This will take awhile to implement and switch to)
Temporary Solution: Public IP addresses, Private IP addresses, NAT

## Slide 39
The Internet
Every device needs an IP address of some kind…

## Slide 40
The Internet
Every device needs an IP address of some kind…
We could give every device a public IP address (public registered), but this would be expensive, and a waste of IPv4 addresses

## Slide 41
The Internet
Every device needs an IP address of some kind…
We could give every device a public IP address (public registered), but this would be expensive, and a waste of IPv4 addresses
Your ISP will assign your router/modem a public IP address
12.234.56.78

## Slide 42
The Internet
12.234.56.78
Your router will assign private IP addresses to each device via DHCP
Private IP addresses are only used internally, they are not seen by the “outside world”
Private IP addresses typically have a common prefix
10.x.x.x
172.x.x.x
192.168.x.x
192.168.0.1
192.168.0.2
192.168.0.3

## Slide 43
The Internet
12.234.56.78
192.168.0.1
192.168.0.2
192.168.0.3
Issue: When receiving a packet with our public IP address, we need to convert to our private IP address to ensure it gets delivered to the correct host
DST: 12.234.56.78
(and vice versa)

## Slide 44
The Internet
12.234.56.78
192.168.0.1
192.168.0.2
192.168.0.3
NAT (network address translation) is what translates a set of IP addresses to another set of IP addresses (Public  Private)

## Slide 45
The Internet
12.234.56.78
192.168.0.1
192.168.0.2
192.168.0.3
NAT (network address translation) is what translates a set of IP addresses to another set of IP addresses (Public  Private)
DST: 12.234.56.78
NAT
DST: 192.168.0.1

## Slide 46
The Internet
12.234.56.78
192.168.0.1
192.168.0.2
192.168.0.3
NAT (network address translation) is what translates a set of IP addresses to another set of IP addresses (Public  Private)
SRC: 12.234.56.78
NAT
SRC: 192.168.0.1

## Slide 47
The Internet
12.234.56.78
192.168.0.1
192.168.0.2
192.168.0.3
192.168.0.1
192.168.0.5
192.168.0.6
56.131.23.89
Because private IP addresses are only used internally within a subnet, devices on the internet can have the same private IP address (which is fine!)
Devices on the same subnet should not have same private IP addresses

## Slide 48
The Internet
12.234.56.78
192.168.0.1
192.168.0.2
192.168.0.3
192.168.0.4
192.168.0.5

## Slide 49
The Internet
12.234.56.78
192.168.0.1
192.168.0.2
192.168.0.3
192.168.0.4
192.168.0.5
Suppose a host is doing something malicious on some website
The website might decide to block their IP address

## Slide 50
The Internet
12.234.56.78
192.168.0.1
192.168.0.2
192.168.0.3
192.168.0.4
192.168.0.5
Suppose a host is doing something malicious on some website
The website might decide to block their IP address
However, from their perspective, their IP address is 12.234.56.78

## Slide 51
The Internet
12.234.56.78
192.168.0.1
192.168.0.2
192.168.0.3
192.168.0.4
192.168.0.5
Suppose a host is doing something malicious on some website
The website might decide to block their IP address
However, from their perspective, their IP address is 12.234.56.78
So, they block the IP address 12.234.56.78

## Slide 52
The Internet
12.234.56.78
192.168.0.1
192.168.0.2
192.168.0.3
192.168.0.4
192.168.0.5
Suppose a host is doing something malicious on some website
The website might decide to block their IP address
However, from their perspective, their IP address is 12.234.56.78
So, they block the IP address 12.234.56.78
Because this public IP address is shared by several hosts, all the other hosts also get blocked

## Slide 53
How to see your private and public IP address

## Slide 58
Packets traversing through the network layer are referred to as a datagram. Each packet gets an IPv4/IPv6 header
Message
Transport
Layer Header
IP Header
Transport Layer Header
Message
IPv6 Header
TCP header = 20 bytes IP header = 20 bytes
IPv6 = 128 bits
(128 bits)
(128 bits)
The goal is for our internet to be only using IPv6 in the near future? Issues?

## Slide 59
Issue: some routers use IPv4, some use IPv6, some use both. How do we get all networking equipment to coexist with each other?
IPv6
IPv6
IPv4
Solution:

## Slide 60
Issue: some routers use IPv4, some use IPv6, some use both. How do we get all networking equipment to coexist with each other?
IPv6
IPv6
IPv4
Solution: Tunneling

## Slide 61
tl:dr
We wrap our IPv6 datagram in an IPv4 header, and pass it to the IPv4 router!

## Slide 63
Generalized Forwarding and Software Defines Network (SDN)
So far, a router takes input from input port, and then outputs on some output port
What else might a router need to do?

## Slide 64
Generalized Forwarding and Software Defines Network (SDN)
So far, a router takes input from input port, and then outputs on some output port
What else might a router need to do?
Forward, Drop stuff, Modify, Load balance
We need more flexibility and functionality with our forwarding!!

## Slide 65
Generalized Forwarding and Software Defined Network (SDN)
OpenFlow standard
We need headers/rules, which are going to the values the remote controller is going to evaluate
We need actions to do based on some pattern match

## Slide 66
Generalized Forwarding and Software Defines Network (SDN)

## Slide 67
Generalized Forwarding and Software Defines Network (SDN)

## Slide 68
Generalized Forwarding and Software Defines Network (SDN)
22