## Slide 1: CSCI 466: Networks
Lecture 2: Network Edge, Network Core
Reese Pearsall
Fall 2024
https://www.cs.montana.edu/pearsall/classes/fall2024/466/main.html

## Slide 2
Announcements
Make sure to get the CSCI 466 role on Discord!
Fill out the course questionnaire
You can call me “Reese”

## Slide 3
End to End Communication
Devices that are connected to network are called hosts or end systems
A typical home network
Wireless endpoints
Wired endpoints
How does out network get access through other networks?

## Slide 4
End to End Communication
Devices that are connected to network are called hosts or end systems
A typical home network
End systems are connected together by a network of communication links and packet switches
wireless access
point (54 Mbps)
Packet Switch
Communication Link

## Slide 5
End to End Communication
Devices that are connected to network are called hosts or end systems
A typical home network
End systems are connected together by a network of communication links and packet switches
wireless access
point (54 Mbps)
Packet Switch
Communication Link
The most common packet switch we see is called a router

## Slide 6
End to End Communication
Devices that are connected to network are called hosts or end systems
A typical home network
End systems are connected together by a network of communication links and packet switches
Packet Switch
The most common packet switch we see is called a router
A packet switch takes a packet arriving on one of its incoming communication links and forwards that packet on one of its outgoing communication links

## Slide 7
End to End Communication
End systems gain access to the internet through Internet Service Providers (ISPs)

## Slide 8
End to End Communication
End systems gain access to the internet through Internet Service Providers (ISPs)

## Slide 9
End to End Communication
End systems gain access to the internet through Internet Service Providers (ISPs)

## Slide 10
End to End Communication
End systems gain access to the internet through Internet Service Providers (ISPs)

## Slide 11
End to End Communication
“End-to-end communication”
Most hosts can be classified into two categories:
Clients
Servers

## Slide 12
End to End Communication
“End-to-end communication”
Most hosts can be classified into two categories:
Clients (Desktops, Laptops, Phones)
Servers (Powerful computers that store web pages, videos, emails, etc)

## Slide 13
End to End Communication
“End-to-end communication”
Servers typically reside in large datacenters

## Slide 14
Network Edge
The network edge consists of end systems

## Slide 15
Network Edge
An access network is the network that physically connects an end system to the first router
The way that homes and enterprises get connected to the internet

## Slide 16
Network Edge
An access network is the network that physically connects an end system to the first router
The way that homes and enterprises get connected to the internet

## Slide 17
End to End Communication
“Edge Routers” act as the boundary between a private network and a public network

## Slide 18
Home Network Access
Uses existing telephone line to connect to internet and transmit data
Digital Subscriber Line (DSL)

## Slide 19
Home Network Access
Uses existing telephone line to connect to internet and transmit data
Digital Subscriber Line (DSL)

## Slide 20
Home Network Access
Uses existing television cable lines to connect to internet and transmit data
Cable Internet Access
Homes will require a modem, which connects to a home PC with an Ethernet cable
*Shared broadcast medium

## Slide 21
Home Network Access
Uses existing television cable lines to connect to internet and transmit data
Cable Internet Access
Homes will require a modem, which connects to a home PC with an Ethernet cable
(WLAN)

## Slide 22
Home Network Access
Connects homes to a shared fiber cable
Fiber Internet Access (FTTH)

## Slide 23
Home Network Access
Ethernet Internet Access

## Slide 24
Ok, but like how ?
???

## Slide 25
Ok, but like how ?

## Slide 26
INFRAPEDIA

## Slide 27
https://www.youtube.com/watch?v=d0gs497KApU

## Slide 29
Physical Mediums
Twisted-Pair Copper Wire
Coaxial Cable
Fiber Optic Cable

## Slide 30
Physical Mediums
Twisted-Pair Copper Wire
Fiber Optic Cable
Cheap
Easy to install
can handle a variety signals
Expensive
A bit more difficult to install
Much higher speeds, can transmit long distances

## Slide 31
Ok, but like how ?
Radio
Microwave
Infrared
Satellite

## Slide 32
Ok, but like how ?
Guided Medium
Unguided Medium

## Slide 33
The Network Core
End systems are connected together by a network of communication links and packet switches
A packet switch takes a packet arriving on one of its incoming communication links and forwards that packet on one of its outgoing communication links
Each communication link has its own transmission rate (bits/sec)
10 Mbps
500 kbps
100 kbps

## Slide 34
The Network Core
Messages going from A to B are split into packets
“Good morning, I hope you are having a good day!”
Good morning, I hope you are having a good day!
To: Host A
John Paxton
192.42.98.11
From: Host B
Reese Pearsall
192.5.223.42
1500 Bytes
Generated Packet

## Slide 35
The Network Core
Messages going from A to B are split into packets
“Good morning, I hope you are having a good day!”
Good morning, I hope you are having a good day!
To: Host A
John Paxton
192.42.98.11
From: Host B
Reese Pearsall
192.5.223.42
1500 Bytes
Generated Packet
P

## Slide 36
The Network Core
Messages going from A to B are split into packets
“Good morning, I hope you are having a good day!”
Good morning, I hope you are having a good day!
To: Host A
John Paxton
192.42.98.11
From: Host B
Reese Pearsall
192.5.223.42
1500 Bytes
Generated Packet
P

## Slide 37
The Network Core
Messages going from A to B are split into packets
“Good morning, I hope you are having a good day!”
Good morning, I hope you are having a good day!
To: Host A
John Paxton
192.42.98.11
From: Host B
Reese Pearsall
192.5.223.42
1500 Bytes
Generated Packet
P

## Slide 38
The Network Core
Messages going from A to B are split into packets
“Good morning, I hope you are having a good day!”
Good morning, I hope you are having a good day!
To: Host A
John Paxton
192.42.98.11
From: Host B
Reese Pearsall
192.5.223.42
1500 Bytes
Generated Packet
P

## Slide 39
The Network Core
Messages going from A to B are split into packets
“Good morning, I hope you are having a good day!”
Good morning, I hope you are having a good day!
To: Host A
John Paxton
192.42.98.11
From: Host B
Reese Pearsall
192.5.223.42
1500 Bytes
Generated Packet
P

## Slide 40
The Network Core
Messages going from A to B are split into packets
“Good morning, I hope you are having a good day!”
Good morning, I hope you are having a good day!
To: Host A
John Paxton
192.42.98.11
From: Host B
Reese Pearsall
192.5.223.42
1500 Bytes
Generated Packet
P

## Slide 41
The Network Core
Messages going from A to B are split into packets
“Good morning, I hope you are having a good day!”
Good morning, I hope you are having a good day!
To: Host A
John Paxton
192.42.98.11
From: Host B
Reese Pearsall
192.5.223.42
1500 Bytes
Generated Packet
P

## Slide 42
The Network Core
Messages going from A to B are split into packets
“Good morning, I hope you are having a good day!”
Good morning, I hope you are having a good day!
To: Host A
John Paxton
192.42.98.11
From: Host B
Reese Pearsall
192.5.223.42
1500 Bytes
Generated Packet
P

## Slide 43
The Network Core
Messages going from A to B are split into packets
P
Packets are generally small, and cannot exceed a certain size

## Slide 44
The Network Core
Messages going from A to B are split into packets
Packets are generally small, and cannot exceed a certain size
What if we are transmitting large pieces of data?

## Slide 45
The Network Core
Messages going from A to B are split into packets
Packets are generally small, and cannot exceed a certain size
What if we are transmitting large pieces of data?
We must split it up!

## Slide 46
The Network Core
Messages going from A to B are split into packets
Packets are generally small, and cannot exceed a certain size
What if we are transmitting large pieces of data?
We must split it up!
To: Host A
John Paxton
192.42.98.11
To: Host A
John Paxton
192.42.98.11
To: Host A
John Paxton
192.42.98.11
From: Host B
Reese Pearsall
192.5.223.42
From: Host B
Reese Pearsall
192.5.223.42
From: Host B
Reese Pearsall
192.5.223.42
P1
P2
P3

## Slide 47
The Network Core
Messages going from A to B are split into packets
Packets are generally small, and cannot exceed a certain size
What if we are transmitting large pieces of data?
We must split it up!
To: Host A
John Paxton
192.42.98.11
To: Host A
John Paxton
192.42.98.11
To: Host A
John Paxton
192.42.98.11
From: Host B
Reese Pearsall
192.5.223.42
From: Host B
Reese Pearsall
192.5.223.42
From: Host B
Reese Pearsall
192.5.223.42
P1
P2
P3
P1
P2
P3

## Slide 48
The Network Core
Messages going from A to B are split into packets
Packets are generally small, and cannot exceed a certain size
What if we are transmitting large pieces of data?
We must split it up!
To: Host A
John Paxton
192.42.98.11
To: Host A
John Paxton
192.42.98.11
To: Host A
John Paxton
192.42.98.11
From: Host B
Reese Pearsall
192.5.223.42
From: Host B
Reese Pearsall
192.5.223.42
From: Host B
Reese Pearsall
192.5.223.42
P1
P2
P3
P1
P2
P3

## Slide 49
The Network Core
Messages going from A to B are split into packets
Packets are generally small, and cannot exceed a certain size
What if we are transmitting large pieces of data?
We must split it up!
To: Host A
John Paxton
192.42.98.11
To: Host A
John Paxton
192.42.98.11
To: Host A
John Paxton
192.42.98.11
From: Host B
Reese Pearsall
192.5.223.42
From: Host B
Reese Pearsall
192.5.223.42
From: Host B
Reese Pearsall
192.5.223.42
P1
P2
P3
P1
P2
P3

## Slide 50
The Network Core
Messages going from A to B are split into packets
Packets are generally small, and cannot exceed a certain size
What if we are transmitting large pieces of data?
We must split it up!
To: Host A
John Paxton
192.42.98.11
To: Host A
John Paxton
192.42.98.11
To: Host A
John Paxton
192.42.98.11
From: Host B
Reese Pearsall
192.5.223.42
From: Host B
Reese Pearsall
192.5.223.42
From: Host B
Reese Pearsall
192.5.223.42
P1
P2
P3
P1
P2
P3

## Slide 51
The Network Core
Messages going from A to B are split into packets
Packets are generally small, and cannot exceed a certain size
What if we are transmitting large pieces of data?
We must split it up!
To: Host A
John Paxton
192.42.98.11
To: Host A
John Paxton
192.42.98.11
To: Host A
John Paxton
192.42.98.11
From: Host B
Reese Pearsall
192.5.223.42
From: Host B
Reese Pearsall
192.5.223.42
From: Host B
Reese Pearsall
192.5.223.42
P1
P2
P3
P1
P2
P3

## Slide 52
The Network Core
Messages going from A to B are split into packets
Packets are generally small, and cannot exceed a certain size
What if we are transmitting large pieces of data?
We must split it up!
To: Host A
John Paxton
192.42.98.11
To: Host A
John Paxton
192.42.98.11
To: Host A
John Paxton
192.42.98.11
From: Host B
Reese Pearsall
192.5.223.42
From: Host B
Reese Pearsall
192.5.223.42
From: Host B
Reese Pearsall
192.5.223.42
P1
P2
P3
P1
P2
P3

## Slide 53
The Network Core
Messages going from A to B are split into packets
Packets are generally small, and cannot exceed a certain size
What if we are transmitting large pieces of data?
We must split it up!
To: Host A
John Paxton
192.42.98.11
To: Host A
John Paxton
192.42.98.11
To: Host A
John Paxton
192.42.98.11
From: Host B
Reese Pearsall
192.5.223.42
From: Host B
Reese Pearsall
192.5.223.42
From: Host B
Reese Pearsall
192.5.223.42
P1
P2
P3
P1
P2
P3

## Slide 54
The Network Core
Messages going from A to B are split into packets
Packets are generally small, and cannot exceed a certain size
What if we are transmitting large pieces of data?
We must split it up!
To: Host A
John Paxton
192.42.98.11
To: Host A
John Paxton
192.42.98.11
To: Host A
John Paxton
192.42.98.11
From: Host B
Reese Pearsall
192.5.223.42
From: Host B
Reese Pearsall
192.5.223.42
From: Host B
Reese Pearsall
192.5.223.42
P1
P2
P3
P1
P2
P3

## Slide 55
The Network Core
Messages going from A to B are split into packets
Packets are generally small, and cannot exceed a certain size
What if we are transmitting large pieces of data?
We must split it up!
To: Host A
John Paxton
192.42.98.11
To: Host A
John Paxton
192.42.98.11
To: Host A
John Paxton
192.42.98.11
From: Host B
Reese Pearsall
192.5.223.42
From: Host B
Reese Pearsall
192.5.223.42
From: Host B
Reese Pearsall
192.5.223.42
P1
P2
P3
P1
P2
P3

## Slide 56
The Network Core
Messages going from A to B are split into packets
Packets are generally small, and cannot exceed a certain size
What if we are transmitting large pieces of data?
We must split it up!
To: Host A
John Paxton
192.42.98.11
To: Host A
John Paxton
192.42.98.11
To: Host A
John Paxton
192.42.98.11
From: Host B
Reese Pearsall
192.5.223.42
From: Host B
Reese Pearsall
192.5.223.42
From: Host B
Reese Pearsall
192.5.223.42
P1
P2
P3
P1
P2
P3

## Slide 57
The Network Core
Messages going from A to B are split into packets
Packets are generally small, and cannot exceed a certain size
What if we are transmitting large pieces of data?
We must split it up!
To: Host A
John Paxton
192.42.98.11
To: Host A
John Paxton
192.42.98.11
To: Host A
John Paxton
192.42.98.11
From: Host B
Reese Pearsall
192.5.223.42
From: Host B
Reese Pearsall
192.5.223.42
From: Host B
Reese Pearsall
192.5.223.42
P1
P2
P3
P1
P2
P3

## Slide 58
The Network Core
Messages going from A to B are split into packets
Packets are generally small, and cannot exceed a certain size
What if we are transmitting large pieces of data?
We must split it up!
To: Host A
John Paxton
192.42.98.11
To: Host A
John Paxton
192.42.98.11
To: Host A
John Paxton
192.42.98.11
From: Host B
Reese Pearsall
192.5.223.42
From: Host B
Reese Pearsall
192.5.223.42
From: Host B
Reese Pearsall
192.5.223.42
P1
P2
P3
P1
P2
P3

## Slide 59
The Network Core
Messages going from A to B are split into packets
Packets are generally small, and cannot exceed a certain size
What if we are transmitting large pieces of data?
We must split it up!
To: Host A
John Paxton
192.42.98.11
To: Host A
John Paxton
192.42.98.11
To: Host A
John Paxton
192.42.98.11
From: Host B
Reese Pearsall
192.5.223.42
From: Host B
Reese Pearsall
192.5.223.42
From: Host B
Reese Pearsall
192.5.223.42
P1
P2
P3
P1
P2
P3

## Slide 60
The Network Core
Messages going from A to B are split into packets
Packets are generally small, and cannot exceed a certain size
To: Host A
John Paxton
192.42.98.11
To: Host A
John Paxton
192.42.98.11
To: Host A
John Paxton
192.42.98.11
From: Host B
Reese Pearsall
192.5.223.42
From: Host B
Reese Pearsall
192.5.223.42
From: Host B
Reese Pearsall
192.5.223.42
P2
P3
P1
P1
P2
P3
Final Result:

## Slide 61
The Network Core
Messages going from A to B are split into packets
Packets are generally small, and cannot exceed a certain size
To: Host A
John Paxton
192.42.98.11
To: Host A
John Paxton
192.42.98.11
From: Host B
Reese Pearsall
192.5.223.42
From: Host B
Reese Pearsall
192.5.223.42
P1
P2
P3
P1
P2
P3
Lost, Discarded, Corrupt

## Slide 62
The Network Core
Messages going from A to B are split into packets
Packets are generally small, and cannot exceed a certain size
To: Host A
John Paxton
192.42.98.11
To: Host A
John Paxton
192.42.98.11
To: Host A
John Paxton
192.42.98.11
From: Host B
Reese Pearsall
192.5.223.42
From: Host B
Reese Pearsall
192.5.223.42
From: Host B
Reese Pearsall
192.5.223.42
P2
P3
P1
P1
P2
P3
Final Result:
Solution?

## Slide 63
The Network Core
Messages going from A to B are split into packets
Packets are generally small, and cannot exceed a certain size
To: Host A
John Paxton
192.42.98.11
To: Host A
John Paxton
192.42.98.11
To: Host A
John Paxton
192.42.98.11
From: Host B
Reese Pearsall
192.5.223.42
From: Host B
Reese Pearsall
192.5.223.42
From: Host B
Reese Pearsall
192.5.223.42
P2
P3
P1
P1
P2
P3
Final Result:
Solution?
1/3
2/3
3/3

## Slide 64
The Network Core
Messages going from A to B are split into packets
Packets are generally small, and cannot exceed a certain size
To: Host A
John Paxton
192.42.98.11
To: Host A
John Paxton
192.42.98.11
To: Host A
John Paxton
192.42.98.11
From: Host B
Reese Pearsall
192.5.223.42
From: Host B
Reese Pearsall
192.5.223.42
From: Host B
Reese Pearsall
192.5.223.42
P2
P3
P1
P1
P2
P3
Final Result:
Solution?
1/3
2/3
3/3

## Slide 65
The Network Core
Messages going from A to B are split into packets
Packets are generally small, and cannot exceed a certain size
To: Host A
John Paxton
192.42.98.11
To: Host A
John Paxton
192.42.98.11
To: Host A
John Paxton
192.42.98.11
From: Host B
Reese Pearsall
192.5.223.42
From: Host B
Reese Pearsall
192.5.223.42
From: Host B
Reese Pearsall
192.5.223.42
P2
P3
P1
P1
P2
P3
Final Result:
Solution?
1/3
2/3
3/3

## Slide 66
Anatomy of a Packet
What a packet looks like depends on where it’s at in its journey!
“Hello John.”

## Slide 67
Anatomy of a Packet
What a packet looks like depends on where it’s at in its journey!
“Hello John.”
User-level message

## Slide 68
Anatomy of a Packet
What a packet looks like depends on where it’s at in its journey!
“Hello John.”
“Hello John.”
To: John
From: Reese
Intended receiver and sender of message

## Slide 69
Anatomy of a Packet
What a packet looks like depends on where it’s at in its journey!
“Hello John.”
“Hello John.”
To: John
From: Reese
“Hello John.”
To: John
From: Reese
Address of Sender and Receiver
To: 555 Bozeman Ave
From: 123 Highland Ave

## Slide 70
Anatomy of a Packet
What a packet looks like depends on where it’s at in its journey!
“Hello John.”
“Hello John.”
To: John
From: Reese
“Hello John.”
To: John
From: Reese
To: 555 Bozeman Ave
From: 123 Highland Ave
“Hello John.”
To: John
From: Reese
To: 555 Bozeman Ave
From: 123 Highland Ave
To: Apt B
From: Apt F
Specific location of sender and receiver’s homes

## Slide 71
Anatomy of a Packet
What a packet looks like depends on where it’s at in its journey!
“Hello John.”
“Hello John.”
To: John
From: Reese
“Hello John.”
To: John
From: Reese
To: 555 Bozeman Ave
From: 123 Highland Ave
“Hello John.”
To: John
From: Reese
To: 555 Bozeman Ave
From: 123 Highland Ave
To: Apt B
From: Apt F
Specific location of sender and receiver’s homes
Our original message gets encapsulated with many pieces of information
These pieces of information help make sure our mail get sent to the correct place

## Slide 72
Anatomy of a Packet
It’s a complicated system!

## Slide 73
Application Layer
Presentation Layer
Session Layer
Transport Layer
Network Layer
Data Link Layer
Physical Layer
OSI Model
Open Systems Interconnection Model

## Slide 74
Application Layer
Presentation Layer
Session Layer
Transport Layer
Network Layer
Data Link Layer
Physical Layer
OSI Model
Messages from Network Applications
Application Layer
Physical Layer
Bits being transmitted over a copper wire

## Slide 76
Questions?