## Slide 1: CSCI 466: Networks Network Layer – Data Plane
Reese Pearsall Fall 2024
https://www.cs.montana.edu/pearsall/classes/fall2024/466/main.html
1
*All images are stolen from the internet

## Slide 2: Announcements
Wireshark Lab 2 due on Wednesday
Quiz 4 also on Friday
No lecture on Friday

## Slide 3: Announcements

## Slide 4: Application Layer
Presentation Layer
Session Layer
Transport Layer
Network Layer
Data Link Layer
Messages from Network Applications
Application Layer
Physical Layer
Physical Layer
*In the textbook, they condense it to a 5-layer model,
but 7 layers is what is most used
Bits being transmitted over a medium
*
*

## Slide 5: Application Layer
Presentation Layer
Session Layer
Transport Layer
Network Layer
Data Link Layer
Messages from Network Applications
Application Layer
Physical Layer
Bits being transmitted over a medium
*
*
Physical Layer
*In the textbook, they condense it to a 5-layer model,
but 7 layers is what is most used

## Slide 6: Application Layer
Transport Layer
Message
Transport Layer Header
“Segment”
Application Layer Protocol (ex. HTPP)
Transport Layer Protocol
(ex. TCP)
Our packet of information so far…

## Slide 7: Application Layer
Transport Layer
Message
Transport Layer Header
“Segment”
Application Layer Protocol (ex. DNS)
Transport Layer Protocol
(ex. UDP)
Our packet of information so far…

## Slide 8
Application Layer
Transport Layer
???
Network Layer
We’ve only looked at protocols that are running on some host

## Slide 9: We will now shift our focus towards routers, or packet switches
In the network layer, we finally get to leave the host and adventure into the network

## Slide 10
Routers do not have functionality for application & transport layer protocols
TCP
TCP

## Slide 11: We will now shift our focus towards routers, or packet switches
Routing: determine route taken by packets from source to destination

## Slide 12
We will now shift our focus towards routers, or packet switches
Routing: determine route taken by packets from source to destination
There is likely very many paths from one host to another! Which is the most efficient path?

## Slide 13: We will now shift our focus towards routers, or packet switches
Forwarding: move packets from router’s input to appropriate router output
?
?
?
Which path should be taken?

## Slide 14
Individual routing algorithm components in each and every router interact in the control plane
Routing
Algorithm
data
plane
control
plane
1
2
0111
values in arriving
packet header
3

## Slide 15
Individual routing algorithm components in each and every router interact in the control plane
Routing
Algorithm
data
plane
control
plane
1
2
0111
values in arriving
packet header
3

## Slide 16: Software-Defined Networking (SDN) control plane
Remote controller computes, installs forwarding tables in routers
data
plane
control
plane
Remote Controller
CA
CA
CA
CA
CA
1
2
0111
3
values in arriving
packet header

## Slide 17: Network Layer
Responsible for the delivery of data through a network
Routing
Forwarding
forwarding
routing

## Slide 18: Network Layer
No guarantees on:
  successful datagram delivery to destination
  timing or order of delivery
  bandwidth available to end-end flow
Internet “best effort” service model

## Slide 19: Router Architecture Overview
Destination-based forwarding
  Forwarding decisions are based on the destination of the packet
Generalized forwarding
  Forwarding decisions based on any set of header field values

## Slide 20: Router Architecture Overview
Bit-level reception (physical layer)
Link Layer Protocol
Lookup, forwarding, queueing
Bits received
…
…
Such as over the wire or through the air
Next layer of OSI
model
Ex. Ethernet
Evaluate header field values, lookup output port using forwarding table in memory
Queueing will occur if datagrams arrive faster
than forwarding rate into the switching fabric
“Switching Fabric”
INPUT PORT

## Slide 21: Router Architecture Overview
Storing, ready for send off
Link Layer Protocol
Send bits
“Switching Fabric”
…
…
To destination
OUTPUT PORT

## Slide 22: Forwarding Techniques
Lookup, forwarding, queueing
…
…
Address range | Interface (output link)
128.11.52.0 – 128.11.52.255 | 1
153.90.2.0 – 153.90.2.255 | 2
153.90.2.87 – 153.90.2.89 | 3
Routing Table
Connection-less
does not require startup,
Has no idea where the final destination is
This routing table could get very big…
IP addresses need 32/128 bits of memory each

## Slide 23: Forwarding Techniques
Lookup, forwarding, queueing
…
…
Address range | Interface (output link)
128.11.52.0 – 128.11.52.255 | 1
153.90.2.0 – 153.90.2.255 | 2
153.90.2.87 – 153.90.2.89 | 3
Routing Table
Connection-less
does not require startup,
Has no idea where the final destination is
Ranges of IP Addresses
Prefix of IP addresses

## Slide 24: Forwarding Techniques
Lookup, forwarding, queueing
…
…
Address range | Interface (output link)
11001000 00010111 00010*** ********* | 1
11001000 00010111 00011000 ********* | 2
11001000 00010111 00011*** ******** | 3
otherwise | 4
Longest prefix matching
when looking for forwarding table entry for given destination address, use longest address prefix that matches destination address
examples:
DA: 11001000 00010111 000
11000 10101010
DA: 11001000 00010111 000
10110 10100001
which interface? which interface?

## Slide 25: Forwarding Techniques
Lookup, forwarding, queueing
…
…
Address range | Interface (output link)
11001000 00010111 00010*** ********* | 1
11001000 00010111 00011000 ********* | 2
11001000 00010111 00011*** ******** | 3
otherwise | 4
Longest prefix matching
when looking for forwarding table entry for given destination address, use longest address prefix that matches destination address
examples:
DA: 11001000 00010111 000
11000 10101010
DA: 11001000 00010111 000
10110 10100001
which interface? which interface?

## Slide 26: Forwarding Techniques
Lookup, forwarding, queueing
…
…
Address range | Interface (output link)
11001000 00010111 00010*** ********* | 1
11001000 00010111 00011000 ********* | 2
11001000 00010111 00011*** ******** | 3
otherwise | 4
Longest prefix matching
when looking for forwarding table entry for given destination address, use longest address prefix that matches destination address
examples:
DA: 11001000 00010111 000
11000 10101010
DA: 11001000 00010111 000
10110 10100001
which interface? which interface?

## Slide 27: Forwarding Techniques
Lookup, forwarding, queueing
…
…
Address range | Interface (output link)
11001000 00010111 00010*** ********* | 1
11001000 00010111 00011000 ********* | 2
11001000 00010111 00011*** ******** | 3
otherwise | 4
Longest prefix matching
when looking for forwarding table entry for given destination address, use longest address prefix that matches destination address
examples:
DA: 11001000 00010111 000
11000 10101010
DA: 11001000 00010111 000
10110 10100001
which interface? which interface?

## Slide 28: Forwarding Techniques
Lookup, forwarding, queueing
…
…
Address range | Interface (output link)
11001000 00010111 00010*** ********* | 1
11001000 00010111 00011000 ********* | 2
11001000 00010111 00011*** ******** | 3
otherwise | 4
Longest prefix matching
when looking for forwarding table entry for given destination address, use longest address prefix that matches destination address
These lookups need to happen in nanoseconds for our network to function
Ternary content addressable memories (TCAMs) are used in modern routers to do LPM
Cisco routers can carry millions of TCAM entries in their routers

## Slide 29: Fabric Switch and Switching
Switching fabric: Mechanism that forwards data from an input port to output port
Switching via memory:
Handled by a CPU (routing processor) Cannot forward data in parallel

## Slide 30: Fabric Switch and Switching
Switching fabric: Mechanism that forwards data from an input port to output port
Switching via memory:
Handled by a CPU (routing processor) Cannot forward data in parallel
Switching via bus:
Datagrams are prepended with a header
A “bus” transports input port datagrams to output ports
“keep going around the roundabout until you find your port”

## Slide 31: Fabric Switch and Switching
Switching fabric: Mechanism that forwards data from an input port to output port
Switching via memory:
Handled by a CPU (routing processor) Cannot forward data in parallel
Switching via bus:
Datagrams are prepended with a header
A “bus” transports input port datagrams to output ports
Switching via network:
A network of buses
“keep going around the roundabout until you find your port”
One shared bus, but can only fit one datagram

## Slide 32: Input Queueing
fabric slower than input ports combined  queueing may occur at input queues
Input ports
Input ports
Output ports
Output ports
Head-of-the-Line (HOL) blocking: queued datagram at front of queue prevents others in queue from moving forward

## Slide 33: Output Queueing
Storing, ready
for send off
Link Layer Protocol
Send bits
OUTPUT PORT
Input
port
Input port
Input port
Input
port
Switching Fabric
Incoming packets will have to wait for buffer space to become available
Possible solutions:
Remove a packet
  Tail drop: drop arriving packet
  Priority: drop/remove on a priority basis
  Random: drop/remove randomly

## Slide 34: Packet Scheduling
Scheduling is used to determine the next packet to send on the link
FIFO (first in first out): Send in order of arrival to queue

## Slide 35: Packet Scheduling
Scheduling is used to determine the next packet to send on the link
Priority: packets are classified into priority classes. High priority = sent over link first

## Slide 36: Packet Scheduling
Scheduling is used to determine the next packet to send on the link
Round robin weighted fair queueing: packets are classified into priority classes. Each class gets to send one packet during a “cycle”
Packet from the priority group gets sent
Packet from the middle class gets sent Packet from the plebian class gets sent

## Slide 37: A Router

## Slide 38: A Router
A router has software, hardware, and some kind of OS running on it
Routing-Protocols
OSPF
BGP
RIP
Network Protocols
DHCP
DNS
NAT
Network Services
Firewall
VPN
Logging

## Slide 39: IP addressing, IPv4, and IPv6
https://www.rfc-editor.org/rfc/rfc791

## Slide 40: IPv4: 32-bit addresses (decimal)
Packets traversing through the network layer are referred to as a datagram. Each packet gets an IPv4/IPv6 header
Message
Transport
Layer Header
IP Header
Transport Layer Header
Message
IPv4 Header
192.149.252.76
IPv6: 128-bit addresses (hexademical)
3ffe:1900:fe21:4545::
Why do we need IPv6?

## Slide 41: Packets traversing through the network layer are referred to as a datagram. Each packet gets an IPv4/IPv6 header
Message
Transport
Layer Header
IP Header
Transport Layer Header
Message
IPv4 Header
TCP header = 20 bytes IP header = 20 bytes

## Slide 42
IP Address: Globally unique* 32 bit (4 byte) dotted decimal number assigned to interfaces on hosts and routers
193.32.216.9

## Slide 43: IP Address: Globally unique* 32 bit (4 byte) dotted decimal number assigned to interfaces on hosts and routers
193.32.216.9
1 bytes
1 bytes 1 bytes
1 bytes
(1 byte = 8 bits)
128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
1 | 1 | 0 | 0 | 0 | 0 | 0 | 1
128 + 64 + 1 = 193
193 = 11000001 in binary

## Slide 44
IP Address: Globally unique* 32 bit (4 byte) dotted decimal number assigned to interfaces on hosts and routers
193.32.216.9
=
11000001 00100000 11011000 00001001
(1 byte = 8 bits)
How many addresses are possible with a 32 bit number? ~4 billion possible IPv4 addresses

## Slide 45: How do IPs get obtained/assigned?
The Internet Corporation for Assigned Names and Numbers (ICANN) is responsible for managing and allocating IP address space for ISPs and organizations
(they also manage the DNS root servers!)
When an organization gets a range of IP addresses to use, how to we give assign them to devices?
Do we do it manually?
we could….

## Slide 46: DHCP
Dynamic Host Configuration Protocol (DHCP) is a plug-and-play, client-server protocol that allows a host to obtain an IP address automatically
When a host is automatically assigned an IP address, it might keep that one forever, or the IP addresses can be temporary
(more common)
When DHCP finishes, the new host will have an IP address and contact info for the local DNS server

## Slide 47: This process is similar to a TCP handshake!
Broadcast gets sent to all devices on the subnet!!
But devices that are not the dhcp server will ignore it

## Slide 48
This process is similar to a TCP handshake!

## Slide 49
This process is similar to a TCP handshake!

## Slide 50
IP/DHCP in Wireshark