## Slide 1: CSCI 466: Networks Wireless Networks, WiFi
Reese Pearsall Fall 2024
https://www.cs.montana.edu/pearsall/classes/fall2024/466/main.html
1
*All images are stolen from the internet

## Slide 2
Announcements
Quiz on Friday (no class)
Message Confidentiality (Encryption)
Message Integrity and Authentication (Hashing)
Network Attacks (SYN flooding, SYN reset, SYN Hijacking, DNS attacks, BGP attacks, Smurf Attack)
Security Protocols (TLS, Ipsec)
Operational Security (Firewalls, IDS, IOCs)
Wireless Networks, WiFi
PA3 due on Sunday @ 11:59 PM

## Slide 4: Wireless and Mobile Networks: context
more wireless (mobile) phone subscribers than fixed (wired) phone subscribers (10-to-1 in 2019)!
more mobile-broadband-connected devices than fixed-broadband-connected devices devices (5-1 in 2019)!
  4G/5G cellular networks now embracing Internet protocol stack, including SDN
two important (but different) challenges
  wireless: communication over wireless link
  mobility: handling the mobile user who changes point of attachment to network

## Slide 5
Wireless Networks
Transmission Medium = waves in the air
We can transmit waves at different frequencies
Lower frequency The farther the wave can travel

## Slide 6
The government controls which frequencies should be used for different technologies/services
AM radio
TV
TV
TV
TV
TV
Cellular
WIFI
WIFI
3 kHz
300
kHz
3
MHz
30
MHz
300
MHz
3
GHz
30
GHz

## Slide 7: Elements of a wireless network
wired network
infrastructure
wireless hosts
laptop, smartphone, IoT
run applications
may be stationary (non-mobile) or mobile
  wireless does not always mean mobility!

## Slide 8: Elements of a wireless network
wired network
infrastructure
base station
typically connected to wired network
relay - responsible for sending packets between wired network and wireless host(s) in its “area”
  e.g., cell towers, 802.11 access points

## Slide 9: Elements of a wireless network
wired network
infrastructure
wireless link
typically used to connect mobile(s) to base station, also used as backbone link
multiple access protocol coordinates link access
various transmission rates and distances, frequency bands

## Slide 10: Elements of a wireless network
Wireless networks are an extension of the standard internet, and usually only occur at the network edge
(Wired)
Wireless hosts connect to a wireless access point that will connect them to the greater internet. Typically linked to a geographic location
Cell towers are the access points in cellular networks
If you are not in range of a wireless access point, you will not be able to connect to the internet

## Slide 11: Elements of a wireless network
Easer to create high bandwidth links over high frequency carriers, but higher frequencies lose energy more rapidly and it propagates
Generally, lower frequencies are better for long distance communication
802.11 = WiFi
(These are just Wireless and wireless LAN protocols, there are many more ways!)

## Slide 12: Elements of a wireless network

## Slide 13: Elements of a wireless network
Ad hoc mode
No base stations
Nodes can only transmit to other nodes within link coverage
Nodes organize themselves into a network: route amongst themselves
This is advantageous where infrastructure may be damaged or not available

## Slide 14
Wireless network taxonomy
single hop
multiple hops
infrastructure
(e.g., APs)
no
infrastructure
host connects to base station (WiFi, cellular) which connects to larger Internet
no base station, no connection to larger Internet (Bluetooth, ad hoc nets)
host may have to relay through several wireless nodes to connect to larger
Internet: mesh net
no base station, no connection to larger Internet. May have to relay to reach other a given wireless node MANET, VANET

## Slide 15: Wireless link characteristics: fading (attenuation)
  Wireless radio signal attenuates (loses power) as it propagates (free space “path loss”)
Free space path loss ~ (fd)2
f: frequency
d: distance
higher frequency or longer distance
larger free space
path loss

## Slide 16: Wireless link characteristics: multipath
  multipath propagation: radio signal reflects off objects ground, built environment, arriving at destination at slightly different times
line of sight
(LOS) path
reflected path
reflected path

## Slide 17: Wireless link characteristics: multipath
Important differences from wired link…
Decreased signal strength: radio signal attenuates as it propagates through matter (path loss)
Interference from other sources: wireless network frequencies (such as 2.4 ghz) shared by many devices will cause interferences
Multipath propagation: radio signal reflects off objects ground, arriving at destination at slightly different speeds
This makes wireless link communication much more challenging, compared to wired links

## Slide 18: Wireless link characteristics: multipath
Wireless links have a threshold value they must operate over
 If the wireless link does not meet this threshold, then a receiver cannot extract signal
SNR: signal-to-noise ratio
Larger SNR – easier to extract signal from noise (more power) (good thing)
BER: Bit Error Rate
 Large BER – data is corrupted more frequently
SNR vs BER tradeoff
Given physical layer: increase power  increase SNR  decrease BER
Given SNR: choose physical layer that meets BER requirement, giving highest throughput
10
20
30
40
QAM256 (8 Mbps)
QAM16 (4 Mbps)
BPSK (1 Mbps)
SNR(dB)
BER
10-1
10-2
10-3
10-5
10-6
10-7
10-4
(encoding methods)

## Slide 19: Shared Medium
Because wireless networks are sharing a medium/frequency, we need mechanisms for sharing bandwidth so that collisions don’t occur
In the link layer we have three types
1. TDMA (Time division Multiple Access)
2. FDMA (Frequency Division Multiple Access)
3. CDMA (Code Division Multiple Access)
Wired Networks
Wireless Networks

## Slide 20
In a CDMA protocol, each bit being sent is encoded by multiplying the bit by a signal (the code)
All users transmit on the same frequency, but are assigned a unique code (chipping sequence)
Encoding: inner product: (original data) * (chipping sequence)
Decoding: summed inner-product: (encoded data) * (chipping sequence)
CDMA (Code Division Multiple Access)

## Slide 21
CDMA (Code Division Multiple Access)

## Slide 22
CDMA (Code Division Multiple Access) (Multiple Senders)
using same code as sender 1, receiver recovers sender 1’s original data from summed channel data!
Sender 1
Sender 2
channel sums together transmissions by sender 1 and 2
… now that’s useful!

## Slide 23: IEEE 802.11 Wireless LAN
IEEE 802.11 standard | Year | Max data rate | Range | Frequency
802.11b | 1999 | 11 Mbps | 30 m | 2.4 Ghz
802.11g | 2003 | 54 Mbps | 30m | 2.4 Ghz
802.11n (WiFi 4) | 2009 | 600 | 70m | 2.4, 5 Ghz
802.11ac (WiFi 5) | 2013 | 3.47Gpbs | 70m | 5 Ghz
802.11ax (WiFi 6) | 2020 (exp.) | 14 Gbps | 70m | 2.4, 5 Ghz
802.11af | 2014 | 35 – 560 Mbps | 1 Km | unused TV bands (54-790 MHz)
802.11ah | 2017 | 347Mbps | 1 Km | 900 Mhz
all use CSMA/CA for multiple access, and have base-station and ad-hoc network versions

## Slide 24: IEEE 802.11 Wireless LAN Architecture
wireless host communicates with base station
  base station = access point (AP)
Basic Service Set (BSS) (aka “cell”) in infrastructure mode contains:
  wireless hosts
  access point (AP): base station
  ad hoc mode: hosts only
BSS 1
BSS 2
Internet
switch
or router

## Slide 25: 802.11: Channels
spectrum divided into channels at different frequencies
  AP admin chooses frequency for AP
  interference possible: channel can be same as that chosen by neighboring AP!
Example: 2.4 GHz

## Slide 26: 802.11: Channels

## Slide 27: 802.11: Association
arriving host: must associate with an AP
  scans channels, listening for beacon frames containing AP’s name (SSID) and MAC address
  selects AP to associate with
  then may perform authentication
  then typically run DHCP to get IP address in AP’s subnet
BSS

## Slide 28: 802.11: Association
AP 2
AP 1
H1
BBS 2
BBS 1
1
2
3
1
passive scanning:
beacon frames sent from APs
association Request frame sent: H1 to selected AP
association Response frame sent from selected AP to H1
AP 2
AP 1
H1
BBS 2
BBS 1
1
2
2
3
4
active scanning:
Probe Request frame broadcast from H1
Probe Response frames sent from APs
Association Request frame sent: H1 to selected AP
Association Response frame sent from selected AP to H1

## Slide 29: 802.11: Association
In (wired) ethernet, we had MAC protocols that would listen on a channel, and only transmit if the channel was empty
 Requires the ability to listen and transmit at the same time (full-duplex)
WiFi is not full-duplex, which means it cannot detect collisions, so we must avoid collisions instead
When WiFi begins to transmit a frame, it transmits the frame in its entirety; there is no going back

## Slide 30
IEEE 802.11: multiple access
avoid collisions: 2+ nodes transmitting at same time
802.11: CSMA - sense before transmitting
  don’t collide with detected ongoing transmission by another node
802.11: no collision detection!
  difficult to sense collisions: high transmitting signal, weak received signal due to fading
  can’t sense all collisions in any case: hidden terminal, fading
  goal: avoid collisions: CSMA/CollisionAvoidance
A
B
C
A
B
C
A’s signal
strength
C’s signal
strength

## Slide 31: IEEE 802.11 MAC Protocol: CSMA/CA
802.11 sender
1 if sense channel idle for DIFS then
  transmit entire frame (no CD)
sender
receiver
DIFS
data
SIFS
ACK
802.11 receiver
if frame received OK
return ACK after SIFS (ACK needed due to hidden terminal problem)
2 if sense channel busy then
  start random backoff time
  timer counts down while channel idle
  transmit when timer expires
  if no ACK, increase random backoff interval, repeat 2
(time to wait before transmitting)
Distributed Inter-frame Space (DIFS)
Short Inter-frame Spacing (SIFS)

## Slide 32: IEEE 802.11 MAC Protocol: CSMA/CA
idea: sender “reserves” channel use for data frames using small reservation packets
sender first transmits small request-to-send (RTS) packet to BS using CSMA
  RTSs may still collide with each other (but they’re short)
BS broadcasts clear-to-send CTS in response to RTS
CTS heard by all nodes
  sender transmits data frame
  other stations defer transmissions

## Slide 33: IEEE 802.11 MAC Protocol: CSMA/CA
AP
A
B
RTS(A)
RTS(B)
RTS(A)
CTS(A)
CTS(A)
DATA (A)
ACK(A)
ACK(A)
reservation collision
defer
time

## Slide 34: IEEE 802.11 frame: addressing
2
2
6
6
6
2
6
0 - 2312
4
Address 1: MAC address of wireless host or AP to receive this frame
Address 4: used only in ad hoc mode
frame
control
duration
address
1
address
2
address
4
address
3
payload
CRC
seq
control
Address 2: MAC address
of wireless host or AP
transmitting this frame
Address 3: MAC address of router interface to which AP is attached

## Slide 35: IEEE 802.11 frame: addressing
Internet
H1
R1
AP MAC addr
address 1
address 2
address 3
802.11 WiFi frame
R1 MAC addr
H1 MAC addr
R1 MAC addr
MAC dest addr
MAC source addr
802.3 Ethernet frame
H2 MAC addr
Once the AP gets the WiFi frame, it can convert it to a ethernet frame and send it through the main internet

## Slide 36: IEEE 802.11 frame: addressing
2
2
6
6
6
2
6
0 - 2312
4
frame
control
duration
address
1
address
2
address
4
address
3
payload
CRC
seq
control
duration of reserved
transmission time (RTS/CTS)
frame sequence # (for reliable data transfer)
2
2
4
1
1
1
1
1
1
1
1
type
from
AP
subtype
to
AP
more
frag
WEP
more
data
power
mgt
retry
rsvd
protocol
version
frame type (RTS, CTS, ACK, data)

## Slide 37: 802.11: advanced capabilities
Rate adaptation
base station, mobile dynamically change transmission rate (physical layer modulation technique) as mobile moves, SNR varies
10
20
30
40
SNR(dB)
BER
10-1
10-2
10-3
10-5
10-6
10-7
10-4
QAM256 (8 Mbps)
QAM16 (4 Mbps)
BPSK (1 Mbps)
operating point
1. SNR decreases, BER increase as node moves away from base station
2. When BER becomes too high, switch to lower transmission rate but with lower BER

## Slide 38: Personal area networks: Bluetooth
less than 10 m diameter
replacement for cables (mouse, keyboard, headphones)
ad hoc: no infrastructure
2.4-2.5 GHz ISM radio band, up to 3 Mbps
master controller / client devices:
  master polls clients, grants requests for client transmissions
radius of
coverage
C
C
C
P
P
P
P
M
C
master controller
client device
parked device (inactive)
P
M
“piconet”