## Slide 1: CSCI 466: Networks Link Layer
Reese Pearsall Fall 2022
https://www.cs.montana.edu/pearsall/classes/fall2022/466/main.html
1
*All images are stolen from the internet

## Slide 2: Announcements
NO CLASS Friday 11/11
Lab 2 Posted Later today

## Slide 3
Application Layer
Presentation Layer
Session Layer
Transport Layer
Network Layer
Data Link Layer
Physical Layer
OSI Model
Messages from Network Applications
Application Layer
Physical Layer
Bits being transmitted over a copper wire
*In the textbook, they condense it to a 5-layer model, but 7 layers is what is most used
*
*

## Slide 4
Physical Layer
Ethernet Frame
0101011101010101010101111101000010101010101010101
Bit Pattern
Bit Pattern
Goal: To transmit N bits from a transmitter to a receiver over an analog channel in a timely manner and with low error
What types of medium?
Copper Wire
Optic Fiber
Radio Frequency / Through the air

## Slide 5
Physical Layer
Ethernet Frame
0101011101010101010101111101000010101010101010101
Representing zeros and ones in the physical layer
0 1 0 1 0 0 1
0 = no electricity
1 = electricity
There are a lot of ways to represent 0/1s

## Slide 6
Physical Layer
Ethernet Frame
0101011101010101010101111101000010101010101010101
Representing zeros and ones in the physical layer
0 1 0 1 0 0 1
0 = no electricity
1 = electricity
There are a lot of ways to represent 0/1s

## Slide 7
Physical Layer
Ethernet Frame
0101011101010101010101111101000010101010101010101
Physical Layer typically has three sub layers
PCS- Encoding the binary data
PMA- Parallel to serial or serial to parallel
PMD – Voltage amplifiers/LEDs/Lasers

## Slide 8
Physical Layer
Ethernet Frame
0101011101010101010101111101000010101010101010101
Noise and interference will corrupt the analog waveforms as they travel through the channel
Each analog channel has a probability p of bit error
Typical Values of p?
A wireless link may have a raw p of 1e-3, with error correction, this can be improved to 1e-6
Fiber optic link may have p of 1e-12
That a very low probability!!!

## Slide 9
Physical Layer
Ethernet Frame
0101011101010101010101111101000010101010101010101
Noise and interference will corrupt the analog waveforms as they travel through the channel
Each analog channel has a probability p of bit error
Typical Values of p?
A wireless link may have a raw p of 1e-3, with error correction, this can be improved to 1e-6
Fiber optic link may have p of 1e-12
That a very low probability!!!
80 Mbs Wifi Link where p=1e-3 means 4,800 bit errors every minute
10 Gbps fiber optic link where p=1e-12 means 36 bit errors every hour

## Slide 10
Physical Layer
Ethernet Frame
0101011101010101010101111101000010101010101010101
Error Patterns
Frame transmitted: 10110
Error Pattern: 10001
Suppose through error correction in the link layer, we found that a bit error occurred on the first bit and last bit of our pattern
How to get the correct bit pattern of our frame?

## Slide 11
Physical Layer
Ethernet Frame
0101011101010101010101111101000010101010101010101
Error Patterns
Frame transmitted: 10110
Error Pattern: 10001
Suppose through error correction in the link layer, we found that a bit error occurred on the first bit and last bit of our pattern
We can run the XOR operator to get the correct pattern back

## Slide 12
Physical Layer
Ethernet Frame
0101011101010101010101111101000010101010101010101
Physical Layer Transmission

## Slide 13
Session Layer
Traffic Control between Computers
Controls connections and connection information
Establishes, manages, and terminates connections
Authorization, and Authentication between endpoints happens here
Secure Sockets Layer (SSL)- protocol used to establish a safe, encrypted connection between a web application and web server
Establishes a digital certificate to verify a server’s identify
Web Server
Client
Certificate
Before transmitting Data, your machine may do some SSL communication to verify or check the existence of a certificate
No certificate? Cant do HTTPS
Session Layer also makes sure separate files are downloaded correctly

## Slide 14
Presentation Layer
The layer that allows applications to interpret meanings of data
Three main jobs:
1. Translation
Formats data for proper compatibility between devices
ASCII
GIF
JPG
Ensures the data is readable by receiving system

## Slide 15
Presentation Layer
The layer that allows applications to interpret meanings of data
Three main jobs:
Translation
Compression
Message
Compression Algorithm
Message
“Reduce the size of some data”
Type of compression:
1. Lossy- loses some of the original data during compression (is that ok?)
2. Lossless- doesn’t remove data, instead it transforms it to reduce its size
Data vs Information??

## Slide 16
Presentation Layer
The layer that allows applications to interpret meanings of data
Three main jobs:
Translation
Compression

## Slide 17
Presentation Layer
The layer that allows applications to interpret meanings of data
Three main jobs:
Translation
Compression

## Slide 18
Presentation Layer
The layer that allows applications to interpret meanings of data
Three main jobs:
Translation
Compression
Encryption
Encryption- securing communication between two endpoints (typically in the presence of an adversary)
Hi there!
Shared medium
A threat actor could listen in on these channels

## Slide 19
Presentation Layer
The layer that allows applications to interpret meanings of data
Three main jobs:
Translation
Compression
Encryption
Encryption- securing communication between two endpoints (typically in the presence of an adversary)
Hi there!
Xb8yDD54zmbm/JFr9phqTjMzKV98m88kMYfvSqBoe+Q=
Bob encrypts his message using a key
Hi there!
Xb8yDD54zmbm/JFr9phqTjMzKV98m88kMYfvSqBoe+Q=
Plaintext
Ciphertext

## Slide 20
Presentation Layer
The layer that allows applications to interpret meanings of data
Three main jobs:
Translation
Compression
Encryption
Encryption- securing communication between two endpoints (typically in the presence of an adversary)
Hi there!
Xb8yDD54zmbm/JFr9phqTjMzKV98m88kMYfvSqBoe+Q=
Bob encrypts his message using a key
And sends the ciphertext over the channel
Hi there!
Xb8yDD54zmbm/JFr9phqTjMzKV98m88kMYfvSqBoe+Q=
Plaintext
Ciphertext

## Slide 21
Presentation Layer
The layer that allows applications to interpret meanings of data
Three main jobs:
Translation
Compression
Encryption
Encryption- securing communication between two endpoints (typically in the presence of an adversary)
Hi there!
Xb8yDD54zmbm/JFr9phqTjMzKV98m88kMYfvSqBoe+Q=
Bob encrypts his message using a key
And sends the ciphertext over the channel
Hi there!
Xb8yDD54zmbm/JFr9phqTjMzKV98m88kMYfvSqBoe+Q=
Plaintext
Ciphertext
Alice receives the ciphertext and decrypts it with her key
Hi there!

## Slide 22
Presentation Layer
The layer that allows applications to interpret meanings of data
Three main jobs:
Translation
Compression
Encryption
Encryption- securing communication between two endpoints (typically in the presence of an adversary)
Hi there!
Xb8yDD54zmbm/JFr9phqTjMzKV98m88kMYfvSqBoe+Q=
Plaintext
Ciphertext
Symmetric Cryptography (Secret Key Encryption)- Same set of keys are used

## Slide 23
Presentation Layer
The layer that allows applications to interpret meanings of data
Three main jobs:
Translation
Compression
Encryption
Encryption- securing communication between two endpoints (typically in the presence of an adversary)
Hi there!
Xb8yDD54zmbm/JFr9phqTjMzKV98m88kMYfvSqBoe+Q=
Plaintext
Ciphertext
Asymmetric Cryptography (Public Key Encryption)- Different set of keys are used

## Slide 24
Next up:
Security
Firewalls/Tunnels/VPNs
Encryption
Network Attacks and Defenses
Wireless Networks + Wifi