## Slide 1: CSCI 466: Networks
OSI Model, Packet Forwarding
Reese Pearsall
Fall 2024
https://www.cs.montana.edu/pearsall/classes/fall2024/466/main.html

## Slide 2
Announcements
TA: Justin Mau
          Office Hours: Mondays 3:00PM – 5:00PM in Barnard Hall 259
          Email: justindmau@gmail.com

## Slide 4
Application Layer
Presentation Layer
Session Layer
Transport Layer
Network Layer
Data Link Layer
Physical Layer
OSI Model
Messages from Network Applications
Application Layer
Physical Layer
Bits being transmitted over a copper wire
*In the textbook, they condense it to a 5-layer model, but 7 layers is what is most used
*
*

## Slide 5
What is a protocol?

## Slide 6
What is a protocol?

## Slide 7
What is a protocol?
A protocol defines the format and the order of messages exchanges between two or more communicating entities, as well as the actions taken on the transmission and/or receipt of the message or event

## Slide 8
Application Layer
OSI Model
The layer which interacts directly with applications and provides necessary protocols and services for web applications
Humans interact with this layer
Data from user  Application Layer  Sent to next layer down

## Slide 9
Application Layer
OSI Model
The layer which interacts directly with applications and provides necessary protocols and services for web applications
Humans interact with this layer
Data from user  Application Layer  Sent to next layer down
Search query on website 
 Sent to presentation layer

## Slide 10
Application Layer
OSI Model
The layer which interacts directly with applications and provides necessary protocols and services for web applications
Humans interact with this layer
Data from user  Application Layer  Sent to next layer down
Search query on website 
 Sent to presentation layer
Protocol defines the steps of getting data from application to application

## Slide 11
Application Layer
OSI Model
The layer which interacts directly with applications and provides necessary protocols and services for web applications
Humans interact with this layer
Data from user  Application Layer  Sent to next layer down
Search query on website 
 Sent to presentation layer
Protocol defines the steps of getting data from application to application

## Slide 12
OSI Model
The layer which allows applications to interpret meaning of data
Presentation Layer
Translation
Encryption
Compression
Text encoding  Encoding, Ascii
Bit/Byte order
File Syntax

## Slide 13
OSI Model
Session Layer
Manages, monitors, and synchronizing “sessions” between endpoints
Authentication
Authorization
Implements checkpoints while data is flowing

## Slide 14
OSI Model
Application Layer
Presentation Layer
Session Layer
Most of this functionality is handled by our web browsers

## Slide 15
OSI Model
Transport Layer
Manges end to end communication and method of how data will be transferred
Ensures that the data received at host will be in the same order in which it was transmitted
Splits up packets into smaller segments
What should the transmission rate be?

## Slide 16
OSI Model
Transport Layer
Transmission Control Protocol (TCP)
User Datagram Protocol (UDP)
Requires an established connection to transmit data.
Guarantees delivery of data in order
Extensive error checking and acknowledgement of data
Connectionless protocol
Faster, Simpler
Not reliable
No acknowledgement of data, basic error checking

## Slide 17
OSI Model
Transport Layer
Network Layer
Primary purpose is to move datagrams from one host to another, and to determine physical path to destination
What route to take?
We also assign IP addresses to our packet

## Slide 18
OSI Model
Transport Layer
Network Layer
Handles the formatting and physical addressing of the “packet” before reaching the destination
Data Link Layer
Good morning, I hope you are having a good day!
To From
Link layer needs to pack bits into frames
Source MAC
Destination MAC
011010110111010101110111010110110101010101011101100011110101011010110101010010011110010111010101110101011011011011010101011101101110101011011101011010111011010110110110101100010101
011010110111010101110111010110110101010101011101100011110101011010110101010010011110010111010101110101011011011011010101011101101110101011011101011010111011010110110110101100010101
110101101110101011101110101101110101101110101011101110101101110101101110101011101110101101010101110101011001010111010101100101011101010110010101110101011001010111010101100101011101
011010110111010101110111010110110101010101011101100011110101011010110101010010011110010111010101110101011011011011010101011101101110101011011101011010111011010110110110101100010101
Frame

## Slide 19
OSI Model
Transport Layer
Network Layer
Data Link Layer
Physical Layer
Transmits bits into physical signals over some medium

## Slide 20
OSI Model
Encapsulation
Application Layer
Presentation Layer
Session Layer
Data
Data
Data

## Slide 21
OSI Model
Encapsulation
Application Layer
Presentation Layer
Session Layer
Data
Data
Data
Transport Layer
Data
TCP Header
“Segment”

## Slide 22
OSI Model
Encapsulation
Application Layer
Presentation Layer
Session Layer
Data
Data
Data
Transport Layer
Data
TCP Header
Network Layer
Data
TCP Header
IP Header
“Datagram”
“Segment”

## Slide 23
OSI Model
Encapsulation
Application Layer
Presentation Layer
Session Layer
Data
Data
Data
Transport Layer
Data
TCP Header
Network Layer
Data
TCP Header
IP Header
Data Link Layer
Data
TCP Header
IP Header
MAC Header
“Segment”
“Frame”
“Datagram”

## Slide 24
OSI Model
Encapsulation
Application Layer
Presentation Layer
Session Layer
Data
Data
Data
Transport Layer
Data
TCP Header
Network Layer
Data
TCP Header
IP Header
Data Link Layer
Data
TCP Header
IP Header
MAC Header
Physical Layer
0101010101111010100110101010101010

## Slide 25
OSI Model
Encapsulation

## Slide 26
OSI Model
Ticket (purchase)

## Slide 27
OSI Model
Ticket (purchase)
Baggage (Check)

## Slide 28
OSI Model
Ticket (purchase)
Baggage (Check)
Gates (load)

## Slide 29
OSI Model
Ticket (purchase)
Baggage (Check)
Gates (load)
Runway Takeoff

## Slide 30
OSI Model
Ticket (purchase)
Baggage (Check)
Gates (load)
Runway Takeoff
Airplane Routing

## Slide 31
OSI Model
Ticket (purchase)
Baggage (Check)
Gates (load)
Runway Takeoff
Airplane Routing
Airplane Routing

## Slide 32
OSI Model
Ticket (purchase)
Baggage (Check)
Gates (load)
Runway Takeoff
Airplane Routing
Airplane Routing
Runway landing

## Slide 33
OSI Model
Ticket (purchase)
Baggage (Check)
Gates (load)
Runway Takeoff
Airplane Routing
Airplane Routing
Runway landing
Gates (unload)

## Slide 34
OSI Model
Ticket (purchase)
Baggage (Check)
Gates (load)
Runway Takeoff
Airplane Routing
Airplane Routing
Runway landing
Gates (unload)
Baggage (claim)

## Slide 35
OSI Model
Ticket (purchase)
Baggage (Check)
Gates (load)
Runway Takeoff
Airplane Routing
Airplane Routing
Runway landing
Gates (unload)
Baggage (claim)
Tickets (complain)

## Slide 36
OSI Model

## Slide 37
OSI Model

## Slide 38
10 Mbps
500 kbps
100 kbps
The internet is a network of networks, connected by packet switches and communication links
Communication links have different transmission rates
“Good morning, I hope you are having a good day!”
Good morning, I hope you are having a good day!
To: Host A
John Paxton
192.42.98.11
From: Host B
Reese Pearsall
192.5.223.42
Generated Packet
Messages going from A to B are split into packets

## Slide 39
10 Mbps
500 kbps
100 kbps
The internet is a network of networks, connected by packet switches and communication links
Communication links have different transmission rates
“Good morning, I hope you are having a good day!”
Good morning, I hope you are having a good day!
To: Host A
John Paxton
192.42.98.11
From: Host B
Reese Pearsall
192.5.223.42
Generated Packet
Messages going from A to B are split into packets

## Slide 40
Data Forwarding
Packet Switching
Uses store-and-forward transmission
Store and forward- wait for the entire packet to arrive, check value(s) of packet, and then forward to next location

## Slide 41
Data Forwarding
Routing Table
Network 192.47.0.1
Network 192.4.02.11
Network 192.27.3.11
Network 101.0.1
Network 103.44.7
1
2
3
4
1
2
3

## Slide 42
Data Forwarding
Routing Table
Network 192.47.0.1
Network 192.4.02.11
Network 192.27.3.11
Network 101.0.1
Network 103.44.7
1
2
3
4
1
2
3
Network 192.4.02.11
Network 192.47.0.1
Network 192.27.3.11
Network 101.0.1
Network 103.44.7
Destination
Interface
3
1
2
4
4

## Slide 43
Data Forwarding
Routing Table
Network 192.47.0.1
Network 192.4.02.11
Network 192.27.3.11
Network 101.0.1
Network 103.44.7
1
2
3
4
1
2
3
Network 192.4.02.11
Network 192.47.0.1
Network 192.27.3.11
Network 101.0.1
Network 103.44.7
Destination
Interface
3
1
2
4
4
We will discuss how these tables are populated in several weeks

## Slide 44
Data Forwarding
In circuit switching, the path and resources for transmitting from A to B is reserved
Communication links are divided into circuits, which allow for concurrent usage of the link

## Slide 45
Data Forwarding
In circuit switching, the path and resources for transmitting from A to B is reserved
Communication links are divided into circuits, which allow for concurrent usage of the link
Reserved spaces that are not in use result in silent periods

## Slide 46
How are links “reserved” ?

## Slide 47
Traceroute
Network diagnostic tool that displays route taken to destination and RTT for each hop

## Slide 48
Traceroute
Network diagnostic tool that displays route taken to destination and RTT for each hop
Destination
Hop #
RTT time for each packet

## Slide 49
Traceroute
Network diagnostic tool that displays route taken to destination and RTT for each hop
Destination
Hop #
RTT time for each packet
whois- provides registration data of a domain or IP address

## Slide 50
Traceroute
Network diagnostic tool that displays route taken to destination and RTT for each hop
Destination
Hop #
RTT time for each packet
whois- provides registration data of a domain or IP address

## Slide 51
Traceroute
Network diagnostic tool that displays route taken to destination and RTT for each hop
Destination
Hop #
RTT time for each packet
whois- provides registration data of a domain or IP address